## Slide 1: Multi-Hypothesis INTER PREDICTION JVET-J0041 Martin Winken, Christian Bartnik, Heiko Schwarz, Detlev Marpe, Thomas Wiegand

## Slide 2: Basic concept
Superpose multiple (i.e., more than 2) motion-compensated prediction signals
Allow different weights for the individual prediction signals (“hypotheses”)
Idea: Use recursive approach
    : ordinary uni/bi-prediction signal (as in HEVC/H.265)
    : additional 3rd hypothesis
    : weighted 3-hypotheses inter prediction signal
    : weighting factor with
  Generalize to N hypotheses:

## Slide 3: Interaction with MERGE mode
Additional hypotheses are also allowed in MERGE mode (but not SKIP)
Additional hypotheses are part of the merging candidate (i.e., can be inherited)
There is a limit on the total number of additional hypotheses (for our CfP response: 1)

## Slide 4: Syntax
A single combined reference picture list is used.

## Slide 5: Multi-Hypothesis Motion Estimation
For a given CU, the conventional inter modes are tested first.
For the best of these, an additional prediction hypothesis is searched.
A reduced search range of 16 is used.
If more additional hypotheses allowed, another hypothesis is searched like above.

## Slide 6: Experimental results: Configuration settings
Only QT+BTS partitioning (see JVET-J0035) and multi-hypothesis inter prediction enabled
Test set: Common Test Conditions (CTC) + Call for Proposals (CfP) sequences
First 49 frames are encoded.

## Slide 7: Experimental results: 1 add.hyp, 1 ref, 1 weight
Random Access |  |  |  |  |  |  |  |  |  | 
 | QP values 22, 27, 32, 37 |  |  |  |  | QP values 27, 32, 37, 42 |  |  |  | 
 | Y | Cb | Cr | EncT | DecT | Y | Cb | Cr | EncT | DecT
JVET A1 | -0.46% | -0.79% | -0.56% | 109% | 100% | -0.11% | -0.56% | -0.23% | 109% | 99%
JVET A2 | -0.97% | -1.10% | -0.99% | 108% | 97% | -0.38% | -0.35% | -0.30% | 108% | 97%
JVET B | -0.93% | -0.81% | -0.46% | 109% | 99% | -0.41% | -0.51% | -0.09% | 110% | 101%
JVET C | -0.43% | -0.03% | -0.13% | 120% | 105% | -0.15% | -0.03% | -0.01% | 114% | 99%
JVET D | -0.32% | -0.28% | -0.26% | 116% | 99% | -0.05% | -0.28% | -0.33% | 114% | 96%
JVET E | -0.73% | -0.04% | -0.53% | 115% | 101% | -0.30% | 0.09% | -0.18% | 114% | 99%
JVET F | -0.34% | -0.24% | -0.11% | 113% | 104% | -0.19% | -0.23% | -0.08% | 112% | 103%
CfP 360 | -0.24% | -0.38% | -0.30% | 107% | 94% | -0.10% | -0.39% | -0.09% | 109% | 96%
CfP SDR-A | -0.46% | -0.69% | -0.55% | 110% | 100% | -0.13% | -0.16% | -0.01% | 108% | 99%
CfP SDR-B | -1.02% | -0.84% | -0.59% | 111% | 100% | -0.46% | -0.37% | -0.19% | 112% | 102%
CfP HDR-A | -0.22% | -0.19% | -0.23% | 111% | 101% | -0.14% | -0.16% | -0.15% | 111% | 100%
CfP HDR-B | -0.25% | -0.21% | -0.24% | 109% | 99% | -0.09% | 0.01% | 0.07% | 111% | 99%
JVET all | -0.61% | -0.50% | -0.43% | 112% | 100% | -0.23% | -0.29% | -0.17% | 111% | 99%
CfP all | -0.46% | -0.49% | -0.40% | 110% | 99% | -0.19% | -0.22% | -0.07% | 110% | 99%
JVET + CfP | -0.48% | -0.43% | -0.38% | 112% | 100% | -0.19% | -0.25% | -0.14% | 111% | 99%
Low Delay |  |  |  |  |  |  |  |  |  | 
 | QP values 22, 27, 32, 37 |  |  |  |  | QP values 27, 32, 37, 42 |  |  |  | 
 | Y | Cb | Cr | EncT | DecT | Y | Cb | Cr | EncT | DecT
Cactus | -0.50% | -0.44% | -0.63% | 114% | 99% | -0.24% | -0.26% | -0.41% | 113% | 99%
BasketballDrive | -0.39% | -0.75% | -0.57% | 110% | 93% | -0.21% | -0.66% | -0.06% | 114% | 101%
BQTerrace | -1.79% | -0.70% | -0.40% | 113% | 102% | -0.91% | -0.23% | 0.13% | 114% | 101%
RitualDance | -0.13% | 0.02% | -0.54% | 117% | 105% | 0.02% | 0.20% | -0.45% | 116% | 104%
MarketPlace | -0.13% | 0.29% | 0.59% | 115% | 100% | 0.07% | -0.21% | 1.27% | 115% | 100%
all | -0.59% | -0.32% | -0.31% | 114% | 100% | -0.25% | -0.23% | 0.10% | 114% | 101%

## Slide 8: Experimental results: 1 add.hyp, 2 refs, 2 weights
Random Access |  |  |  |  |  |  |  |  |  | 
 | QP values 22, 27, 32, 37 |  |  |  |  | QP values 27, 32, 37, 42 |  |  |  | 
 | Y | Cb | Cr | EncT | DecT | Y | Cb | Cr | EncT | DecT
JVET A1 | -0.57% | -0.88% | -0.73% | 119% | 104% | -0.11% | -0.68% | -0.34% | 119% | 103%
JVET A2 | -1.50% | -1.47% | -1.40% | 118% | 100% | -0.65% | -0.62% | -0.57% | 119% | 99%
JVET B | -1.68% | -0.71% | -0.67% | 117% | 100% | -0.86% | -0.27% | -0.14% | 120% | 102%
JVET C | -1.30% | -0.40% | -0.35% | 122% | 102% | -0.69% | -0.16% | 0.12% | 120% | 97%
JVET D | -1.82% | -0.40% | -0.50% | 127% | 104% | -0.92% | -0.13% | -0.04% | 126% | 102%
JVET E | -1.46% | -0.06% | -0.72% | 125% | 103% | -0.63% | 0.09% | -0.46% | 128% | 103%
JVET F | -1.18% | -0.47% | -0.48% | 118% | 104% | -0.84% | -0.36% | -0.21% | 119% | 104%
CfP 360 | -0.41% | -0.25% | -0.37% | 116% | 95% | -0.19% | -0.11% | -0.34% | 119% | 96%
CfP SDR-A | -0.72% | -0.92% | -0.87% | 118% | 102% | -0.24% | -0.43% | -0.27% | 119% | 102%
CfP SDR-B | -1.89% | -1.02% | -0.84% | 115% | 100% | -0.98% | -0.26% | -0.09% | 118% | 101%
CfP HDR-A | -0.31% | -0.21% | -0.28% | 121% | 102% | -0.17% | -0.13% | -0.20% | 122% | 101%
CfP HDR-B | -0.64% | -0.37% | -0.58% | 121% | 101% | -0.25% | -0.05% | -0.15% | 122% | 102%
JVET all | -1.37% | -0.65% | -0.69% | 121% | 102% | -0.68% | -0.32% | -0.22% | 121% | 101%
CfP all | -0.84% | -0.58% | -0.61% | 118% | 100% | -0.38% | -0.20% | -0.21% | 120% | 100%
JVET + CfP | -1.06% | -0.57% | -0.62% | 120% | 101% | -0.52% | -0.26% | -0.23% | 121% | 101%
Low Delay |  |  |  |  |  |  |  |  |  | 
 | QP values 22, 27, 32, 37 |  |  |  |  | QP values 27, 32, 37, 42 |  |  |  | 
 | Y | Cb | Cr | EncT | DecT | Y | Cb | Cr | EncT | DecT
Cactus | -1.01% | -0.53% | -1.13% | 135% | 114% | -0.57% | -0.07% | -0.68% | 133% | 114%
BasketballDrive | -0.44% | -0.74% | -0.45% | 122% | 92% | -0.15% | -0.70% | -0.16% | 127% | 100%
BQTerrace | -3.45% | -1.87% | -1.26% | 125% | 108% | -2.65% | -1.24% | -0.55% | 133% | 113%
RitualDance | -0.52% | -0.08% | -0.21% | 125% | 103% | -0.21% | 0.20% | -0.04% | 125% | 102%
MarketPlace | -0.46% | -0.44% | 0.64% | 127% | 100% | -0.04% | -0.39% | 1.21% | 129% | 100%
all | -1.18% | -0.73% | -0.48% | 127% | 103% | -0.73% | -0.44% | -0.04% | 129% | 106%

## Slide 9: Experimental results: 2 add.hyp, 4 refs, 2 weights
Random Access |  |  |  |  |  |  |  |  |  | 
 | QP values 22, 27, 32, 37 |  |  |  |  | QP values 27, 32, 37, 42 |  |  |  | 
 | Y | Cb | Cr | EncT | DecT | Y | Cb | Cr | EncT | DecT
JVET A1 | -0.86% | -1.22% | -1.06% | 125% | 102% | -0.17% | -0.73% | -0.42% | 125% | 102%
JVET A2 | -2.19% | -2.12% | -1.69% | 130% | 101% | -0.92% | -0.94% | -0.59% | 129% | 100%
JVET B | -2.17% | -1.08% | -0.99% | 131% | 100% | -1.07% | -0.43% | -0.18% | 131% | 102%
JVET C | -1.67% | -0.55% | -0.64% | 135% | 104% | -0.82% | -0.20% | 0.04% | 136% | 101%
JVET D | -2.36% | -0.31% | -0.65% | 142% | 102% | -1.02% | 0.09% | 0.04% | 142% | 103%
JVET E | -1.65% | -0.21% | -0.43% | 141% | 106% | -0.62% | 0.05% | -0.24% | 141% | 104%
JVET F | -1.37% | -0.70% | -0.53% | 127% | 102% | -0.91% | -0.43% | -0.37% | 128% | 103%
CfP 360 | -0.56% | -0.31% | -0.43% | 130% | 98% | -0.27% | -0.21% | -0.39% | 132% | 99%
CfP SDR-A | -0.99% | -1.33% | -0.93% | 128% | 103% | -0.33% | -0.64% | -0.25% | 128% | 103%
CfP SDR-B | -2.45% | -1.41% | -1.45% | 128% | 99% | -1.18% | -0.50% | -0.60% | 127% | 101%
CfP HDR-A | -0.56% | -0.36% | -0.47% | 132% | 103% | -0.38% | -0.24% | -0.28% | 132% | 102%
CfP HDR-B | -0.82% | -0.50% | -0.76% | 133% | 103% | -0.32% | -0.21% | -0.15% | 134% | 103%
JVET all | -1.77% | -0.91% | -0.88% | 132% | 102% | -0.81% | -0.39% | -0.24% | 133% | 102%
CfP all | -1.12% | -0.82% | -0.84% | 130% | 101% | -0.51% | -0.37% | -0.34% | 131% | 102%
JVET + CfP | -1.39% | -0.79% | -0.79% | 132% | 102% | -0.63% | -0.37% | -0.29% | 132% | 102%
Low Delay |  |  |  |  |  |  |  |  |  | 
 | QP values 22, 27, 32, 37 |  |  |  |  | QP values 27, 32, 37, 42 |  |  |  | 
 | Y | Cb | Cr | EncT | DecT | Y | Cb | Cr | EncT | DecT
Cactus | -1.38% | -1.03% | -1.33% | 144% | 100% | -0.79% | -0.29% | -0.71% | 143% | 100%
BasketballDrive | -0.84% | -0.64% | -0.98% | 148% | 101% | -0.67% | -0.53% | -0.50% | 155% | 110%
BQTerrace | -5.07% | -2.49% | -2.11% | 141% | 106% | -3.72% | -1.42% | -1.12% | 144% | 106%
RitualDance | -1.00% | -0.91% | -1.15% | 136% | 101% | -0.61% | -0.72% | -0.47% | 138% | 100%
MarketPlace | -0.83% | -0.82% | -0.08% | 147% | 100% | -0.44% | -0.65% | 0.78% | 148% | 100%
all | -1.83% | -1.18% | -1.13% | 143% | 101% | -1.25% | -0.72% | -0.40% | 146% | 103%

## Slide 10: Experimental results (Random Access)

## Slide 11: Experimental results (Low delay B)

## Slide 12: Conclusion
Different complexity-gain trade-offs possible
Random Access at CTC QPs (22,27,32,37):
  Coding gains: -0.5…-1.4% Y BD bit rate
  Complexity: ~112…132% encoder, ~100…102% decoder
Propose to consider for further standardization work