## Slide 1
JVET-J0042
Intra Block Copy for Intra-Frame Coding
Xuguang Zuo, Li Wang, Fangdong Chen and Xiaodan Song
Hikvision

## Slide 2: Outline
Introduction
Proposed IBC
Experimental Results
Conclusion

## Slide 3: Introduction
Concept of IBC
IBC is a block matching technique wherein the current block is predicted by a reference block located in the already reconstructed region in the same frame.

## Slide 4: Introduction
Advantage of IBC
Exploit the non-local correlation in frame containing repeated textures or patterns.
IBC technique has been proved efficient for the coding of screen content video.
Motivation of the proposed IBC
There are also repeated contents in frame of natural video, theoretically IBC technique can also help improve the coding efficiency.

## Slide 5: Proposed IBC
Implemented on JEM 7.1 for intra-frame coding
Separate coding of luma and chroma for intra-frame in JEM
Independent Quadtree plus binary tree block structure of luma and chroma
Luma: 67 intra prediction modes
Chroma: 6 CCLM modes and 5 intra prediction modes.
Separate implementation of IBC for luma and chroma

## Slide 6: Proposed IBC for luma frame
IBC mode is considered as an inter mode. The coding of luma frame is similar to an inter frame.
Syntax change: remove skip mode flag

## Slide 7: Proposed IBC for chroma frame
IBC mode is a new mode added to the mode candidate list.
Process:
Decide if IBC mode should be put into the candidate list.
Check the prediction type of the luma blocks covering the co-located five positions of the current chroma block. The five positions are checked in the order of center (CR), top-left (TL), top-right (TR), bottom-left (BL) and bottom-right (BR).
Scale the motion vectors (MVs) of checked inter luma blocks. Then check if the scaled MV is valid for current chroma block.

## Slide 8: Proposed IBC for chroma frame
Process:
If an inter luma block is found and its MV is valid for current chroma block after scaling, then the IBC mode is put into the candidate list just behind the CCLM modes. Length of candidate list not changed
MV of IBC mode: first valid scaled MV from the inter luma blocks

## Slide 9: Motion estimation for luma IBC
Search Range: a rectangular area surrounding current block. top-left and bottom-right points of the search area are (-SHor, -SVer) and (SHor, SVer)
Search Method:
Horizontal search and vertical search
Interlaced search
Refinement
Hash-based method used for 8x8 block

## Slide 10: Experimental Results
Results for AI Main10 VS JEM 7.0
Thank Samsung for help with the crosscheck.
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | -0.05% | -0.07% | 175% | 101%
Class A2 | -1.42% | -1.75% | -1.89% | 146% | 101%
Class B | -1.04% | -1.60% | -1.58% | 181% | 100%
Class C | -0.30% | -0.42% | -0.38% | 147% | 101%
Class D | -0.29% | -0.55% | -0.47% | 121% | 101%
Class E | -1.48% | -1.88% | -1.91% | 133% | 100%
Overall | -0.75% | -1.03% | -1.04% | 151% | 101%
Class F | -19.92% | -20.22% | -20.41% | 130% | 97%

## Slide 11: Experimental Results
Prediction of IBC
Prediction of JEM
Original image

## Slide 12: Conclusion
Propose a IBC method for intra-frame coding on JEM.
  Separate implementation for luma and chroma
  Luma: IBC mode is an inter mode. Skip mode flag removed.
  Chroma: IBC mode is added to the intra prediction mode candidate list
Experimental results :
Natural video: -0.75%, -1.03% and -1.04% YUV gain, 51% encoding complexity increase, no decoding complexity increase.
Screen content video: -19.92%, -20.22%, -20.41% YUV gain, 30% encoding complexity increase, no decoding complexity increase.
It is suggested to further study IBC in CE.

## Slide 13
Thank you！