## Slide 1: Coding performance of Tencent’s structure only scheme (JVET-J0049)
X. Li, X. Zhao, S. Liu
2018/04

## Slide 2: Introduction
Coding performance of structure only is reported in this contribution
Structure only improvement from JVET-J0047
  Quad-tree
  Binary-tree
  Triple-Tree
  SplitToSquare
  Multi-parameter CABAC engine is used to support coefficient group smaller than 4x4
Tools are turned off by cfg options except multi-parameter CABAC

## Slide 3: Simulation Results
Coding performance over constraint set 1
Coding performance over constraint set 2
Multi-parameter CABAC was reportedly bring 1.2% gain in random access [JVET-B0022]
Over 12% coding gain can be achieved by structure only method for random access
 | Over HM-16.6 |  |  |  | 
 | Y | U | V | EncT | DecT
Class UHD | -16.87% | -17.95% | -19.57% | 320% | 123%
Class HD | -12.66% | -22.41% | -25.48% | 266% | 114%
Overall (Ref) | -14.76% | -20.18% | -22.52% | 292% | 118%
 | Over HM-16.6 |  |  |  | 
 | Y | U | V | EncT | DecT
HD | -13.25% | -35.18% | -37.43% | 209% | 105%
Overall (Ref) | -13.25% | -35.18% | -37.43% | 213% | 106%

## Slide 4: Conclusions
Coding performance of structure only is reported in this contribution
Significant rate reduction is observed by structure only methods
It is proposed to include structure tools into test model