## Slide 1: Adaptive GOP structure with future reference picture in random access configuration
JVET-J0051
Yi-Wen Chen

## Slide 2: Introduction
New prediction structure IIB for random access conditions
  Prediction structure is similar to hierarchical structure (e.g. GOP16)
  Provide 4.4% and 4.8% BD-rate savings over GOP16 in HM and JEM
  Applicable to all CTC sequences with intra period 32, 48, 64 and 96
  The increase of run time memory usage is minimum (10% increased over GOP16)
  No decoder change
  RPS in HEVC can be used to signal the IIB structure
  One additional picture buffer is required in DPB

## Slide 3: Limitations of Applying GOP32/64
Picture buffer size is increased by 1 or 2 over GOP 16
Less Flexibility
  For GOP 32, intra periods of 48 cannot be applied
  For GOP 64, intra periods of 32, 48 or 96 cannot be applied
larger GOP size is difficult to adapt to various characteristics of target video sequences
  Accuracy of inter prediction degrade when the reference picture is far away
The encoding run time memory usage is significantly increased due to the implementation
  In HM, 1.9GB for GOP16, 2.8GB for GOP32, 5.4GB for GOP64

## Slide 4: The Proposed Structure: IIB-N
For each intra period, coding the beginning I-pic and then the future I-pic followed by the coding of the B-pics in between
The future I-pic is stored in DPB and used as reference pics for B-pics
N represents the GOP N structure used for coding the B-pics
For example, the prediction structure of IIB-16:
  Coding order: beginning I-pic, future I-pic, 1st GOP16, 2nd GOP16, 3rd GOP16. 4th GOP16

## Slide 5: IIB Structure
Applicable to all CTC sequences with intra period 32, 48, 64 and 96
Encoding run time memory usage is increased by 10% due to the easy implementation
No decoder change
RPS could signal the IIB-N structure
Only require one additional picture buffer in DPB
 | GOP 16 | GOP 32 | GOP64 | IIB-16 | IIB-8
DPB Size | 5 | 6 | 7 | 6 | 5

## Slide 6: IIB-16 vs. GOP32/64
 | GOP32/GOP64 |  |  | IIB-16 |  | 
 | BD-rate | Enc. time | Dec. time | BD-rate | Enc. time | Dec. time
Seqs IP=32 on HM | -4.18% | 99% | 100% | -4.17% | 98% | 101%
Seqs IP=32 on JEM | -4.29% | 103% | 100% | -4.44% | 101% | 100%
Seqs IP=64 on HM | -3.73% | 97% | 98% | -3.99% | 96% | 100%
Seqs IP=64 on JEM | -4.03% | 106% | 101% | -4.24% | 104% | 100%

## Slide 7: IIB-16 on HM-16.18
Anchor: HM-16.18
Test : Anchor + IIB-16
SR=Clip3(96, 384, 384*abs(CurrPOC - RefPOC)/IntraPeriod)

## Slide 8: IIB-16 on JEM-7.1
Anchor: JEM-7.1
Test : Anchor + IIB-16
SR=Clip3(96, 384, 384*abs(CurrPOC - RefPOC)/IntraPeriod)

## Slide 9: Conclusions
It is suggested to use the proposed IIB-16 for CTC RA for the development of the next generation video coding standard
  Provide 4.4% and 4.8% gain over GOP16 in HM and JEM under CTC
  Applicable to all CTC sequences with intra period 32, 48, 64 and 96
  Encoding run time memory usage is increased by 10% due to the easy implementation
  No decoder change
  RPS could signal the IIB-N structure
  Only require one additional picture buffer in DPB
 | GOP 16 | GOP 32 | GOP64 | IIB-16 | IIB-8
DPB Size | 5 | 6 | 7 | 6 | 5