## Slide 1: JVET-J0055: Adaptive chroma QP offset on top of Tencent's CfP response
M. Xu, X. Li, S. Liu

## Slide 2: Overview
Observation: luma-chroma gain tradeoff is content-dependent
Encoder-only solution
  Slice-level adaptive chroma QP offset
  On/off decision based on a previously coded picture

## Slide 3: Chroma QP offset in HEVC
Slice header syntax in HEVC
Chroma QP scaling table for 4:2:0 in HEVC
slice_segment_header( ) { | Descriptor
… | 
slice_qp_delta | se(v)
if( pps_slice_chroma_qp_offsets_present_flag ) { | 
slice_cb_qp_offset | se(v)
slice_cr_qp_offset | se(v)
} | 
… | 
qPi | < 30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | > 43
QpC | = qPi | 29 | 30 | 31 | 32 | 33 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | = qPi − 6

## Slide 4: Adaptive chroma QP offset
Slice level chroma QP adjustment
Activation condition: PSNRL+TH<PSNRC in a previously coded picture
Desired chroma QP after scaling: Qpw=(w*qPi+(8-w)*Qpc)>>3
minimum dQP satisfying f(qPi+dQP)>=Qpw
qPi | < 30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | > 43
QpC | = qPi | 29 | 30 | 31 | 32 | 33 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | = qPi − 6
qPi
Qpc
QpW
qPi+dQP

## Slide 5: Simulation results
Sequences | RA (Y) | RA (Cb) | RA (Cr) | Enc Time | Dec Time
FoodMarket4 | -0.13% | 0.71% | 0.99% | 100% | 99%
CatRobot1 | -0.40% | 1.99% | 2.10% | 100% | 110%
DaylightRoad2 | 0.00% | 0.00% | 0.00% | 100% | 105%
ParkRunning3 | -6.59% | 14.06% | 14.72% | 100% | 97%
CampfireParty2 | -13.49% | 12.06% | -0.58% | 97% | 105%
UHD Average | -4.12% | 5.67% | 3.45% | 99% | 103%
BQTerrace | 0.04% | 0.03% | 0.03% | 100% | 101%
RitualDance | 0.01% | 0.30% | 0.22% | 100% | 100%
MarketPlace | 0.01% | 0.02% | 0.01% | 100% | 99%
BasketballDrive | 0.02% | 0.02% | 0.02% | 100% | 99%
Cactus | -0.03% | 1.11% | 1.27% | 100% | 100%
HD Average | 0.01% | 0.30% | 0.31% | 100% | 100%

## Slide 6: Conclusions
Encoder-only adaptive chroma QP offset
It is suggested to consider including this tool in the common software