## Slide 1: JVET-J0064: Prediction dependent transform for intra and inter frame coding
Yongbing Lin, Min Mao, Shichang Song, Jicheng An, Jianhua Zheng, Ce Zhu
HiSilicon, UESTC

## Slide 2: Introduction
In JEM7, multiple core transform has been exploited to improve coding efficiency with significantly increased encoding time
Prediction dependent transform is proposed for better trade-off between coding efficiency and complexity
  Transform selection depends on prediction characteristics of intra/inter coded block, and no additional signaling of transform selection
For intra residual transform
  #1 Intra prediction mode dependent transform for luma and chroma
For inter residual transform
  #2 position dependent transform for HEVC merge mode
  #3 DST-7 for FRUC template matching mode

## Slide 3: #1 Intra prediction mode dependent transform for luma and chroma
Intra prediction mode | Horizontal T | Vertical T | Block Size constraint
Planar Ang. 31,32,34,36,37 | DST-7 | DST-7 | Width <= 64 && Height <= 64
DC Ang. 33, 35 | DCT-2 | DCT-2 | Width <= 64 && Height <= 64
Ang. 2, 4, 6…28,30 Ang. 39,41,43…63,65 | DST-7 | DCT-2 | Width <= 64 && Height <= 64
Ang. 3,5,7…27,29 Ang. 38,40,42…64,66 | DCT-2 | DST-7 | Width <= 64 && Height <= 64
Intra prediction mode | Horizontal T | Vertical T | Block Size constraint
LM, MMLM, 4 MFLMs | DST-7 | DST-7 | Width <= 8 && Height <= 8
Planar | DST-7 | DST-7 | Width <= 16 && Height <= 16
Hor | DST-7 | DCT-2 | Width <= 16 && Height <= 32
Ver, VDIA | DCT-2 | DST-7 | Width <= 32 && Height <= 16
Transform mapping table for luma residual
Transform mapping table for chroma residual
Notes: Different intra prediction mode has different prediction characteristics. Transform selection depends on intra prediction mode and block size
For planar and 5 ANG, DST is applied
For DC and 2 ANG, DCT is used.
For other ANG modes, grouped 2 categories, and apple different combination of DCT and DST
MDD is also applied to chroma residual. LM & planar use DST, HOR and ver use combination of DST and DCT.
Other mode use DCT.

## Slide 4: #2 Position dependent transform for residual of HEVC merge mode
MVP position | Horizontal T | Vertical T | Block Size constraint
L (left) | DST-7 | DCT-2 | Width <= 32 && Height <= 32
A (above) | DCT-2 | DST-7 | Width <= 32 && Height <= 32
Figure 1. Spatial merge MVP candidates
Transform mapping table based on the spatial MVP position
Notes: Transform selection depends on the position of the selected MVP candidate

## Slide 5: #3 DST-7 for residual of FRUC template matching mode
Figure 2. Residual energy distribution of FURC template matching mode. SAD of 8x8 residual block for BasketballDrill sequence coded with QP22
Always use DST-7 transform for residual of FRUC template matching mode in horizontal and vertical directions.
Notes: Residual energy increases from left to right and from above to bottom. DST-7 is used in both hor and ver directions

## Slide 6: Test results under ToolsOff configuration(1/2)
Anchor: JEM7.0 under ToolsOff configuration
ToolsOff: “--EMT=0 --NSST=0 --PDPC=0 --FRUC=0 --BIO=0 --OBMC=0 --IlluCompEnable=0 --AFFINE=0 --ATMVP=0 --IMV=0 --DMVR=0 --BilateralFilter=0 --ALF=0”
Performance of proposed transform ( #1+#2+#3, Intra + inter )
It is observed that 2.45%(AI) and 2.24%(RA) BD-rate reduction with slight encoding time increase can be achieved
Performance of proposed transform ( #1, Intra only)
Notes: It is observed that 2.45%(AI) and 2.24%(RA) BD-rate reduction compared to JEM7 under ToolsOff configuration

## Slide 7: Test results under CTC configuration(2/2)
Anchor: JEM7.0 under CTC configuration
Performance of proposed transform ( #1+#2+#3, Intra+Inter )
It is observed that almost 50%(AI) of encoding time is reduced compared to JEM7
Performance of proposed transform ( #1, Intra only )

## Slide 8: Summary
Prediction dependent transform for better trade-off between coding performance and complexity
  Transform selection depends on prediction characteristics of Intra/inter coded block.
  Totally 2 transform cores: DCT-2 & DST-7
  No additional signaling
  Coding gain of 2.45%(AI) with 109%ET, 2.24%(RA) with 102%ET under ToolsOff configuration
Suggest to further investigation in the next version of reference software

## Slide 9
Thank You
www.hisilicon.com