## Slide 1: JVET-K0366: CE1-related: Partial CU for picture boundary
M. Xu, X. Li, S. Liu

## Slide 2: Overview
In VTM-1/BMS-1 and CE1 sub test 2, at picture boundary, a CU is forced to split until the entire region is inside picture boundary
In some cases, non-split may provide better RD

## Slide 3: Partial CU
A CU may contain a valid and an invalid region
  Valid region is coded as non-split
  Invalid region is ignored
Partial CU in K0366
  Enabled only when the valid region is not power of 2
  Skip mode is inferred for the valid region
  Signaling
valid
invalid
QT
BT
Non-split

## Slide 4: Simulation results
Implemented on top of BMS-1.0
Anchor: VTM-1.0
  Left: RA Right: LB
Thank Bytedance for cross-checking

## Slide 5: Conclusion
A CU may contain both valid and invalid regions
Average 0.33%/0.56% BD-rate gain for RA/LB
It is suggested to test the proposed method in CE