## Slide 1: A Proposal of Simplification of IRAP
October, 2018
JVET 12th Meeting
GaHyun Ryu
WoogIl Choi
MinWoo Park
KiHo Choi

## Slide 2
Contents
Proposal 1 – IRAP type
Proposal 2 – Random Access Flag
Ⅰ
Ⅱ
Ⅲ
Summary

## Slide 3: Proposal Summary
So we propose simple picture type signaling & semantics of IRAP
First, the semantic definition IRAP
Second, the signaling for IRAP picture
Do we need all these Random Access Picture types????
IDR pictures (2): IDR_W_RADL, IDR_N_LP
Clean Random Access (1) : CRA_NUT
Broken Link Access (3) : BLA_W_LP, BLA_W_RADL, BLA_N_LP

## Slide 4: [Proposal 1] IRAP type
A IRAP is a I picture and supports random access and splicing condition
When nal_unit_type is a IRAP then it should guarantee error free decoding process for non leading pictures that follows IRAP
  Leading pictures are not allowed to be referenced by non leading pictures
When bitstream contains IRAP + Leading Pictures + Non Leading Pictures
  The decoder first acquire POC or related values to get leading picture boundary
  The leading pictures should not be referenced by non leading pictures
IRAP
0
3
1
2
4
5
6
7
10
11
10
8
9
Leading
Pictures
Non Leading
Pictures
※ Numbers represents POC or related values
X

## Slide 5: [Proposal 2] broken_link_flag
This flag signals that picture type is a IRAP
Procedures
  If broken_link_flag is 1 → Picture type for random access or splicing condition
  : All pictures in DPB are marked as “unused for reference”
  : The leading pictures should not be referenced by non leading pictures
  If broken_link_flag is 0 → Picture type for normal play condition
  : The leading pictures should be processed as usual
nal_unit_header( ) { | Descriptor
forbidden_zero_bit | f(1)
broken_link_flag | u(1)
nal_unit_type | u(5)
nuh_temporal_id_plus1 | u(3)
reserved | u(6)
} | 

## Slide 6
Thank you