## Slide 1: JVET-L0079 AHG14: Study of methods for progressive intra refresh
K.Kazui (Fujitsu)
12th JVET meeting, Macao, 2018/10/3–12

## Slide 2: Summary
Possible methods for ensuring “exact match” at/after recovery point picture in progressive intra refresh encoding
Possible non-normative methods on VVC tools
  ATMVP
  Intra prediction (incl. CPR)
  Inter prediction
  In-loop filtering (Deblocking, SAO, ALF)
Possible normative method
  Prohibiting reference across clean region boundary
Testing is for further study

## Slide 3: Progressive intra refresh (PIR)
Well-known method for “very” low-delay coding
  Inter-picture only, no bit-consuming Intra-picture (excl. first IDR)
  Each picture has approx. the same number of intra CU and bits
  The position of an intra-coded region shifts picture-by-picture to refresh the entire picture progressively.

## Slide 4: Latency = CPB size
AU-based HRD: latency ≧ (bps/fps)
  Minimum case: Each picture has the same size
DU-based HRD: latency ≧ (bps/fps)/(pic_hgt/CTU_hgt)
  Minimum case: Each CTU-line has the same size

## Slide 5: Intra-coded region (example)
Horizontally long region (top ⇋ bottom)
  Large fluctuation of bits in each CTU line
Vertically long region (left ⇋ right)
  Small fluctuation of bits in each CTU line
  Suitable for DU-based HRD

## Slide 6: For “exact match” with PIR
Essential: disabling reference from clean to dirty region
  Both spatially and horizontally
  Both sample and coding parameter
  Reason: for gradual refresh
Existing standards do not guarantee exact match of pictures in random-access.
  No normative way to distinguish between clean and dirty region
  Several non-normative ways exist.

## Slide 7: Restrictions on reference
ATMVP
Inter prediction
Intra prediction
In-loop filter

## Slide 8: Non-normative methods
Tool | Method | Applied to
ATMVP | slice_temporal_mvp_enable_flag = 0 | R-Access picture
Intra | constrained_intra_pred_flag = 1 | Every picture
 | Limited prediction mode | Clean CU near boundary
 | Slice boundary insertion(*1) | Clean CTU at boundary
CPR | Limited search range | Clean CU
Inter | Limited search range | Clean CU
SAO | Disable edge offset mode | Clean CTU at boundary
 | Slice boundary insertion(*1) | Clean CTU at boundary
DF | Slice boundary insertion(*1) | Clean CTU at boundary
 | Insert semi-dirty region | Every picture
ALF(*2) | Disable ALF | Clean CTU at boundary
(*1) Only effective when clean region boundary is on the CTU grid
(*2) ALF in Draft 2.0

## Slide 9: Limited intra prediction mode

## Slide 10: Semi-dirty region concept
Intra-coded semi-dirty region avoids error propagation from dirty region in deblocking.

## Slide 11: Possible normative method
Normative clean region boundary to control reference
  To be handled similarly as tile/picture boundary
For spatial prediction
  Intra prediction, CPR
  In-loop filtering
  Note: potentially applicable also to 360° video
For temporal prediction
  ATMVP
  Inter prediction
  Note: potentially applicable also to MCTS

## Slide 12: Expected loss mitigation
Benefit to each tool is purely additive to overall coding efficiency
Tool | Loss mitigation | Applied to
ATMVP | Use of TMVP | Dirty CU in R-access pic.
Intra | Refer to inter CU | All CU
 | No limit on prediction mode | Clean CU at boundary
 | No multiple slice insertion | Picture
CPR | Refer to sample near boundary | Clean CU
Inter | Refer to sample near boundary | Clean CU
SAO | No limit on prediction mode | Clean CU at boundary
 | No multiple slice insertion | Picture
DF | No multiple slice insertion | Picture
 | No need for semi-dirty region | Picture
ALF | Use of ALF | Clean CTU at boundary

## Slide 13: Conclusion
Tools in VVC shall be restricted for exact match at recovery point picture in progressive intra refresh
Some non-normative methods exist, but overdo.
Theoretically, normative clean region boundary can mitigate loss.
Suggestion to next round of AHG14
  To develop VTM software for progressive intra refresh with most suitable non-normative methods.
  To discuss normative methods further.