## Slide 1
JVET-L0104
AHG5: Reducing VVC worst-case memory bandwidth by restricting bi-directional 4x4 inter CUs/sub-blocks
Yi-Wen Chen, Xianglin Wang

## Slide 2: Introduction
In VVC, the worst case of MC bandwidth occurs with the bi-prediction 4x4 block
  4x4 CU coded as bi-directional inter mode (AMVP or normal merge mode)
  CUs coded as ATMVP merge mode with 4x4 size of sub-blocks
  CUs coded as bi-directional affine mode (where sub-block size is always 4x4)
8
VVC worst case (4x4 Bi):
No. of ref samples: (4+7) x (4+7) x 2 x 4 = 968
HEVC worst case (8x8 Bi):
No. of ref samples: (8+7) x (8+7) x 2 = 450
8
115% increase

## Slide 3: Proposal: restricting bi-prediction for 4x4 blocks
Disallow bi-directional inter mode (AMVP mode and Merge mode) for 4x4 CU.
ATMVP
  Minimum sub-block size: enlarge from 4x4 to 8x8 (i.e. disabled if either width or height of a CU is equal to 4).
Affine:
  4x4 sub-block size used for uni-directional affine mode;
  8x4/4x8 sub-block size used for bi-directional affine mode.
8
VVC worst case with proposal: (8x4 Bi):
No. of ref samples: (8+7) x (4+7) x 2 x 2= 660
HEVC worst case (8x8 Bi):
No. of ref samples: (8+7) x (8+7) x 2 = 450
8
47% increase

## Slide 4: Results
Anchor: VTM-2.0.1
Test : Anchor + Proposed modifications

## Slide 5: Summary
By restricting 4x4 block Bi-prediction in VVC:
  Worse case MC bandwidth requirement can be significantly reduced.
    Overhead relative to HEVC drops from 115% down to 47%.
  Minor BD-rate increase.
    0.14% for RA (98% decoding time)
    0.16% for LDB (96% decoding time)

## Slide 6: Thank you

## Slide 7: Results of Bi-directional Inter Modes
Anchor: VTM-2.0.1
Test : Anchor + Proposed restrictions on bi-directional inter mode (AMVP and Merge)

## Slide 8: Results of ATMVP
Anchor: VTM-2.0.1
Test : Anchor + Proposed restrictions on ATMVP

## Slide 9: Results of Affine Modes
Anchor: VTM-2.0.1
Test : Anchor + Proposed restrictions on Affine Modes