## Slide 1: CE3-related : Reduced number of reference samples for CCLM parameter calculation (JVET-L0138)
Jangwon Choi (jangwon84.choi@lge.com)

## Slide 2: Summary
Reduced number of reference samples for CCLM parameter calculation
  Limit the number of maximum reference sample pairs, which are used in the CCLM parameter determination to reduce the CCLM complexity
  The modified subsampling position is also introduced to improve the proposed reference sample limitation
Experimental results
  For the CCLM parameter calculation, use two reference sample pairs in 2x2 chroma block
  Else, eight maximum reference sample pairs are used
  The modified subsampling position is applied
Crosscheck : Digital Insights (JVET-L0568)
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.15% | -0.31% | 100% | 99%
Class A2 | 0.04% | 0.19% | -0.03% | 101% | 100%
Class B | 0.01% | -0.11% | -0.24% | 100% | 100%
Class C | -0.02% | -0.03% | 0.09% | 100% | 101%
Class E | -0.01% | -0.11% | -0.35% | 100% | 101%
Overall | 0.01% | -0.05% | -0.16% | 100% | 100%
Class D | 0.01% | 0.10% | -0.14% | 99% | 95%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.10% | -0.13% | 101% | 100%
Class A2 | 0.05% | 0.06% | -0.15% | 99% | 98%
Class B | 0.02% | -0.15% | -0.23% | 100% | 101%
Class C | 0.03% | -0.03% | -0.04% | 101% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | -0.07% | -0.15% | 100% | 100%
Class D | 0.03% | -0.31% | 0.09% | 100% | 94%

## Slide 3: Introduction
The CCLM (cross-component linear model) method in the current VTM2.0.1 software obtains the linear model parameter α and β based on the least mean square algorithm as follows:
  : down-sampled top and left neighbouring reconstructed luma samples
  : top and left neighbouring reconstructed chroma samples
  : twice of the minimum of width and height of the current chroma block
N varies from 4 to 64
The number of operations which are needed to derive the CCLM parameters are increased almost proportionally to the number of N
Operation type | Number of operations in equation
Multiplications | 2N+7
Addition | 4N+18
Division | Two operations are required but they are replaced by look up table and shift in VTM2

## Slide 4: Proposed method
A simplified CCLM parameter calculation
  Uses the smaller number of reference samples in the determination of the CCLM parameters so that the required computational complexity can be reduced significantly.
  The maximum number of N is restricted by Nth, so the reference sample pairs are selected with subsampling if it is required.
  The number of N is reduced by half for worst case (i.e. 2x2 block) and up to by eight (i.e. 32x32) for average case.
Chroma block size | N in VTM 2.0.1 | Restricted Nth in proposed method
2 x 2 | 4 | 2
2 x n / n x 2 (n > 2) | 4 | 4
4 x 4 / 4 x n / n x 4 (n > 4) | 8 | 8
8 x 8 / 8 x n / n x 8 (n > 8) | 16 | 8
16x16, 16x32, 32x16 | 32 | 8
32x32 | 64 | 8

## Slide 5: Proposed method
A simplified CCLM parameter calculation
  The modified subsampling pixel position is also proposed.
  The subsampling pixels can be selected in the inverse positions compared to the previous VTM2

## Slide 6: Experimental results
Tool-on test in VTM2.0.1
Test 1 : Nth = 2 in 2x2 chroma block. Others, Nth = 8
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.07% | 0.09% | -0.02% | 100% | 99%
Class A2 | 0.09% | 0.37% | 0.12% | 101% | 100%
Class B | 0.03% | 0.04% | 0.01% | 100% | 99%
Class C | 0.02% | 0.16% | 0.30% | 100% | 100%
Class E | 0.03% | 0.10% | 0.08% | 101% | 100%
Overall | 0.05% | 0.14% | 0.10% | 100% | 100%
Class D | 0.03% | 0.32% | -0.10% | 100% | 95%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.33% | 0.18% | 101% | 100%
Class A2 | 0.04% | 0.14% | 0.02% | 100% | 98%
Class B | 0.03% | -0.06% | -0.05% | 100% | 101%
Class C | 0.03% | 0.21% | 0.34% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.03% | 0.13% | 0.11% | 100% | 100%
Class D | 0.02% | 0.04% | 0.25% | 100% | 94%

## Slide 7: Experimental results
Tool-on test in VTM2.0.1
Test 2 : Test 1 with the modified subsampling pixel position
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.15% | -0.31% | 100% | 99%
Class A2 | 0.04% | 0.19% | -0.03% | 101% | 100%
Class B | 0.01% | -0.11% | -0.24% | 100% | 100%
Class C | -0.02% | -0.03% | 0.09% | 100% | 101%
Class E | -0.01% | -0.11% | -0.35% | 100% | 101%
Overall | 0.01% | -0.05% | -0.16% | 100% | 100%
Class D | 0.01% | 0.10% | -0.14% | 99% | 95%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.10% | -0.13% | 101% | 100%
Class A2 | 0.05% | 0.06% | -0.15% | 99% | 98%
Class B | 0.02% | -0.15% | -0.23% | 100% | 101%
Class C | 0.03% | -0.03% | -0.04% | 101% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | -0.07% | -0.15% | 100% | 100%
Class D | 0.03% | -0.31% | 0.09% | 100% | 94%

## Slide 8: Conclusion
To reduce the complexity of CCLM parameter derivation, the limitation of reference sample number for CCLM parameter calculation is proposed.
This method can reduce the number of operations in the CCLM prediction with the negligible coding performance changes while the computation complexity is reduced significantly.
The modified subsampling position is also introduced in this proposal, and it can bring synergy effect with the proposed reference sample limitation method
It is suggested to study in the CE

## Slide 9: Appendix
The test results of the modified subsampling pixel position only
Tool-on test in VTM2.0.1 ( not stable EncT and DecT )
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.09% | -0.08% | 101% | 102%
Class A2 | -0.02% | -0.02% | -0.11% | 101% | 101%
Class B | 0.01% | -0.02% | -0.05% | 101% | 103%
Class C | -0.03% | -0.20% | -0.01% | 101% | 106%
Class E | -0.01% | -0.10% | -0.26% | 101% | 104%
Overall | -0.01% | -0.09% | -0.09% | 101% | 103%
Class D | 0.00% | 0.06% | -0.37% | 101% | 108%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.10% | 0.00% | 101% | 89%
Class A2 | 0.01% | -0.14% | -0.02% | 101% | 94%
Class B | 0.00% | -0.06% | -0.07% | 101% | 79%
Class C | -0.02% | -0.06% | -0.01% | 102% | 108%
Class E |  |  |  |  | 
Overall | -0.01% | -0.08% | -0.03% | 101% | 91%
Class D | -0.01% | -0.17% | 0.20% | 102% | 114%