## Slide 1: JVET-L0161 AHG14: Normative Intra Refresh Proposal
Jean-Marc Thiesse
Didier Nicholson
David Gommelet

## Slide 2: Summary
Intra Refresh is usually implemented by encoder-only modifications leading to significant efficiency losses as reported in JVET-L0160 (+20% to +60%).
Normative signalization and associated modifications proposed in this contribution.
Improvement of -5% to -7.8% over encoder-only solution are reported with the proposed (early) implementation.
JVET-L0161

## Slide 3: Proposal: Normative Intra Refresh
Add the signalization for indicating the position of IR CUs.
Exploit this IR CUs positions knowledge to improve the quality for this low latency use-case:
  Do not transmit pred_mode_flag nor cu_skip_flag on IR CU.
  Enable CIP only on IR CU.
  Disabling Deblocking at IR boundary
  => This allows to partially relax the MV constraint (from 6 to 2 pixels).
JVET-L0161

## Slide 4: New signalization
PPS level:
  intra_refresh_enabled_flag
  intra_refresh_mode
  intra_refresh_size
  intra_refresh_delta_qp
Slice level:
  intra_refresh_direction
  intra_refresh_position
JVET-L0161

## Slide 5: Normative Intra Refresh Summary
JVET-L0161

## Slide 6: Results: Normative vs Enc-only Intra Refresh
JVET-L0161
 | Low delay B Normative Intra Refresh Main10 |  |  |  | 
 | Over Low delay B Enc-only Intra Refresh Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -5,01% | -7,76% | -8,68% | 93% | 
Class E | -7,80% | -8,05% | -9,17% | 88% | 
Overall |  |  |  |  | 
Class D | -5,17% | -7,46% | -7,74% | 89% | 
Class F (optional) | -7,81% | -9,88% | -10,20% | 90% | 

## Slide 7: Conclusion
A normative support of Intra Refresh has been proposed and evaluated.
Early results shows significant improvement of 6% over the encoder-only solution proposed in JVET-L0160.
More improvements are expected thanks to:
  Handling of all Filters boundaries, Forced CU splits, Better handling of MV constraints.
Recommendation: Further study this in an AhG.
JVET-L0161

## Slide 8: Thank you
The research leading to this work has been supported by the FUI23 EFIGI project, BPIFrance and Region Ile de France.

## Slide 9: On a Tile-based solution
Split the Picture in vertical or horizontal Tiles with « dependent/independent Tiles » combination.
Pros:
  Elegant design which beneficiate from available signalization.
  Efficient handling of boundaries.
Cons:
  Non-desirable loss due to Tiles breaking of CABAC and Intra Prediction.
  Lack of Refresh size flexibility since Tiles are aligned to CTU. Possible to reduce CTU size but this means loss.
JVET-L0161

## Slide 10: Results: Normative Intra Refresh vs
JVET-L0161
 | Low delay B Normative Intra Refresh Main10 |  |  |  | 
 | Over |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 16,11% | 22,15% | 23,59% | 121% | 
Class E | 59,35% | 85,49% | 92,14% | 140% | 
Overall |  |  |  |  | 
Class D | 18,32% | 32,06% | 35,82% | 125% | 
Class F (optional) | 40,67% | 43,76% | 45,43% | 147% |