## Slide 1: JVET-L0257 CE4-related: Mismatch between text specification and reference software on clipping the positions of collocated blocks for alternative temporal motion vector prediction (ATMVP)
Xiaoyu Xiu, Yuwen He, Yan Ye
InterDigital Communications, Inc.
October, 2018

## Slide 2: Introduction
The ATMVP design in the VVC
  Derive a CU-level motion offset from spatial neighbors and applied to derive the sub-CU-level MVs
  Only motion field of size (1 CTU + 4 columns) can be accessed in the collocated picture
  Proposal
  One mismatch is identified between the VVC draft 2 and the test model software VTM-2.0.1 when clipping is performed to obtain the collocated block positions
  Suggest to fix the mismatch by aligning the clipping method to that in the draft specification

## Slide 3: Proposal
Left: the clipping method in the draft specification;
Right: the clipping method in the VTM-2.0.1
Align the clipping method to that in the draft specification

## Slide 4: Simulation results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.12% | -0.06% | 0.05% | 101% | 102%
Class A2 | -0.06% | -0.05% | -0.01% | 101% | 101%
Class B | 0.00% | -0.09% | -0.08% | 101% | 101%
Class C | 0.03% | 0.12% | -0.12% | 101% | 103%
Class E |  |  |  |  | 
Overall | -0.03% | -0.02% | -0.05% | 101% | 102%
Class D | 0.07% | -0.01% | 0.09% | 101% | 102%
Low delay B Main10 |  |  |  | 
Over VTM-2.0.1 |  |  |  | 
Y | U | V | EncT | DecT
-0.03% | -0.17% | -0.37% | 101% | 102%
0.02% | 0.16% | -0.24% | 100% | 103%
-0.11% | -0.47% | 0.23% | 101% | 100%
-0.03% | -0.14% | -0.17% | 101% | 102%
0.01% | 0.28% | -0.26% | 100% | 101%