## Slide 1: CE3-related: Unification of angular intra prediction for square and non-square blocks (JVET-L0279)
L. Zhao, X. Zhao, S. Liu, X. Li ( Tencent )
2018/10

## Slide 2: Proposed method
First, it is proposed to slightly modify the intra prediction angles so that the diagonal directions (1:1, 1:2, 1:4, … 1:16) of all block shapes are included
Less interpolation using adjusted intra prediction angles
Original table | 0 | 1 | 2 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 26 | 29 | 32 | 35 | 39 | 45 | 49 | 54 | 60 | 68 | 79 | 93 | 114
Modified table | 0 | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 23 | 26 | 29 | 32 | 35 | 39 | 45 | 51 | 57 | 64 | 73 | 86 | 102 | 128

## Slide 3: Proposed method
Second, it is proposed to use different intra prediction angles according to the block aspect ratio for 1:4, 1:8, 1:16 blocks

## Slide 4: Simulation Results
Anchor: VTM2.0.1
Test: first modification
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.02% | -0.03% | 100% | 99% | -0.02% | -0.02% | 0.02% | 99% | 99%
Class A2 | -0.06% | -0.04% | -0.11% | 101% | 101% | -0.01% | 0.01% | -0.11% | 100% | 100%
Class B | -0.08% | -0.16% | -0.06% | 98% | 98% | -0.01% | -0.08% | 0.01% | 100% | 100%
Class C | -0.09% | -0.07% | -0.03% | 100% | 104% | -0.01% | 0.13% | -0.08% | 100% | 100%
Class E | -0.06% | 0.06% | 0.02% | 98% | 98% |  |  |  |  | 
Overall | -0.06% | -0.06% | -0.04% | 99% | 100% | -0.01% | 0.00% | -0.04% | 100% | 100%
Class D | -0.01% | 0.15% | -0.08% | 99% | 94% | 0.05% | 0.06% | 0.30% | 100% | 103%
Class F | -0.04% | -0.07% | -0.03% | 100% | 103% | -0.03% | 0.10% | 0.04% | 99% | 101%

## Slide 5: Simulation Results
Anchor: VTM2.0.1
Test condition: first and second modifications
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.04% | -0.04% | 97% | 93% | 0.00% | 0.03% | -0.01% | 96% | 96%
Class A2 | -0.06% | -0.09% | -0.10% | 97% | 96% | -0.03% | -0.17% | -0.11% | 96% | 95%
Class B | -0.09% | -0.15% | -0.10% | 96% | 95% | -0.03% | -0.12% | -0.17% | 98% | 98%
Class C | -0.10% | -0.11% | 0.06% | 99% | 98% | 0.02% | 0.04% | -0.05% | 99% | 96%
Class E | -0.06% | 0.04% | 0.00% | 97% | 97% |  |  |  |  | 
Overall | -0.06% | -0.08% | -0.04% | 97% | 96% | -0.01% | -0.06% | -0.09% | 97% | 97%
Class D | 0.01% | 0.17% | -0.01% | 99% | 89% | 0.00% | -0.20% | 0.11% | 100% | 100%
Class F | -0.05% | -0.11% | -0.16% | 99% | 100% | -0.01% | 0.04% | 0.02% | 99% | 99%

## Slide 6: Conclusion
Further improvements to the angular intra prediction, 0.06% coding gain is achieved on top of VTM-2.0.1
No impact on complexity
Draft text is simplified
It is proposed to adopt this proposal