## Slide 1
Sub-block MV clipping in affine prediction
(JVET-L0317)
Min Gao, Xiang Li, Meng Xu, Shan Liu

## Slide 2
Affine model motion compensation is performed on 4x4 sub-block basis
Affine MV used for motion compensation (MC) is different from MV stored in motion field, which leads trouble in reference block prefetch in hardware:
  Motion compensation:
    MVs calculated from control points (CP) MV
  Motion field:
    The control points MVs
The Current Affine Model Prediction
Memory bandwidth for 4x4 bi-prediction block is too high ( up to 15.125 sample /pixel)

## Slide 3
Replace the MV of the sub-blocks containing CPs with CP MVs
The Proposed Method
MV00
MV01
MV02
MV03
MV10
MV11
MV12
MV13
MV20
MV21
MV22
MV23
MV30
MV31
MV32
MV33
MV1
MV0
MV00=MV0
MV03=MV1

## Slide 4
Clip the 4 sub-block MVs in each 8x8 block
  so that the max difference between integer parts of 4 sub-block MVs is no more than 1 pixel. Consequently, the memory bandwidth for this 8x8 block becomes (8+7+1)*(8+7+1)/(8x8)*2 = 8 sample/ pixel.
The Proposed Method
MV30
MV31
MV32
MV33
MV00
MV01
MV02
MV03
MV10
MV11
MV12
MV13
MV20
MV21
MV22
MV23
MV30
MV31
MV32
MV33

## Slide 5
Clip the 4 sub-block MVs in each 8x8 block
  Get the minimal MV component among the four 4x4 sub-block MVs
  Use the integer part of Mvminx/y as the minimal MV component:
  The maximal MV component is calculated as follows:
  if the top-right control point is in current 8x8 block:
  Clip MV components of each 4x4 block inside the 8x8:
The Proposed Method
MVminx = min(MVx0, MVx1, MVx2, MVx3)
MVminy = min(MVy0, MVy1, MVy2, MVy3)
MVminx = MVminx >> MV_precision << MV_precision
MVminy = MVminy >> MV_precision << MV_precision
MVmaxx = MVminx + (2 << MV_precision) – 1
MVmaxy = MVminy + (2 << MV_precision) – 1
if (MV1x > MVmaxx)
MVminx = (MV1x >> MV_precision << MV_precision) – (1 << MV_precision)
MVmaxx = MVminx + (2 << MV_precision) – 1
if (MV1y > MVmaxy)
MVminy = (MV1y >> MV_precision << MV_precision) – (1 << MV_precision)
MVmaxy = MVminy + (2 << MV_precision) – 1
MVxi = max(MVminx, min(MVmaxx, MVxi))
MVyi = max(MVminy, min(MVmaxy, MVyi))

## Slide 6
Anchor VTM-2.0.1
Experimental Results:

## Slide 7
The memory bandwidth in the worst case is reduced at the minor BD rate loss;
The MV used in Affine Motion Compensation is the same as motion field;
Anchor VTM-2.0.1
  0.08% and -0.01% BD-rate change for RA and LDB configurations;
  The memory bandwidth in the worst case is 8 samples /pixel;
Conclusions:

## Slide 8
Thanks Dolby for Cross-Check!