## Slide 1
Sub-block MV clipping in planar motion vector prediction (JVET-L0319)
Min Gao, Xiang Li, Meng Xu, Shan Liu

## Slide 2
Planar motion vector prediction:
  Planar motion vector prediction (Planar MVP) is derived by averaging a horizontal and a vertical linear interpolation on 4x4 block basis
The Planar Motion Vector Prediction
Memory bandwidth for 4x4 bi-prediction block is too high ( up to 15.125 sample /pixel)

## Slide 3
Clip sub-block MVs in planar MVP:
  Process unit:
    4x16, 16x4 and 8x8;
  Target:
    Clip all sub-block MVs in process unit such that the max difference between integer parts of the MVs is no more than a given threshold;
The Proposed Method

## Slide 4
Clip sub-block MVs in process unit for planar MVP:
  Get the minimal MV component among 4x4 sub-block MVs:
  Use the integer part of Mvminx/y as the minimal MV component:
  The maximal MV component is calculated as follows:
  Clip MV components of each 4x4 block inside the process unit:
The Proposed Method
MVminx = MVminx >> MV_precision << MV_precision
MVminy = MVminy >> MV_precision << MV_precision
MVmaxx = MVminx + ((thresholdx + 1) << MV_precision) – 1
MVmaxy = MVminy + ((thresholdy + 1) << MV_precision) – 1
(MVminx, MVminy) = (min{MVxi}, min{MVyi})
MVxi = max(MVminx, min(MVmaxx, MVxi))
MVyi = max(MVminy, min(MVmaxy, MVyi))

## Slide 5
Method 1:
  thresholdx = thresholdy=1 for 4x16, 16x4 and 8x8.
Anchor VTM-2.0.1
Experimental Results:
Table. 1. The BD-Rate of method 1.

## Slide 6
Method 2:
  thresholdx = 0 and thresholdy = 1 for 4x16; thresholdx=1 and thresholdy=0 for 16x4; thresholdx=thresholdy=1 for 8x8.
Anchor VTM-2.0.1
Experimental Results:
Table. 2. The BD-Rate of method 2.

## Slide 7
The memory bandwidth in the worst case for Planar motion vector prediction is reduced at the minor BD rate loss;
Method 1:
  0.02%, 0.02% BD bitrate loss for RA and LDB configurations;
  The memory bandwidth in worst case is 4x16 or 16x4: (4+7+1)*(16+7+1)/4/16*2=9 samples/pixel
Method 2:
  0.01%, 0.05% BD bitrate loss for RA and LDB configurations;
  The memory bandwidth in the worst case is 4x16 or 16x4: (4+7)*(16+7+1)/4/16*2=8.25 samples/pixel
Conclusions:

## Slide 8
Thanks Hisilicon for Cross-Check!