## Slide 1: JVET-L0371: CE4-related: Reducing worst case memory bandwidth in inter prediction
Huanbang Chen, Haitao Yang, Jianle Chen (Huawei)

## Slide 2: Problems
In VTM, the worst case of memory bandwidth of motion compensation is for 4x4 bi-prediction, which is used by following modes:
  Bi-prediction 4x4 inter CUs
  ATMVP with bi-prediction 4x4 size of sub-blocks
  Bi-prediction affine CUs

## Slide 3: Proposal
4x4 inter CU: Bi-prediction is disabled
ATMVP:
  the sub-block size is fixed to 8x8.
Affine:
  Different sub-block shapes are used
  In affine merge mode, if the CU size is equal to 8x8, the motion vector in L1 direction is discarded for bi-prediction candidates
Prediction direction and CU size | Sub-block size
uni-prediction | 4x4
bi-prediction, CU width >= CU height | 8x4
bi-prediction, CU width < CU height | 4x8

## Slide 4: Simulation Results
Test # | Test description
a | Restrictions in 4x4 CU
b | Restrictions in ATMVP
c | Restrictions in affine
d | a + b + c
 | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
a | 0.03% | 0.04% | 0.02% | 100% | 100% | 0.02% | -0.01% | -0.15% | 100% | 99%
b | 0.00% | 0.02% | -0.03% | 99% | 100% | -0.03% | 0.01% | -0.19% | 99% | 98%
c | 0.10% | 0.10% | 0.05% | 99% | 97% | 0.11% | 0.05% | -0.02% | 98% | 98%
d | 0.12% | 0.16% | 0.05% | 98% | 96% | 0.14% | 0.13% | -0.12% | 97% | 95%

## Slide 5: Test a
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.09% | 0.04% | 100% | 100%
Class A2 | 0.02% | -0.03% | -0.02% | 100% | 100%
Class B | 0.03% | 0.04% | -0.02% | 99% | 99%
Class C | 0.04% | 0.07% | 0.07% | 99% | 100%
Class E |  |  |  |  | 
Overall | 0.03% | 0.04% | 0.02% | 100% | 100%
Class D | 0.08% | 0.09% | 0.17% | 99% | 100%
Class F (optional) | -0.02% | 0.03% | 0.06% | 99% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.04% | -0.13% | -0.19% | 100% | 100%
Class C | 0.08% | 0.11% | 0.20% | 99% | 99%
Class E | -0.11% | 0.06% | -0.54% | 100% | 99%
Overall | 0.02% | -0.01% | -0.15% | 100% | 99%
Class D | 0.14% | 0.46% | -0.22% | 98% | 100%
Class F (optional) | -0.05% | 0.29% | 0.19% | 99% | 100%

## Slide 6: Test b
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.09% | 0.02% | 100% | 101%
Class A2 | 0.00% | -0.01% | -0.04% | 100% | 99%
Class B | 0.00% | 0.04% | -0.05% | 99% | 100%
Class C | 0.02% | 0.09% | -0.04% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | 0.02% | -0.03% | 99% | 100%
Class D | 0.03% | 0.04% | -0.07% | 98% | 97%
Class F (optional) | -0.01% | 0.01% | -0.03% | 99% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.02% | -0.24% | 100% | 98%
Class C | 0.04% | -0.06% | -0.08% | 99% | 97%
Class E | -0.14% | 0.09% | -0.24% | 100% | 97%
Overall | -0.03% | 0.01% | -0.19% | 99% | 98%
Class D | 0.02% | 0.59% | 0.19% | 98% | 97%
Class F (optional) | 0.01% | 0.13% | -0.09% | 99% | 98%

## Slide 7: Test c
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.02% | -0.04% | 99% | 98%
Class A2 | 0.18% | 0.17% | 0.10% | 99% | 94%
Class B | 0.11% | 0.11% | -0.01% | 98% | 96%
Class C | 0.11% | 0.13% | 0.14% | 98% | 98%
Class E |  |  |  |  | 
Overall | 0.10% | 0.10% | 0.05% | 99% | 97%
Class D | 0.24% | 0.20% | 0.18% | 98% | 97%
Class F (optional) | 0.17% | 0.14% | 0.12% | 98% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.17% | 0.08% | 0.04% | 98% | 97%
Class C | 0.07% | -0.03% | -0.01% | 98% | 98%
Class E | 0.06% | 0.09% | -0.11% | 97% | 98%
Overall | 0.11% | 0.05% | -0.02% | 98% | 98%
Class D | 0.25% | 0.71% | 0.18% | 98% | 97%
Class F (optional) | 0.01% | 0.40% | 0.18% | 98% | 98%

## Slide 8: Test d
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.13% | -0.04% | 99% | 99%
Class A2 | 0.19% | 0.17% | 0.07% | 98% | 94%
Class B | 0.13% | 0.09% | 0.04% | 98% | 96%
Class C | 0.16% | 0.27% | 0.12% | 98% | 97%
Class E |  |  |  |  | 
Overall | 0.12% | 0.16% | 0.05% | 98% | 96%
Class D | 0.34% | 0.23% | 0.33% | 97% | 96%
Class F (optional) | 0.16% | 0.18% | 0.17% | 98% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.20% | 0.31% | 0.03% | 97% | 96%
Class C | 0.17% | 0.08% | 0.06% | 97% | 96%
Class E | 0.02% | -0.10% | -0.60% | 97% | 95%
Overall | 0.14% | 0.13% | -0.12% | 97% | 95%
Class D | 0.44% | 0.52% | 0.31% | 97% | 95%
Class F (optional) | 0.01% | 0.70% | 0.68% | 97% | 98%

## Slide 9: Conclusions
Reduce the worst case memory bandwidth in motion compensation
  0.12%/0.14% luma BD-rate loss with 4%/5% decoding time reduction

## Slide 10
Thank You