## Slide 1: Adaptive Motion Vector Resolution Rounding Align
Yan Zhang, Chun-Chi Chen, Han Huang, Yu Han, Wei-Jung Chien, and Marta Karczewicz

## Slide 2: Abstract
This contribution proposes to align the AMVR Motion Vector rounding implementation in the VTM test model with the description of the VVC specification draft.
This contribution also presents the simulation results of the proposed changes tested on VTM2.0.1. The reported average Y BD-rate numbers are 0.02% in RA and -0.01% in LB.

## Slide 3: Technical description
The negative MV component rounding in AMVR is different from the MV rounding used in all other modes as defined in the spec draft:
  For AMVR MV rounding:
mvX = (mvX + Offset) >> Shift;
  For Affine MV rounding:
mvX = (mvX >= 0) ? (mvX + Offset) >> Shift : -((-mvX + Offset) >> Shift);
Propose to align the negative MV component rounding in software

## Slide 4: Technical description
A two-stage rounding is performed when constructing the AMVP candidate list for MV in 1/16-pel precision:
  AMVR rounding (roundMv()):
  round MV according to the current IMV flag
  Set to low precision (setLowPrec()):
  set the MV representation to ¼-pel precision
  However in the spec draft these two rounding are jointly performed:
  mvX = ( mvX >= 0 ? ( mvX + Offset) >> rightShift : − ( (− mvX + Offset ) >>rightShift ) ) ) << leftShift
  Propose to merge the two MV rounding in software

## Slide 5: Simulation results
The proposed changes are implemented on VTM2.0.1 and tested. Tests were preformed with high cluster load which will affect the encoding/decoding time. Crosschecker’s number might be more accurate. Thanks Huawei for crosschecking.
Simulation results for proposed AMVR rounding align
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.13% | 0.00% | 92% | 97%
Class A2 | 0.02% | 0.04% | -0.06% | 84% | 89%
Class B | 0.03% | 0.06% | 0.02% | 91% | 93%
Class C | 0.01% | 0.02% | -0.02% | 99% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | 0.06% | -0.01% | 92% | 95%
Class D | -0.03% | 0.00% | 0.01% | 100% | 101%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | -0.05% | -0.11% | 105% | 108%
Class C | 0.04% | 0.05% | -0.14% | 102% | 110%
Class E | -0.13% | -0.55% | -0.45% | 99% | 105%
Overall | -0.01% | -0.14% | -0.20% | 102% | 108%
Class D | 0.01% | 0.43% | 0.02% | 103% | 106%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!