## Slide 1: CE6-related:Transform skip for 2x2 chroma blocks and disable 2x2 chroma blocks in intra slices
Luong Pham Van, Wei-Jung Chien, Vadim Seregin, Ted Hsieh, Marta Karczewicz

## Slide 2: Introduction
Block partitioning in VVC
(a) quad-tree (b) vertical binary-tree (c) horizontal binary-tree (d)
vertical triple-tree (e) horizontal triple-tree.
Transform coding for small blocks
Transform
Quantization
Entropy coding
Bitstream
Residual
Transform skip
Transform skip flag

## Slide 3: Proposed
Disable 2x2 chroma in intra slice
Force 2x2 chroma in inter slices to be transform skip
Transform
Quantization
Entropy coding
Bitstream
Residual
Transform skip
Transform skip flag
Entropy coding
Bitstream
Residual
Transform skip

## Slide 4: Experimental Results
Reference software: VTM-2.0.1, VTM configuration
Provided results to assess the proposed methods:
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.05% | 0.03% | 99% | 100%
Class A2 | -0.01% | 0.02% | 0.01% | 99% | 100%
Class B | 0.01% | 0.01% | 0.06% | 100% | 100%
Class C | -0.02% | 0.13% | 0.36% | 99% | 102%
Class E | 0.01% | 0.05% | -0.06% | 100% | 102%
Overall | 0.00% | 0.05% | 0.09% | 100% | 101%
Class D | 0.00% | 0.21% | 0.23% | 99% | 99%
Class F (optional) | 0.01% | 0.26% | 0.45% | 99% | 102%

## Slide 5: Experimental Results
Disable 2x2 chroma in intra slices + 2x2 chroma transform skip in inter slices
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.04% | 0.04% | 99% | 99%
Class A2 | -0.02% | 0.02% | -0.01% | 96% | 99%
Class B | 0.01% | 0.09% | 0.17% | 99% | 99%
Class C | 0.03% | 0.32% | 0.50% | 98% | 97%
Class E |  |  |  |  | 
Overall | 0.01% | 0.13% | 0.19% | 98% | 99%
Class D | 0.02% | 0.40% | 0.43% | 98% | 97%
Class F (optional) | 0.02% | 0.33% | 0.44% | 98% | 98%
 | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.14% | 0.02% | 102% | 119%
Class C | 0.05% | 0.28% | 0.19% | 97% | 96%
Class E | -0.19% | -0.63% | -0.81% | 99% | 102%
Overall | -0.03% | -0.01% | -0.13% | 100% | 107%
Class D | 0.01% | 0.75% | 0.30% | 99% | 96%
Class F (optional) | -0.09% | 0.36% | 0.60% | 99% | 99%

## Slide 6: Conclusions
Two proposed techniques for simplification 2x2 chroma blocks
  Disable 2x2 chroma in intra slice
  Transform skip is forced to 2x2 chroma block in inter slices