## Slide 1: CE1: Summary report on Partitioning

## Slide 2: General information for CE1
All participants submitted the software and the results in time
All SubCE tests were cross checked by at least one other person from the participant list
Cross-checking information showed no mismatches in BD rates
Mismatches in timings were reported in some tests

## Slide 3: VPDUs (JVET-L0081)
Adopted at last meeting to support 64x64 pipelining
Cases of undesired binary and ternary splits
Constraints have no effect on AI results

## Slide 4: Overall results (RA, LDB, LDP)
SubCE-1.1.1: Propose non-square VPDUs
SubCE-1.2.1: Propose extension of TU tiling
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0 |  |  |  |  | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SubCE-1.1.1 | -0,25% | -0,23% | -0,23% | 110% | 100% | -0,20% | -0,45% | -0,33% | 105% | 97% | -0,17% | -0,17% | -0,31% | 105% | 99%
SubCE-1.2.1 | -0,34% | -0,36% | -0,27% | 122% | 101% | -0,26% | -0,27% | -0,13% | 115% | 101% |  |  |  |  | 

## Slide 5: SubCE-1.1.1 (M0446)
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0 |  |  |  |  | Over VTM-3. |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0,48% | -0,48% | -0,42% | 117% | 99% |  |  |  |  |  |  |  |  |  | 
Class A2 | -0,48% | -0,37% | -0,31% | 110% | 99% |  |  |  |  |  |  |  |  |  | 
Class B | -0,17% | -0,17% | -0,24% | 110% | 100% | -0,15% | -0,65% | -0,09% | 105% | 96% | -0,14% | 0,00% | 0,07% | 106% | 96%
Class C | 0,00% | 0,00% | -0,03% | 104% | 102% | -0,01% | 0,26% | 0,19% | 102% | 98% | 0,03% | 0,14% | -0,34% | 101% | 100%
Class E |  |  |  |  |  | -0,54% | -1,06% | -1,41% | 109% | 96% | -0,49% | -0,87% | -0,91% | 109% | 101%
Overall | -0,25% | -0,23% | -0,23% | 110% | 100% | -0,20% | -0,45% | -0,33% | 105% | 97% | -0,17% | -0,17% | -0,31% | 105% | 99%
Class D | 0,02% | -0,12% | -0,09% | 102% | 102% | -0,01% | 0,31% | 0,22% | 100% | 100% | 0,01% | -0,40% | -0,36% | 101% | 101%
Class F | -0,11% | -0,11% | -0,04% | 108% | 102% | -0,17% | -0,15% | -0,25% | 102% | 99% | -0,07% | -0,40% | -0,72% | 102% | 101%
Conditions on ternary splits are changed such that 128x32 and 32x128 block sizes are possible
128x128 is allowed to be split using a ternary split
128x64 and 64x128 are not allowed to be split using a ternary split

## Slide 6: Comments from cross-checker on SubCE-1.1.1
Difference in encoder timings LDB: 110% (CC) vs 105% (P)
Generalize constraints to 2MAX_TU_SIZE_FOR_PROFILE x MAX_TU_SIZE_FOR_PROFILE
How many extra partitions are supported when combining non-squared VPDUs with squared VPDUs
Interest on more details on latency impact of using different VPDU shapes were expressed. Example of (1) 64x64 VPDUs vs (2) mixed shaped VPDUs (1) produces less pipeline dependencies and less latency issues than (2).
Interactions with other tools such as CPR/WPP

## Slide 7: SubCE-1.2.1 (M0236)
Conditions on TU_MAX_TR_SPLIT are changed so that the resulting TUs are contained in a single area on a 64x64 grid.
For example, a 128x64 center block resulted from a ternary split is tiled into four 64x32 TUs.
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0_parallel_jvetl1010.tlist |  |  |  |  | Over VTM-3.0_parallel_jvetl1010.tlist |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0,52% | -0,71% | -0,50% | 132% | 98% |  |  |  |  | 
Class A2 | -0,66% | -0,59% | -0,45% | 123% | 100% |  |  |  |  | 
Class B | -0,28% | -0,26% | -0,24% | 122% | 101% | -0,20% | -0,47% | 0,03% | 118% | 97%
Class C | -0,03% | -0,05% | 0,00% | 113% | 104% | 0,00% | 0,24% | -0,12% | 106% | 107%
Class E |  |  |  |  |  | -0,70% | -0,61% | -0,40% | 123% | 99%
Overall | -0,34% | -0,36% | -0,27% | 122% | 101% | -0,26% | -0,27% | -0,13% | 115% | 101%
Class D | -0,05% | -0,08% | -0,03% | 113% | 105% | 0,00% | 0,29% | 0,21% | 103% | 96%
Class F | -0,17% | -0,22% | -0,16% | 120% | 101% | -0,35% | -0,21% | -0,36% | 110% | 104%