## Slide 1: Non-CE4: Syntax change of MMVD
(JVET-M0069)
Eiichi Sasaki
Takeshi Chujoh, Tomohiro Ikai
Sharp Corporation

## Slide 2: Problem Statement
On VTM-3.0, MMVD causes 0.21%/0.95% BD-Rate loss under high QP condition
  MMVD is not so effective in high QP because MMVD needs over 5-bins to express MVD
  syntax elements of MMVD are signalled in skip or merge mode, hence useless mmvd_flag reduces the efficiency of other skip and merge mode in high QPs
Copyright © All rights reserved, SHARP CORPORATION
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
 | -1.20% | -2.01% | -2.69% | 94% | 91%
 | -0.32% | -0.51% | -1.96% | 95% | 95%
 | -1.35% | -1.66% | -1.90% | 97% | 93%
 | -0.95% | -1.42% | -2.25% | 95% | 93%
 | 0.26% | -0.71% | -1.45% | 97% | 94%
 | -0.79% | -0.94% | -0.75% | 97% | 87%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.60% | -1.73% | -1.77% | 83% | 99%
Class A2 | -0.13% | -1.16% | -1.02% | 80% | 96%
Class B | -0.28% | -1.32% | -1.28% | 80% | 95%
Class C | 0.10% | -0.19% | -0.01% | 80% | 95%
Class E |  |  |  |  | 
Overall | -0.21% | -1.07% | -0.99% | 81% | 96%
Class D | 0.05% | -0.39% | -0.10% | 78% | 96%
Class F | -0.14% | -0.33% | -0.30% | 82% | 95%
Simulation Results of VTM-3.0 w/o MMVD under high QP (42, 47, 52, 57) condition

## Slide 3: Proposed Syntax Structure
To suit high QPs, we change the syntax structure of MMVD
  syntax elements of MMVD are signalled when cu_skip_flag and merge_flag are equal to 0. (before inter_pred_idc)
  derivation process of MMVD is not changed
Copyright © All rights reserved, SHARP CORPORATION
…. | 
.. | 
} else { /* MODE_INTER */ | 
if( cu_skip_flag[ x0 ][ y0 ] = = 0 ) { | 
merge_flag[ x0 ][ y0 ] | ae(v)
if( merge_flag[ x0 ][ y0 ] ) { | 
merge_data( x0, y0, cbWidth, cbHeight ) | 
} else { | 
mmvd_flag[ x0 ][ y0 ] | ae(v)
if( mmvd_flag[ x0 ][ y0 ] = = 1 ) { | 
mmvd_merge_flag[ x0 ][ y0 ] | ae(v)
mmvd_distance_idx[ x0 ][ y0 ] | ae(v)
mmvd_direction_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if( slice_type = = B ) | 
inter_pred_idc[ x0 ][ y0 ] | ae(v)
if( sps_affine_enabled_flag && cbWidth >= 16 && cbHeight >= 16 ) { | 
inter_affine_flag[ x0 ][ y0 ] | ae(v)
…. | 
.. | 
Part of coding unit syntax
AMVP mode
proposed MMVD
(a MVD mode)

## Slide 4: Experimental Results
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
 | -0.20% | -0.11% | -0.08% | 102% | 101%
 | -0.21% | 0.05% | -0.14% | 101% | 101%
 | -0.32% | -0.01% | -0.36% | 102% | 100%
 | -0.23% | -0.03% | -0.17% | 102% | 100%
 | -0.28% | 0.23% | 0.21% | 102% | 101%
 | -0.16% | 0.12% | -0.07% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
 | -0.73% | -0.91% | -1.43% | 102% | 93%
 | -0.56% | -0.25% | -0.54% | 102% | 95%
 | -0.99% | -1.21% | -1.68% | 102% | 92%
 | -0.74% | -0.77% | -1.19% | 102% | 94%
 | 0.30% | -0.31% | -0.31% | 104% | 95%
 | -0.53% | -0.64% | -1.58% | 101% | 89%
Proposed Syntax Structure is tested under high QP condition and CTC
Copyright © All rights reserved, SHARP CORPORATION
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.51% | -0.58% | -0.74% | 100% | 101%
Class A2 | -0.49% | -0.48% | -0.65% | 101% | 100%
Class B | -0.39% | -0.73% | -0.73% | 101% | 99%
Class C | -0.10% | 0.12% | -0.12% | 101% | 96%
Class E |  |  |  |  | 
Overall | -0.36% | -0.42% | -0.55% | 101% | 99%
Class D | -0.14% | -0.51% | 0.02% | 101% | 96%
Class F | -0.22% | -0.27% | -0.31% | 100% | 95%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.07% | 0.04% | 101% | 100%
Class A2 | -0.08% | 0.14% | 0.24% | 103% | 100%
Class B | -0.13% | 0.15% | 0.02% | 102% | 100%
Class C | -0.13% | 0.03% | 0.17% | 101% | 101%
Class E |  |  |  |  | 
Overall | -0.11% | 0.07% | 0.11% | 102% | 100%
Class D | -0.12% | 0.19% | 0.16% | 103% | 101%
Class F | -0.09% | -0.03% | -0.02% | 105% | 100%
Results of high QP condition
Results of CTC

## Slide 5: Conclusion
Syntax change of MMVD is proposed
Experimental results show
  -0.36%/-0.74% BD-Rate gain in RA and LB under high QP condition
  -0.11%/-0.23% luma BD-Rate gain in RA and LB under CTC
It is suggested to adopt proposed syntax structure in the next VVC draft