## Slide 1
JVET-M0226
CE2: Reducing worst-case memory bandwidth of affine mode (test 2.4.1)
Yi-Wen Chen, Xianglin Wang

## Slide 2: Introduction
In VVC, the worst case of MC bandwidth occurs with CUs coded as bi-directional affine mode
8
VVC worst case (4x4 Bi):
No. of ref samples: (4+7) x (4+7) x 2 x 4 = 968
HEVC worst case (8x8 Bi):
No. of ref samples: (8+7) x (8+7) x 2 = 450
8
115% increase

## Slide 3: CE2.4.1: restricting bi-prediction for 4x4 blocks
CE2.4.1.a
  4x4 sub-block size used for uni-directional affine mode
  8x4/4x8 sub-block size used for bi-directional affine mode according to its width and height
CE2.4.1.b
  4x4 sub-block size used for uni-directional affine mode
  8x4 sub-block size used for bi-directional affine mode
CE2.4.1.c
  4x4 sub-block size used for uni-directional affine mode
  4x8 sub-block size used for bi-directional affine mode
8
VVC worst case with proposal: (8x4 Bi):
No. of ref samples: (8+7) x (4+7) x 2 x 2= 660
HEVC worst case (8x8 Bi):
No. of ref samples: (8+7) x (8+7) x 2 = 450
8
47% increase

## Slide 4: Results CE2.4.1.a
Anchor: VTM-3.0
Test : Anchor + 8x4/4x8 sub-block size used for bi-directional affine mode.

## Slide 5: Results CE2.4.1.b
Anchor: VTM-3.0
Test : Anchor + 8x4 sub-block size used for bi-directional affine mode.

## Slide 6: Results CE2.4.1.c
Anchor: VTM-3.0
Test : Anchor + 4x8 sub-block size used for bi-directional affine mode.

## Slide 7: Summary
Results are provided for restricting the bi-directional MC block size to be at least 4x8/8x4 or larger
The proposal results in 32% reduction of the worst-case bandwidth requirement for the current VVC, with about 0.1% BD-rate increase
It is recommended to consider adoption of the restriction of CE2.4.1.b into VVC

## Slide 8: Thank you