## Slide 1
JVET-M0234
Non-CE10: Triangle prediction merge index coding
Xianglin Wang, Yi-Wen Chen

## Slide 2: Current Triangle Prediction Merge Index Signaling
(Partition orientation, idx1, idx2)
g_triangleCombination[40][3] = {
{ 0, 1, 0 }, { 1, 0, 1 }, { 1, 0, 2 }, { 0, 0, 1 }, { 0, 2, 0 },
{ 1, 0, 3 }, { 1, 0, 4 }, { 1, 1, 0 }, { 0, 3, 0 }, { 0, 4, 0 },
{ 0, 0, 2 }, { 0, 1, 2 }, { 1, 1, 2 }, { 0, 0, 4 }, { 0, 0, 3 },
{ 0, 1, 3 }, { 0, 1, 4 }, { 1, 1, 4 }, { 1, 1, 3 }, { 1, 2, 1 },
{ 1, 2, 0 }, { 0, 2, 1 }, { 0, 4, 3 }, { 1, 3, 0 }, { 1, 3, 2 },
{ 1, 3, 4 }, { 1, 4, 0 }, { 1, 3, 1 }, { 1, 2, 3 }, { 1, 4, 1 },
{ 0, 4, 1 }, { 0, 2, 3 }, { 1, 4, 2 }, { 0, 3, 2 }, { 1, 4, 3 },
{ 0, 3, 1 }, { 0, 2, 4 }, { 1, 2, 4 }, { 0, 4, 2 }, { 0, 3, 4 },
};
Bit string form | Range of code value
0 x0 | 0 ~ 1
1 0 x1 x0 | 2 ~ 5
1 1 0 x2 x1 x0 | 6 ~ 13
1 1 1 0 x3 x2 x1 x0 | 14 ~ 29
1 1 1 1 0 x4 x3 x2 x1 x0 | 30 ~ 39

## Slide 3: Proposed Triangle Merge Index Signaling
Separate signaling of a partition orientation flag
Separate signaling of the index mapping
Joint index signaling
g_triangleCombination[10][2] = {
{ 0, 1 }, { 0, 2 }, { 1, 2 }, { 0, 3 }, { 1, 3 },
{ 2, 3 }, { 0, 4 }, { 1, 4 },{ 2, 4 }, { 3, 4 },
};
Bit string form | Range of code value
0 x0 | 0 ~ 1
1 x2 x1 x0 | 2 ~ 9

## Slide 4: Proposal Results
Anchor: VTM-3.0

## Slide 5: Triangle Mode Flag Signaling
Disable triangle mode flag signaling if either CIIP flag or MMVD flag is true.

## Slide 6: Thank you