## Slide 1: Non-CE9: Modifications on Bi-Directional Optical Flow
Hongbin Liu, Li Zhang, Kai Zhang, Jizheng Xu Yue Wang, Pengwei Zhao, Dingkun Hong

## Slide 2: Summary
Motivation
  BDOF is allowed for large block size, which requires large local buffer.
  In early termination, SAD is calculated for each 4x4 sub-block, which is complex.
Proposed solution
  Split large blocks into small blocks
  SAD is calculated only using 4 corner pixels of each 4x4 sub-block.
  No impact on compression performance.
Thanks Foxconn for crosschecking (JVET-M0731)

## Slide 3: Proposed Method
If a CU contains more than N pixels, it is split into sub-blocks with N pixels.
  N = 4096 or 1024.
SAD is calculated only using 4 corner pixels of each 4x4 sub-block.
  Operations required in SAD calculation is reduced by around 75%.

## Slide 4: Simulation results (N = 4096)
Anchor: VTM-3.0
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.04% | 0.05% | 101% | 99%
Class A2 | -0.01% | 0.01% | 0.01% | 100% | 100%
Class B | 0.00% | -0.02% | -0.05% | 101% | 100%
Class C | 0.00% | -0.01% | 0.00% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | -0.01% | 101% | 100%
Class D | 0.00% | 0.00% | 0.01% | 100% | 100%
Class F | -0.01% | 0.01% | 0.01% | 100% | 101%

## Slide 5: Simulation results (N = 1024)
Anchor: VTM-3.0
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | -0.01% | 100% | 101%
Class A2 | -0.01% | 0.03% | 0.04% | 100% | 100%
Class B | -0.01% | 0.03% | 0.00% | 101% | 100%
Class C | -0.01% | 0.03% | -0.01% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.01% | 0.03% | 0.01% | 100% | 100%
Class D | 0.01% | -0.02% | 0.05% | 101% | 101%
Class F | -0.01% | 0.00% | 0.00% | 101% | 103%

## Slide 6: Simulation results (SAD simplification)
Anchor: VTM-3.0
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.02% | 0.00% | 100% | 100%
Class A2 | 0.00% | 0.02% | 0.03% | 100% | 101%
Class B | 0.00% | 0.03% | -0.06% | 100% | 100%
Class C | 0.02% | 0.03% | -0.04% | 100% | 98%
Class E |  |  |  |  | 
Overall | 0.01% | 0.03% | -0.02% | 100% | 99%
Class D | 0.04% | -0.05% | 0.06% | 101% | 99%
Class F | -0.01% | -0.05% | -0.04% | 101% | 100%

## Slide 7: Simulation results (N=1024 + SAD simplification)
Anchor: VTM-3.0
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.05% | 0.06% | 100% | 101%
Class A2 | 0.00% | -0.03% | 0.05% | 100% | 101%
Class B | 0.01% | 0.01% | -0.02% | 99% | 100%
Class C | 0.01% | 0.00% | -0.03% | 98% | 98%
Class E |  |  |  |  | 
Overall | 0.01% | 0.01% | 0.01% | 99% | 100%
Class D | 0.05% | -0.09% | 0.03% | 101% | 102%
Class F | 0.00% | -0.04% | -0.03% | 99% | 100%

## Slide 8
Thanks！