## Slide 1: JVET-M0281 CE4.1.5: Inter Motion Vector Pruning
January 2019
A. Robert - Technicolor

## Slide 2: Motivation
  VTM-3:
    In AMVP and Merge coding modes, motion predictor lists are constructed.
    But in the current reference software, some predictor redundancy can be observed
  Goal of this contribution:
    Reduce predictor redundancies
    Harmonize motion predictor lists construction

## Slide 3: AMVP coding mode
  Adopted last meeting:
    Perform ¼-pel rounding with AMVR one
    Prune all predictors
  For non AMVR predictors, ¼-pel rounding is still performed at the end of the list construction
  Proposed uniformization of the roundings
    Perform ¼-pel or AMVR+1/4-pel rounding before every pruning
List | AMVP
Candidates type | - Spatial A0/A1 + unscaled/scaled - Spatial B0/B1/B2 + unscaled/scaled - Rounding AMVR+¼-pel/¼-pel - Pruned spatial cand - TMVP C0/C1 + rounding AMVR+¼-pel/¼-pel + pruned all - HMVP last to first + rounding AMVR+¼-pel/¼-pel + pruned all - Rounding ¼-pel for non AMVR case - Fulfill with zero
list size/total nb of possible candidates | 2 / 2+1+6+2 = 11 for each ref pic
Nb comparison mv refidx total int | 1+1+6+0 = 8+0 = 8 for each ref pic (x4) 16 16
  → no integer comparisons added

## Slide 4: Merge coding mode
  Adopted last meeting:
    Simplified pruning of spatial predictors
    Remove pruning of temporal predictor
  Proposed pruning for pair-wise predictor
    Simple and early
    For each pair (A,B), discard pair-wise calculation
      If A and B are bi-directional and MV are equal,
      If A and B are uni-directional or only A is bi-directional and MV from common list are equal,
      If only B is bi-directional and MV and reference frame from the common list are equal.
List | Merge
Candidates | - Spatial A1 - Spatial B1 + pruned A1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP last to first + pruned all + let one space for pairwise - Pairwise of pruned cand {0,1}, {0,2}, {1,2}, {0,3}, {1,3}, {2,3} - Fulfill with zero
list size / total nb of possible candidates | 6 / 5+1+6+6+6 = 24
Nb comparison mv refidx total int | (5+0+(6*4)+6+0)*2 = 58+12 = 70 (5+0+(6*4)+0+0)*2 = 58 = 58 174 198
  → 24 integer comparisons more (+12%)

## Slide 5: Simulation Results
  Results over VTM-3.0:
    AMVP uniformization

## Slide 6: Simulation Results
  Results over VTM-3.0:
    Merge pair-wise pruning

## Slide 7: Simulation Results
  Results over VTM-3.0:
    Proposed AMVP + Merge