## Slide 1: Reduced Secondary Transform (RST) Algorithm Description (JVET-M0292)
Moonmo Koo, Mehdi Salehifar, Jaehyun Kim, and Seung Hwan Kim

## Slide 2: Overview
Reduced Secondary Transform (RST)
  16x16 and 16x64 non-separable transform for 4x4 and 8x8 blocks, respectively
Primary forward and inverse transforms are still performed the same way
  As two 1-D horizontal/vertical transform passes
Secondary forward and inverse transforms are a separate process step from that of primary transforms
  For encoder
    Primary forward transform is performed first, then followed by secondary forward transform and quantization, and CABAC bit encoding
  For decoder
    CABAC bit decoding and inverse Q, then Secondary inverse transform is performed first, then followed by primary inverse transform.
RST applies only to intra coded TU. (no inter coded TU).
  Intra coded TU in both intra slice and inter slice that has blocks coded in intra.

## Slide 3: Encoder Side – 5 cases
4x4
Residual
4x4
Prim.
Coeff
2D Forward
Primary
Transform
Forward
Secondary
Transform
4x2
Sec. Coeff
0
Case 1 : TU = 4x4
Bitstream
max. contains
8 non-zero
coefficients
8x4
Residual
2D Forward
Primary
Transform
8x4
Primary Coeff.
Forward
Secondary
Transform
4x4
Sec.
Coeff
4x4
Prim.
Coeff
2D Forward
Primary
Transform
Forward
Secondary
Transform
4x4
Sec.
Coeff
4x4
Prim.
Coeff
4x8
Residual
4x8
Prim.
Coeff
Case 2 : TU = 8x4, 4x8
Bitstream
max. contains
32 non-zero
coefficients
4x4
Rig-Half Prim.
Coeff
4x4
Bot-Half
Prim.
Coeff
    [16x16 kernel] * [16x1 prim]  [16x1 sec]
    [8x16 kernel] * [16x1 prim]  [8x1 sec]

## Slide 4: Encoder Side – 5 cases
Nx4
Residual
2D Forward
Primary
Transform
Forward
Secondary
Transform
2D Forward
Primary
Transform
Forward
Secondary
Transform
4x4
Sec.
Coeff
4x4
Prim.
Coeff
4xN
Residual
4xN
Prim.
Coeff
Case 3 : TU = Nx4, 4xN (N ≥ 16)
Bitstream
max. contains
Nx4 non-zero
coefficients
(N-8)x4
Remain.
Prim.
Coeff
    Two times of [16x16 kernel] * [16x1 prim]  Two [16x1 sec]
Nx4
Primary Coeff.
4x4
Sec.
Coeff
4x4
Sec.
Coeff
(N-8)x4
Remaining Prim.
Coeff
4x4
Sec.
Coeff

## Slide 5: Encoder Side – 4 cases (Cont’d)
8x8
Residual
Case 4 : TU = 8x8
2D Forward
Primary
Transform
Forward
Secondary
Transform
8x8
Primary
Coefficients
4x2
Sec. Coeff
0
0
0
0
Bitstream
max. contains
8 non-zero
coefficients
[8x64 kernel] * [64x1 prim]  [8x1 sec]

## Slide 6: Encoder Side – 4 cases (Cont’d)
8x16
Residual
Case 5 : TU = 8x16, 16x8, and >=16x16 (larger or equal to 16x16)
2D Forward
Primary
Transform
Forward
Secondary
Transform
8x16
Primary
Coefficients
0
0
0
Bitstream max. contains 80 non-zero coefficients
8x8
Bottom-Half
Primary
Coefficients
4x4
Sec.
Coeff
    [16x64 kernel] * [64x1 prim]  [16x1 sec]

## Slide 7: Encoder Side – 4 cases (Cont’d)
8x16
Primary
Coefficients
16x8
Residual
Case 5 : TU = 8x16, 16x8, and >=16x16
2D Forward
Primary
Transform
Forward
Secondary
Transform
0
0
0
Bitstream max. contains 80 non-zero coefficients
8x8
Right-Half
Primary
Coefficients
4x4
Sec.
Coeff
    [16x64 kernel] * [64x1 prim]  [16x1 sec]

## Slide 8: Encoder Side – 4 cases (Cont’d)
16x16
Residual
Case 5 : TU = 8x16, 16x8, and >=16x16
2D Forward
Primary
Transform
Forward
Secondary
Transform
16x16
Primary
Coefficients
Bitstream
max. contains
16 non-zero secondary coefficents and
192 non-zero primary
coefficients
    [16x64 kernel] * [64x1 prim]  [16x1 sec]
4x4
Sec.
Coeff
0
0
0
8x8 top-right
Prim coeff.
8x8 bottom-right
Prim coeff.
8x8 bottom-left
Prim coeff.

## Slide 9: Encoder Side – 5 cases
4x4
  4x4 primary forward transform coefficients are input to the secondary forward transform.
    [8x16 kernel] * [16x1 prim]  [8x1 sec]
  The secondary forward transform output ([8x1]) is placed following residual coding scan order. The other 8 coefficients are set to all 0.
  Bitstream does not contain any coefficient from the primary forward transform.
4x8, 8x4
  Only the top/left 4x4 primary forward transform coefficients (as 16x1) are input to the secondary forward transform.
    [16x16 kernel] * [16x1 prim]  [16x1 sec]
  The secondary forward transform output is also an 4x4 coefficient block (top/left 4x4 inside 4x8/8x4)
  Bitstream contains max. 4x4 secondary forward transformed coefficients and 4x4 primary forward transformed coefficients.
4xN, Nx4 (N ≥ 16)
  Two adjacent top-left 4x4 primary forward transform coefficients (as two 16x1) are input to the secondary forward transform.
    Two times of [16x16 kernel] * [16x1 prim]  two [16x1 sec]
  The secondary forward transform output is TWO adjacent top-left 4x4 coefficient blocks.
  Bitstream contains max. two 4x4 blocks of secondary forward transformed coefficients and remaining primary forward transformed coefficients.
8x8
  8x8 primary forward transform coefficients are input to the secondary forward transform.
    [8x64 kernel] * [64x1prim]  [8x1 sec]
  The secondary forward transform output ([8x1]) is placed following residual coding scan order. The other 48 coefficients are set to all 0.
  Bitstream does not contain any coefficient from the primary forward transform.
8x16, 16x8, and >=16x16
  Top/Left/Top-left 8x8 primary forward transform coefficients are input to the secondary forward transform.
    [16x64 kernel] * [64x1 prim]  [16x1 sec]
  The secondary forward transform output is only ONE 4x4 coefficient block ([16x1]; top-left 4x4 coefficient block of 8x16/16x8/>=16x16 TU)
  Bitstream contains max. 4x4 secondary forward transformed coefficients and three 8x8 primary forward transformed coefficients.
    Basically zeroed 3 4x4 coefficients within the top-left corner 8x8 block in the bitstream.

## Slide 10: Decoder Side – 5 cases
4x4
  Bitstream contains 8 coefficients and are input to the secondary inverse transform.
    [16x8 kernel] * [8x1 from bitstream]  [16x1 insert into prim]
  The secondary inverse transform output is also an 4x4 coefficient block ([16x1]).
  Bitstream does not contain any coefficient from the primary transform.
4x8, 8x4
  Bitstream contains 16 coefficients and are input to the secondary inverse transform.
    [16x16 kernel] * [16x1 from bitstream]  [16x1 insert into prim]
  The secondary inverse transform output is ONLY ONE 4x4 coefficient block (top/left 4x4 inside 4x8/8x4)
  Bitstream contains the remaining ONE bottom/right 4x4 coefficients of the primary transform.
4xN, Nx4
  Bitstream contains 32 coefficients (two 16x1) and are input to the secondary inverse transform.
    Two times of [16x16 kernel] * [16x1 from bitstream]  two [16x1 insert into prim]
  The secondary inverse transform output is TWO adjacent top-left 4x4 coefficient blocks.
  Bitstream contains the remaining bottom/right 4x4 coefficient blocks of the primary transform.
8x8
  Bitstream contains 8 coefficients and are input to the secondary inverse transform.
    [64x8 kernel] * [8x1 from bitstream]  [64x1 insert into prim]
  The secondary inverse transform output is an 8x8 coefficient block ([64x1]).
  Bitstream does not contain any coefficient from the primary transform.
8x16, 16x8, and >=16x16
  Bitstream contains 16 coefficients and are input to the secondary inverse transform.
    [64x16 kernel] * [16x1 from bitstream]  [64x1 insert into prim]
  The secondary inverse transform output only ONE 8x8 coefficient block (top-left 8x8)
  Bitstream contains the remaining 8x8 coefficient blocks of the primary transform.
    Basically zeroed all other coefficients within the top-left corner 8x8 block in the bitstream.

## Slide 11: Worst Case Performance
Restriction of max. computation complexity to 8 multiplications per sample of any block size
  # of multiplications / # of samples per TU ≤ 8
Analysis of the max. computation complexity
  4x4 TU: (16x8) / (4x4) = 8
  8x8 TU: (64x8) / (8x8) = 8
  4x8/8x4 TU: (16x16) / (4x8) = 8
  4xN/Nx4 TU (N ≥ 16): 2x(16x16) / (4xN) ≤ 2x(16x16) / (4x16) = 8
  Others (8x16/16x8/>=16x16 TU)
    8x16/16x8 TU: (64x16) / (8x16) = 8
    >=16x16 TU: (64x16) / (M x N) ≤ (64x16) / (16 x 16) = 4, where M, N ≥ 16

## Slide 12: RST Kernel
Encoder
  2 base kernels : 16x16 and 16x64
    [16x16 kernel]
    [16x8 kernel], top-left corner subsampled from 16x16 base kernel.
    [16x64 kernel]
    [8x64 kernel], top-left corner subsampled from 16x64 base kernel.
Decoder
  The 2 decoder base kernels are the transpose of the corresponding encoder base kernels.
    [16x16 kernel]
    [16x8 kernel], top-left corner subsampled from 16x16 base kernel.
    [64x16 kernel]
    [64x8 kernel], top-left corner subsampled from 64x16 base kernel.
Total RST kernel memory usage is 10 Kbytes.
  4 transform sets && 2 transforms per set, for each of 16x16 and 16x64
  4 x 2 x ( 16x16 + 16x64 ) = 10 x 1024 bytes
  10K contains 4 sets of the “two base kernels”, that can be selected based on intra prediction modes of the block.

## Slide 13: Mapping from Intra Prediction Modes to Base Kernel Selection
Range of input intra prediction mode for transform set selection
  [ -14, 83 ]: including wide angles and CCLM modes
4 sets of Base Kernel (0 to 3)
If CCLM modes (> 80), transform set 0 is selected.
Otherwise,
intraPredMode | Tr. set index
intraPredMode < 0 | 1
0 <= intraPredMode <= 1 | 0
2 <= intraPredMode <= 12 | 1
13 <= intraPredMode <= 23 | 2
24 <= intraPredMode <= 44 | 3
45 <= intraPredMode <= 55 | 2
56 <= intraPredMode | 1

## Slide 14: Precisions
Encoder Multipliers
  16-bit signed coefficients (from primary transform) * 8-bit signed kernel
Decoder Multipliers
  16-bit signed coefficients (from bitstream) * 8-bit signed kernel

## Slide 15: Encoder Notes
There is no change to the parsing of the coefficients in the bitstream.
  The final composite transform output coefficient block is sent to bitstream CABAC packing.
    No distinction in coding secondary transform coefficients as compared with that of primary transform coefficients.

## Slide 16: Decoder Notes
From the bitstream, there is no awareness of the presence of the secondary transform coefficients. As such, the coefficient scan path for a TU block is not affected by the secondary transform.