## Slide 1: CE10-related: Modification for blocks applied with Combined Inter-Intra prediction （JVET-M0294）
Biao Wang, Anand Meher Kotra, Semih Esenlik,
Han Gao, Jianle Chen

## Slide 2: Problem and Proposal of CIIP (I)
Problem: Inconsistency of blocks with CIIP in MPM list construction
  Intra block: neighboring blocks with CIIP are considered as Inter block
  Blocks with CIIP: neighboring blocks with CIIP are considered as Intra block
    require extra memory storing intra mode for CIIP blocks
Proposed: consistency of blocks with CIIP in MPM list construction
  Intra block: neighboring blocks with CIIP are considered as Inter block
  Blocks with CIIP: neighboring blocks with CIIP are considered as Inter block
    NO extra memory needs to store intra mode for CIIP blocks

## Slide 3: Results:
 | Random access Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.06% | 0.03% | 100% | 100%
Class A2 | -0.02% | 0.02% | 0.09% | 100% | 100%
Class B | -0.01% | 0.02% | -0.01% | 100% | 100%
Class C | 0.00% | -0.02% | -0.03% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.01% | -0.01% | 0.01% | 100% | 100%
Class D | 0.01% | -0.05% | 0.02% | 100% | 100%
Class F | 0.02% | -0.01% | -0.02% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | -0.25% | -0.11% | 100% | 99%
Class C | 0.02% | 0.25% | 0.01% | 100% | 99%
Class E | 0.01% | 0.11% | -0.21% | 100% | 101%
Overall | 0.01% | 0.01% | -0.10% | 100% | 99%
Class D | -0.03% | 0.17% | 0.14% | 100% | 100%
Class F | -0.01% | 0.08% | -0.05% | 100% | 100%
Significant simplification with small coding gain:
RA: -0.01%
LDB: 0.01%
LDP: -0.04%
 | Low delay P Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.02% | 0.31% | 0.19% | 100% | 98%
Class C | -0.02% | 0.13% | -0.10% | 100% | 100%
Class E | -0.11% | -0.04% | -0.91% | 100% | 101%
Overall | -0.04% | 0.16% | -0.18% | 100% | 99%
Class D | 0.00% | -0.42% | 0.04% | 100% | 99%
Class F | 0.06% | -0.48% | -0.43% | 100% | 100%

## Slide 4: Problem and Proposal of CIIP (II)
Problem: in DBF, CIIP blocks are considered as inter blocks
  CIIP introduces intra prediction and might introduce blocking artifacts.
Proposed:
  Proposal I + Consider CIIP blocks as Intra block in DBF

## Slide 5: Results:
 | Random access Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.21% | -0.34% | 101% | 100%
Class A2 | -0.01% | -0.06% | 0.02% | 100% | 101%
Class B | 0.00% | -0.05% | -0.30% | 101% | 102%
Class C | 0.02% | -0.15% | -0.14% | 100% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | -0.11% | -0.20% | 100% | 101%
Class D | 0.01% | -0.05% | -0.19% | 100% | 101%
Class F | 0.02% | -0.11% | -0.07% | 100% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | -0.62% | -0.37% | 100% | 101%
Class C | -0.02% | -0.07% | -0.17% | 100% | 101%
Class E | -0.01% | -0.11% | -0.30% | 100% | 103%
Overall | 0.00% | -0.31% | -0.29% | 100% | 101%
Class D | 0.02% | -0.11% | -0.10% | 100% | 101%
Class F | -0.02% | 0.09% | 0.05% | 100% | 102%
Objective results:
RA: 0.00%
LDB: 0.00%
LDP: -0.07%
 | Low delay P Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.09% | -0.47% | 100% | 100%
Class C | -0.05% | -0.20% | -0.47% | 100% | 101%
Class E | -0.17% | -0.23% | -1.41% | 100% | 102%
Overall | -0.07% | -0.16% | -0.70% | 100% | 101%
Class D | -0.03% | -0.74% | -0.51% | 100% | 101%
Class F | 0.09% | -0.47% | 0.13% | 100% | 101%

## Slide 6
Bottom: Cactus encoded at QP 37, proposed
Top: Cactus encoded at QP 37, VTM3.0

## Slide 7: Summary & Conclusion
Consider neighbor CIIP blocks as Inter block in MPM list construction
  reduced memory storage to store intra modes for CIIP blocks
Consider CIIP blocks as intra block in Deblocking filtering:
  RA: 0.00%, LDB: 0.00%, LDP: -0.07%
  Subjective improvements
We suggest to adopt the proposed method in VVC
Thanks to Bytedance for crosschecking

## Slide 8
Thank You
www.huawei.com