## Slide 1: JVET-M0300, CE4-related: HMVP and parallel processing with tiles and tile groups
Anand Meher Kotra, Jianle Chen, Semih Esenlik, Biao Wang, Han Gao

## Slide 2: Overview
In VTM-3.0, History-based motion vector prediction (HMVP) list/table is reset at the beginning of each CTU row
  Enables parallel processing with tools such as waterfronts (WPP)
  Syntax is based on slices, which is as follows:
Current proposal extends the idea for tiles and tile groups
  Reset HMVP table at beginning of tile group, tile and beginning of each CTU row inside a tile
if (slice_type != I && (CtbAddrInRs % PicWidthInCtbsY = = 0 ) ¦¦ ( CtbAddrInRs = = slice_address ) )
NumHmvpCand = 0

## Slide 3: Syntax is as follows
tile_group_data( ) { | Descriptor
tileIdx = tile_group_address | 
for( i = 0; i <= num_tiles_in_tile_group_minus1; i++, tileIdx++ ) { | 
ctbAddrInTs = FirstCtbAddrTs[ tileIdx ] | 
for( j = 0; j < NumCtusInTile[ tileIdx ]; j++, ctbAddrInTs++ ) { | 
firstCtbInCtuRowInTile = j % ColWidth[tileIdx] == 0) ? 1 : 0 if ( ( tile_group_type ! = I ) && ( firstCtbInCtuRowInTile ) ) HMVPCandNum = 0 | 
CtbAddrInRs = CtbAddrTsToRs[ ctbAddrInTs ] | 
coding_tree_unit( ) | 
} | 
end_of_tile_one_bit /* equal to 1 */ | ae(v)
if( i < num_tiles_in_tile_group_minus1 ) | 
byte_alignment( ) | 
} | 
} | 

## Slide 4
Thank You
www.huawei.com

## Slide 5
Backup

## Slide 6: HMVP list reset for tile groups, tiles, CTU row beginning inside each tile
12 tiles and 3 tile groups
Tile 1
Tile 2
Tile Group1
Tile Group2
Tile Group3
Tile 3
Tile 4
Tile 5
Tile 6
Tile 8
Tile 7
Tile 9
Tile 10
Tile 11
Tile 12
Tile Group scan order (raster scan across tiles)
CTU scan order (inside tiles)
HMVP list reset is performed for all the combinations below:
At the beginning of each tile group (equivalent of beginning of slice)
At the beginning of each tile inside a tile group
At the first CTU for each CTU row inside a give tile
HMVP
list reset
HMVP list reset