## Slide 1: JVET-M0307 CE4-related : Candidates optimization on MMVD
N. Park, H. Jang, J. Nam, J. Lim, S. Kim

## Slide 2: Introduction
MMVD was adopted in previous meeting
New motion vector expressions was introduced
  starting point (2), motion distance (8), motion direction (4) : Overall number of candidates is 64
MmvdOffset[ x0 ][ y0 ][ 0 ] = ( MmvdDistance[ x0 ][ y0 ] << 2 ) * MmvdSign[ x0 ][ y0 ][0]
MmvdOffset[ x0 ][ y0 ][ 1 ] = ( MmvdDistance[ x0 ][ y0 ] << 2 ) * MmvdSign[ x0 ][ y0 ][1]
mmvd_distance_idx [ x0 ][ y0 ] | MmvdDistance [ x0 ][ y0 ]
0 | 1
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
mmvd_direction_idx [ x0 ][ y0 ] | MmvdSign [ x0 ][ y0 ][0] | MmvdSign [ x0 ][ y0 ][1]
0 | +1 | 0
1 | -1 | 0
2 | 0 | +1
3 | 0 | -1
< motion distance >
< motion direction >

## Slide 3: Proposed methods
In this proposal, instead of 8 motion distance indices, 4 motion distance indices are used
  Overall number of candidates is reduced to 32.
mmvd_distance_idx[ x0 ][ y0 ] | MmvdDistance[ x0 ][ y0 ] | 
 | VTM3.0 | Proposed
0 | 1 | 1
1 | 2 | 2
2 | 4 | 4
3 | 8 | 8
4 | 16 | -
5 | 32 | -
6 | 64 | -
7 | 128 | -
removed

## Slide 4: Proposed methods
Indicated motion distance is further adjusted considering
  Test #1 : the magnitude of the base motion vector and block size
  Test #2 : mv resolution of the base motion vector
if (MV ≥ 128 && W > 32 && H > 32 ) distance = MmvdDistance[ x0 ][ y0 ] << 2; else if (MV ≥ 16) distance = MmvdDistance[ x0 ][ y0 ] << 1; else distance = MmvdDistance[ x0 ][ y0 ];
if ((MV % 32) == 0) distance = MmvdDistance[ x0 ][ y0 ] << 2; else if ((MV % 16) == 0) distance = MmvdDistance[ x0 ][ y0 ] << 1; else distance = MmvdDistance[ x0 ][ y0 ] ;
MmvdOffset[ x0 ][ y0 ][ 0 ] = ( distance << 2 ) * MmvdSign[ x0 ][ y0 ][0]
MmvdOffset[ x0 ][ y0 ][ 1 ] = ( distance << 2 ) * MmvdSign[ x0 ][ y0 ][1]

## Slide 5: Experimental results
Test #1 : the magnitude of the base motion vector and block size
Test #2 : mv resolution of the base motion vector

## Slide 6: Experimental results
Simulation results of the CE4.4.4a + Test #1
Simulation results of the CE4.4.4a + Test #2
CE4.4.4a) RA : -0.13% -0.07% -0.08% 106% 100%
LB : -0.05% 0.03% 0.00% 104% 100%

## Slide 7: Conclusion
In this proposal, instead of 8 motion distance indices, 4 motion distance indices are used
  Overall number of candidates is reduced to 32.
Indicated motion distance is further adjusted considering
  Test #1 : the magnitude of the base motion vector and block size
  Test #2 : mv resolution of the base motion vector
Simulation results show the coding gain with reduced complexity
Also, proposed schemes are tested with CE4.4.4a (extended direction to 8).
Simulation results show the coding gain without noticeable increment of complexity
Recommended to consider this method for next VTM.
Thanks to Kwai(JVET-M0621) and Sharp (JVET-M0779) for crosscheck

## Slide 8
Thank you