## Slide 1
JVET-M0310
CE2-related: Using shorter-tap filter for 4x4 sized partition
Jingya Li, Ru-Ling Liao Chong Soon Lim

## Slide 2: Introduction
6-tap interpolation filter is used for 4×4 sized block including
  4×4 CU
  4×4 affine sub-block
Memory bandwidth and number of operations are reduced
0.08% loss in RA, 0.14% loss in LB

## Slide 3: Memory bandwidth reduction
Number of samples to be fetched is reduced to 67%
filter tap | # of samples to be fetched for a 4×4 block | Ratio to 8 tap filter
8 | 121 | -
6 | 81 | 67%
CU size (W×H) | Number of luma samples to be fetched per luma sample (W + N) × (H + N) / (W × H)
8×8 Bi-prediction 8 tap | 7.03
4×4 uni-prediction 8 tap | 7.56
4×4 Uni-prediction 6 tap | 5.06

## Slide 4: Number of operations reduction
Number of multiplications is reduced from 130% to 85% compared with 8x8 bi-pred MC.
Number of additions is reduced from 130% to 81% compared with 8x8 bi-pred MC.

## Slide 5: Simulation results
Random Access | 6-tap interpolation filter |  |  |  | 
Main 10 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.05% | -0.04% | 100% | 100%
Class A2 | 0.09% | 0.09% | 0.20% | 100% | 98%
Class B | 0.05% | 0.08% | -0.10% | 100% | 99%
Class C | 0.16% | 0.10% | 0.09% | 100% | 100%
Overall | 0.08% | 0.06% | 0.02% | 100% | 99%
Class D | 0.25% | 0.15% | 0.38% | 100% | 100%
Class F | 0.05% | -0.04% | 0.03% | 100% | 101%
Low delay B | 6-tap interpolation filter |  |  |  | 
Main 10 | Y | U | V | EncT | DecT
Class B | 0.09% | -0.08% | 0.17% | 100% | 101%
Class C | 0.22% | 0.45% | 0.35% | 100% | 101%
Class E | 0.09% | 0.17% | 0.50% | 100% | 101%
Overall | 0.14% | 0.16% | 0.31% | 100% | 101%
Class D | 0.42% | 0.48% | 0.46% | 100% | 101%
Class F | 0.19% | 0.02% | -0.17% | 100% | 101%

## Slide 6: Conclusions
6-tap interpolation is proposed for 4×4 block to reduce
  memory bandwidth
  number of multiplications and additions
0.08% loss in RA, 0.14% loss in LB
It is suggested to adopt this proposal to VVC

## Slide 7: Acknowledgments
Thank MediaTek for cross-checking

## Slide 8: 6-tap interpolation filter
MV | 6-tap interpolation filter |  |  |  |  | 
0 | 0 | 0 | 64 | 0 | 0 | 0
1/16 | 1 | -3 | 63 | 4 | -2 | 1
1/8 | 1 | -5 | 62 | 8 | -3 | 1
3/16 | 2 | -8 | 60 | 13 | -4 | 1
1/4 | 3 | -10 | 58 | 17 | -5 | 1
5/16 | 3 | -11 | 52 | 26 | -8 | 2
3/8 | 2 | -9 | 47 | 31 | -10 | 3
7/16 | 3 | -11 | 45 | 34 | -10 | 3
1/2 | 3 | -11 | 40 | 40 | -11 | 3
9/16 | 3 | -10 | 34 | 45 | -11 | 3
5/8 | 3 | -10 | 31 | 47 | -9 | 2
11/16 | 2 | -8 | 26 | 52 | -11 | 3
6/8 | 1 | -5 | 17 | 58 | -10 | 3
13/16 | 1 | -4 | 13 | 60 | -8 | 2
7/8 | 1 | -3 | 8 | 62 | -5 | 1
15/16 | 1 | -2 | 4 | 63 | -3 | 1

## Slide 9: 4-tap interpolation filter
Number of samples to be fetched is reduced to 40%
Number of multiplications is reduced to 37%
Number of additions is reduced to 31%
filter tap | # of samples to be fetched for a 4×4 block | Ratio to 8 tap filter
8 | 121 | -
6 | 81 | 67%
4 | 49 | 40%

## Slide 10: 4-tap interpolation filter
MV | 4-tap interpolation filter |  |  | 
0 | 0 | 64 | 0 | 0
1/16 | -2 | 62 | 4 | 0
1/8 | -2 | 58 | 10 | -2
3/16 | -4 | 56 | 14 | -2
1/4 | -4 | 54 | 16 | -2
5/16 | -6 | 52 | 20 | -2
3/8 | -6 | 46 | 28 | -4
7/16 | -4 | 42 | 30 | -4
1/2 | -4 | 36 | 36 | -4
9/16 | -4 | 30 | 42 | -4
5/8 | -4 | 28 | 46 | -6
11/16 | -2 | 20 | 52 | -6
6/8 | -2 | 16 | 54 | -4
13/16 | -2 | 14 | 56 | -4
7/8 | -2 | 10 | 58 | -2
15/16 | 0 | 4 | 62 | -2

## Slide 11: Simulation results
Random Access | 4-tap interpolation filter |  |  |  | 
Main 10 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.13% | -0.10% | 100% | 100%
Class A2 | 0.30% | 0.06% | 0.08% | 100% | 98%
Class B | 0.35% | 0.16% | 0.02% | 100% | 99%
Class C | 0.65% | 0.33% | 0.29% | 100% | 99%
Overall | 0.35% | 0.13% | 0.08% | 100% | 99%
Class D | 1.27% | 0.68% | 0.91% | 100% | 98%
Class F | 0.12% | 0.08% | 0.15% | 100% | 101%
Low delay B | 4-tap interpolation filter |  |  |  | 
Main 10 | Y | U | V | EncT | DecT
Class B | 0.65% | -0.04% | 0.33% | 100% | 99%
Class C | 0.90% | 0.71% | 0.56% | 100% | 98%
Class E | 0.73% | 0.45% | -0.05% | 100% | 100%
Overall | 0.75% | 0.33% | 0.31% | 100% | 99%
Class D | 2.48% | 1.24% | 1.46% | 99% | 98%
Class F | 0.51% | 0.42% | 0.24% | 100% | 100%