## Slide 1: Non-CE11: Considering boundary strength on CPR coded block (JVET-M0336)
Hyeongmun Jang (hm.jang@lge.com)

## Slide 2: Summary
Suggest boundary strength decision for CPR coded block boundary
  Method 1.
    Boundary strength is set as 0 when at least one of block is coded as CPR across the block boundary.
  Method 2.
    Boundary strength is set as 0 when both block are coded as CPR and is set as 1 when only one block is coded as CPR across the block boundary
Provide visual quality improvement on computer generated video sequence where CPR mode occurs frequently.

## Slide 3: Proposed method
Method 1
  Boundary strength is set as 0 when at least one of block is coded as CPR across the block boundary.
P is CPR || Q is CPR
BS set equal 0
P is INTRA || Q is INTRA
BS set equal 1
BS set equal 2
Same refer. idx && mv difference < THR
y
n

## Slide 4: Proposed method
Method 2
  Boundary strength is set as 0 when both block are coded as CPR and is set as 1 when only one block is coded as CPR across the block boundary
P is CPR || Q is CPR
BS set equal 0
P is INTRA || Q is INTRA
BS set equal 1
BS set equal 2
Same refer. idx && mv difference < THR
y
n
Both P and Q is CPR
y
n

## Slide 5: Subjective quality(Method 1)
Figure 1. Anchor FlyingGraphics QP37 1st frame
Figure 2. Proposed FlyingGraphics QP37 1st frame

## Slide 6: Experimental results
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.10% | 0.06% | 126% | 100% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class A2 | -0.47% | -0.50% | -0.54% | 128% | 100% | 0.00% | 0.01% | 0.01% | 100% | 100%
Class B | -0.29% | -0.39% | -0.36% | 135% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | -0.08% | -0.24% | -0.25% | 139% | 101% | 0.01% | 0.00% | 0.00% | 100% | 100%
Class E | -0.61% | -0.81% | -0.60% | 139% | 100% | 0.03% | 0.00% | 0.00% | 100% | 100%
Overall | -0.27% | -0.40% | -0.33% | 134% | 100% | 0.01% | 0.00% | 0.00% | 100% | 100%
Class D | -0.10% | -0.23% | 0.22% | 136% | 101% | 0.00% | 0.00% | 0.01% | 100% | 100%
Class F (optional) | -12.05% | -12.04% | -12.09% | 154% | 98% | 0.05% | 0.00% | 0.00% | 100% | 99%
Class SCC 1080p | -36.89% | -36.11% | -36.36% | 109% | 80% | 0.03% | 0.00% | 0.00% | 100% | 99%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.13% | -0.01% | 0.24% | 99% | 100% | -0.01% | 0.03% | 0.01% | 100% | 100%
Class A2 | 0.01% | 0.12% | 0.22% | 97% | 100% | 0.01% | 0.05% | -0.02% | 100% | 100%
Class B | 0.02% | 0.00% | -0.24% | 99% | 100% | 0.00% | 0.00% | -0.04% | 100% | 100%
Class C | 0.19% | -0.08% | 0.16% | 102% | 100% | 0.00% | -0.02% | 0.08% | 100% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.08% | 0.00% | 0.05% | 99% | 100% | 0.00% | 0.01% | 0.01% | 100% | 100%
Class D | 0.21% | -0.33% | 0.12% | 102% | 99% | 0.06% | -0.05% | -0.04% | 100% | 100%
Class F (optional) | -9.87% | -10.00% | -10.00% | 107% | 99% | 0.02% | -0.09% | -0.05% | 100% | 99%
Class SCC 1080p | -22.02% | -21.69% | -22.27% | 103% | 95% | 0.00% | -0.14% | -0.19% | 100% | 99%
Method 1

## Slide 7: Experimental results
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.10% | 0.06% | 126% | 100% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class A2 | -0.47% | -0.50% | -0.54% | 128% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class B | -0.29% | -0.39% | -0.35% | 135% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | -0.09% | -0.25% | -0.25% | 139% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E | -0.63% | -0.81% | -0.59% | 139% | 101% | 0.01% | 0.00% | 0.00% | 99% | 100%
Overall | -0.27% | -0.40% | -0.33% | 134% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | -0.10% | -0.23% | 0.21% | 136% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F (optional) | -12.08% | -12.04% | -12.10% | 154% | 97% | 0.01% | 0.00% | 0.00% | 100% | 99%
Class SCC 1080p | -36.91% | -36.11% | -36.36% | 109% | 80% | 0.01% | 0.00% | 0.00% | 100% | 99%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.14% | -0.03% | 0.23% | 99% | 100% | 0.00% | 0.01% | 0.00% | 100% | 100%
Class A2 | 0.01% | 0.03% | 0.22% | 97% | 100% | 0.01% | -0.04% | -0.02% | 100% | 100%
Class B | 0.02% | -0.05% | -0.24% | 98% | 99% | 0.00% | -0.05% | -0.03% | 100% | 100%
Class C | 0.17% | -0.02% | 0.19% | 102% | 99% | -0.02% | 0.04% | 0.10% | 100% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.08% | -0.02% | 0.06% | 99% | 99% | 0.00% | -0.01% | 0.01% | 100% | 100%
Class D | 0.20% | -0.16% | 0.22% | 102% | 99% | 0.05% | 0.12% | 0.06% | 100% | 100%
Class F (optional) | -9.90% | -9.90% | -9.98% | 107% | 99% | -0.01% | 0.02% | -0.03% | 100% | 99%
Class SCC 1080p | -22.08% | -21.77% | -22.32% | 103% | 96% | -0.06% | -0.22% | -0.25% | 100% | 99%
Method 2