## Slide 1: JVET-M0467 CE2-related: Symmetric MVD for Affine Bi-prediction Coding
Jiancong Luo, Yuwen He
InterDigital Inc.
January, 2019

## Slide 2: Introduction
Symmetric MVD mode in CE4.4.3 (JVET-M0481)
  ref_l0_dx and ref_l1_idx are not signaled but derived
  MvdL0 is signaled, MvdL1 is not signaled.
  MV calculation

## Slide 3: Propose Symmetric MVD for Affine Bi-prediction
Extend symmetric MVD to affine
TL MVD in list-1 is derived from list-0, TR and BL MVD in list-1 is set to 0.
For the TL CPMV:
  For TR and BL CPMV:

## Slide 4: Experimental results
4
© 2018 InterDigital, Inc. All Rights Reserved.
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | -0.11% | -0.10% | 107% | 100%
Class A2 | -0.24% | -0.15% | -0.14% | 109% | 100%
Class B | -0.14% | -0.05% | -0.11% | 106% | 99%
Class C | -0.05% | -0.04% | 0.00% | 104% | 100%
Class E |  |  |  |  | 
Overall | -0.13% | -0.08% | -0.08% | 106% | 100%
Class D | -0.05% | -0.07% | 0.05% | 104% | 100%
Class F (optional) | -0.17% | -0.17% | -0.12% | 105% | 101%
Table 1: Compare to VTM-3.0

## Slide 5: Experimental results
5
© 2018 InterDigital, Inc. All Rights Reserved.
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.45% | -0.52% | -0.55% | 113% | 99%
Class A2 | -0.60% | -0.55% | -0.49% | 114% | 99%
Class B | -0.41% | -0.38% | -0.37% | 112% | 98%
Class C | -0.26% | -0.30% | -0.35% | 109% | 99%
Class E |  |  |  |  | 
Overall | -0.42% | -0.42% | -0.42% | 112% | 99%
Class D | -0.21% | -0.38% | -0.16% | 108% | 99%
Class F (optional) | -0.39% | -0.34% | -0.31% | 110% | 101%
Table 2: Combine with M0444

## Slide 6: Summary
Proposal extends symmetric MVD from regular AMVP to affine AMVP
Performance
  -0.13% for RA
  -0.42% for RA when combine with CE4.4.3
Propose to study in CE
Thank Qualcomm for cross-checking (JVET-M0795)