## Slide 1: CE10-related: Simplified multi-hypothesis intra-inter mode (JVET-M0492)
L. Zhao, X. Zhao, X. Li , S. Liu ( Tencent )
2019/01

## Slide 2: Introduction
In VTM 3.0, multi-hypothesis intra-inter prediction combines intra prediction and merge indexed inter prediction
  For luma component, the intra candidate mode list includes 4 intra prediction modes
In addition to get the inter prediction sample values, intra-inter prediction process in VTM 3.0 includes the following 5 steps.
  Reference sample availability check and substitution
  Reference sample filtering
  Planar prediction
  PDPC
  Weighted average of intra prediction and inter prediction. (one extra buffer is added to store the intra prediction values)

## Slide 3: Proposed method
Firstly, reduce the size of intra candidate list from 4 to 1, and extra signaling of intra mode candidate is avoided
Secondly, PDPC filter is directly applied to the inter prediction samples to get the final prediction values, and steps (2), (3) and (5) are avoided. No extra buffer is needed
  Alternatively, equation (3) can be replaced by equation (4)

## Slide 4: Complexity analysis
The complexity comparison for different block sizes among the proposed method (equation (4) is used) and VTM3.0 (when planar mode is selected for intra-inter mode) in terms of operation counts is given by the following table.
  It should be noted that most of the multiplication operations in VTM3.0 is from Planar prediction.
Block size | Proposed method |  |  | VTM3.0 |  | 
 | multiplication | add | shift | multiplication | add | shift
8x8 | 0 | 480 | 480 | 384 | 896 | 640
16x16 | 0 | 1920 | 1920 | 1536 | 3520 | 2496
32x32 | 0 | 4992 | 4992 | 6144 | 11264 | 7134
64x64 | 0 | 19968 | 19968 | 24576 | 44800 | 28416

## Slide 5: Simulation Results
Anchor: VTM3.0
Test 1: equation (3) is used
 | Random Access Main10 |  |  |  |  | Low Delay B Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.22% | -0.01% | 98% | 96% |  |  |  |  | 
Class A2 | 0.04% | 0.02% | 0.21% | 97% | 97% |  |  |  |  | 
Class B | 0.05% | -0.03% | -0.05% | 99% | 97% | -0.08% | -0.19% | -0.10% | 99% | 97%
Class C | 0.08% | 0.06% | 0.15% | 100% | 100% | -0.02% | 0.09% | 0.06% | 98% | 98%
Class E |  |  |  |  |  | -0.05% | 0.09% | -0.55% | 99% | 98%
Overall | 0.05% | -0.04% | 0.06% | 99% | 98% | -0.05% | -0.03% | -0.16% | 99% | 98%
Class D | 0.03% | -0.13% | 0.04% | 100% | 102% | -0.08% | -0.15% | 0.08% | 100% | 100%
Class F | 0.00% | -0.07% | 0.00% | 101% | 100% | 0.01% | -0.51% | -0.22% | 99% | 98%

## Slide 6: Simulation Results
Anchor: VTM3.0
Test 2: equation (4) is used
 | Random Access Main10 |  |  |  |  | Low Delay B Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.15% | -0.08% | 100% | 101% |  |  |  |  | 
Class A2 | 0.04% | 0.16% | 0.22% | 99% | 100% |  |  |  |  | 
Class B | 0.08% | 0.12% | -0.02% | 99% | 97% | -0.06% | -0.22% | 0.07% | 101% | 103%
Class C | 0.04% | 0.01% | 0.13% | 100% | 101% | -0.04% | -0.11% | 0.16% | 99% | 93%
Class E |  |  |  |  |  | -0.01% | 0.17% | -0.72% | 100% | 94%
Overall | 0.05% | 0.04% | 0.05% | 99% | 99% | -0.04% | -0.09% | -0.10% | 100% | 97%
Class D | 0.00% | 0.04% | -0.02% | 99% | 98% | -0.08% | -0.37% | -0.34% | 100% | 100%
Class F | 0.02% | -0.05% | 0.01% | 99% | 100% | 0.23% | 0.27% | 0.22% | 98% | 99%

## Slide 7: Conclusion
The size of intra candidate list of intra-inter mode is reduced from 4 to 1 such that extra signaling of intra mode candidate is avoided
Intra prediction stage is not avoided in intra-inter prediction mode, and PDPC filter is directly applied to the inter prediction samples to get the final prediction values.
It is proposed to further study this proposal in CE