## Slide 1: CE3-related: Modifications on MPM list generation (JVET-M0494)
L. Zhao, X. Zhao, X. Li , S. Liu ( Tencent )
2019/01

## Slide 2: Problem Statement
Problem #1:
  MPM derivation is different between zero and non-zero line, which is defined using 3 pages’ spec text
    Line 0: 6 MPMs including Planar, DC and 4 Angular modes
    Other lines: 6 Angular modes
Problem #2:
  For zero line, when the two neighboring modes have only one angular mode, left mode is always first MPM which may not be Planar

## Slide 3: Problem Statement
Problem #3:
  MPM derivation for non-zero line has several branches in order to derive 6 different angular MPMs
  If maxAB − minAB is equal to 1, the following applies:
candModeList[ 2 ] = 2 + ( ( minAB + 61 ) % 64 ) (8‑26)
candModeList[ 3 ] = 2 + ( ( maxAB − 1 ) % 64 ) (8‑27)
candModeList[ 4 ] = 2 + ( ( minAB + 60 ) % 64 ) (8‑28)
candModeList[ 5 ] = 2 + ( maxAB % 64 ) (8‑29)
  Otherwise if maxAB − minAB is equal to 2, the following applies:
candModeList[ 2 ] = 2 + ( ( minAB − 1 ) % 64 ) (8‑30)
candModeList[ 3 ] = 2 + ( ( minAB + 61 ) % 64 ) (8‑31)
candModeList[ 4 ] = 2 + ( ( maxAB − 1 ) % 64 ) (8‑32)
candModeList[ 5 ] = 2 + ( ( minAB + 60 ) % 64 ) (8‑33)
  Otherwise if maxAB − minAB is greater than 61, the following applies:
candModeList[ 2 ] = 2 + ( ( minAB − 1 ) % 64 ) (8‑34)
candModeList[ 3 ] = 2 + ( ( maxAB + 61 ) % 64 ) (8‑35)
candModeList[ 4 ] = 2 + ( minAB % 64 ) (8‑36)
candModeList[ 5 ] = 2 + ( ( maxAB + 60 ) % 64 ) (8‑37)
  Otherwise, the following applies:
candModeList[ 2 ] = 2 + ( ( candIntraPredModeA minAB + 61 ) % 64 ) (8‑38)
candModeList[ 3 ] = 2 + ( ( candIntraPredModeA minAB − 1 ) % 64 ) (8‑39)
candModeList[ 4 ] = 2 + ( ( candIntraPredModeB maxAB + 61 ) % 64 ) (8‑40)
candModeList[ 5 ] = 2 + ( ( candIntraPredModeB maxAB − 1 ) % 64 ) (8‑41)

## Slide 4: Proposed method
Method #1 (simplification for non-zero lines)
  For non-zero lines, if left and above modes are different angular modes, MPM list is derived using only one method instead of 4 different methods
    candModeList[ 0 ] = leftIntraDir
    candModeList[ 1 ] = aboveIntraDir
    candModeList[ 2 ] = 2 + ( ( leftIntraDir + 61 ) % 64 )
    candModeList[ 3 ] = 2 + ( ( leftIntraDir − 1 ) % 64 )
    candModeList[ 4 ] = 2 + ( ( aboveIntraDir + 61 ) % 64 )
    candModeList[ 5 ] = 2 + ( (aboveIntraDir − 1) % 64 )

## Slide 5: Proposed method
Method #2 (prioritize Planar mode for zero line)
  For zero line, if only one of the two neighboring modes is Angular mode, Planar mode is put as first MPM
    candModeList[ 0 ] = PLANAR_IDX
    candModeList[ 1 ] = maxAB
    candModeList[ 2 ] = DC_IDX
    candModeList[ 3 ] = 2 + ( ( maxAB + 61 ) % 64 )
    candModeList[ 4 ] = 2 + ( ( maxAB − 1 ) % 64 )
    candModeList[ 5 ] = 2 + ( ( maxAB + 60 ) % 64 )

## Slide 6: Proposed method
Method #3 (Alternative improvement for zero line)
  On top of Method #2, if the neighboring angular mode is vertical or horizontal mode, angular mode is first MPM. Otherwise, Planar mode is first MPM
    candModeList[ 0 ] = (maxAB == VER_IDX || maxAB == HOR_IDX) ? maxAB: PLANAR_IDX
    candModeList[ 1 ] = (maxAB == VER_IDX || maxAB == HOR_IDX) ? PLANAR_IDX: maxAB
    candModeList[ 2 ] = DC_IDX
    candModeList[ 3 ] = 2 + ((maxAB + offset) % mod)
    candModeList[ 4 ] = 2 + (( maxAB − 1 ) % mod )
    candModeList[ 5 ] = 2 + ((maxAB + offset - 1) % mod)

## Slide 7: Proposed method
Method #4 (Unification for zero and non-zero lines)
  Only one MPM list generation method is used, which is the zero-line MPM list generated in VTM3.0
  For non-zero line, only the 4 angular MPMs may apply

## Slide 8: Proposed method
Method #5 (Unification for zero and non-zero lines)
  On top of Method #4, Planar and DC modes are always the first two MPMs
  The first two bins of MPM index is context coded
  Only 4 angular MPMs need to be derived instead of 6 in VTM-3.0

## Slide 9: Simulation Results
Anchor: VTM3.0
Test 1: Method #1 (Simplification for non-zero lines)
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.03% | 0.04% | 98% | 94% | 0.01% | 0.06% | 0.05% | 100% | 99%
Class A2 | 0.01% | 0.09% | -0.03% | 98% | 96% | -0.03% | -0.03% | 0.12% | 99% | 98%
Class B | 0.01% | -0.02% | 0.00% | 99% | 97% | -0.01% | -0.01% | 0.06% | 100% | 100%
Class C | 0.02% | -0.03% | -0.06% | 100% | 101% | 0.00% | -0.07% | 0.14% | 101% | 104%
Class E | 0.03% | 0.03% | -0.04% | 100% | 99% |  |  |  |  | 
Overall | 0.02% | 0.00% | -0.02% | 99% | 97% | -0.01% | -0.02% | 0.09% | 100% | 100%
Class D | 0.01% | 0.04% | 0.03% | 99% | 101% | -0.01% | -0.30% | -0.03% | 101% | 103%
Class F | 0.04% | -0.01% | 0.09% | 99% | 101% | 0.00% | -0.05% | 0.10% | 100% | 101%

## Slide 10: Simulation Results
Anchor: VTM3.0
Test 2: Method #2 (Prioritize Planar mode for zero line)
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.14% | -0.14% | -0.01% | 100% | 96% | -0.04% | 0.11% | 0.03% | 99% | 98%
Class A2 | -0.05% | -0.05% | -0.04% | 98% | 96% | -0.04% | 0.07% | 0.09% | 100% | 99%
Class B | -0.05% | -0.02% | 0.04% | 100% | 98% | -0.03% | 0.13% | -0.24% | 101% | 100%
Class C | -0.02% | -0.02% | -0.03% | 102% | 104% | 0.00% | -0.07% | 0.14% | 102% | 104%
Class E | -0.07% | -0.08% | 0.02% | 101% | 100% |  |  |  |  | 
Overall | -0.06% | -0.06% | 0.00% | 100% | 99% | -0.03% | 0.06% | -0.02% | 100% | 100%
Class D | -0.05% | -0.10% | 0.04% | 101% | 106% | -0.05% | -0.29% | -0.13% | 101% | 103%
Class F | 0.15% | 0.07% | 0.21% | 100% | 102% | 0.11% | 0.21% | 0.14% | 101% | 103%

## Slide 11: Simulation Results
Anchor: VTM3.0
Test 3: Method #3 (Alternative improvement for zero line)
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.11% | -0.17% | -0.06% | 98% | 94% | -0.02% | 0.05% | -0.03% | 99% | 98%
Class A2 | -0.04% | -0.01% | -0.03% | 98% | 95% | -0.01% | 0.08% | 0.22% | 99% | 98%
Class B | -0.04% | -0.05% | 0.01% | 100% | 97% | -0.02% | 0.01% | -0.02% | 100% | 99%
Class C | -0.02% | 0.00% | -0.03% | 100% | 101% | 0.00% | 0.11% | 0.10% | 101% | 104%
Class E | -0.07% | -0.12% | -0.09% | 100% | 99% |  |  |  |  | 
Overall | -0.05% | -0.06% | -0.03% | 99% | 97% | -0.01% | 0.06% | 0.06% | 100% | 100%
Class D | -0.03% | -0.08% | -0.07% | 102% | 105% | -0.04% | -0.21% | -0.10% | 101% | 106%
Class F | 0.01% | 0.01% | 0.03% | 99% | 100% | -0.03% | -0.01% | 0.22% | 101% | 102%

## Slide 12: Simulation Results
Anchor: VTM3.0
Test 4: Method #4 (Unification for zero and non-zero lines)
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.03% | -0.01% | 98% | 94% | 0.02% | -0.04% | 0.03% | 99% | 99%
Class A2 | 0.04% | 0.05% | 0.01% | 98% | 97% | 0.02% | 0.12% | 0.13% | 99% | 99%
Class B | 0.04% | 0.03% | 0.04% | 100% | 96% | 0.03% | 0.14% | -0.10% | 101% | 98%
Class C | 0.08% | -0.03% | -0.12% | 100% | 101% | 0.03% | 0.04% | 0.00% | 102% | 105%
Class E | 0.06% | 0.03% | 0.15% | 101% | 99% |  |  |  |  | 
Overall | 0.05% | 0.01% | 0.01% | 99% | 97% | 0.03% | 0.07% | 0.00% | 100% | 100%
Class D | 0.03% | -0.06% | -0.02% | 100% | 103% | -0.01% | -0.20% | -0.03% | 102% | 107%
Class F | 0.06% | 0.08% | 0.06% | 100% | 101% | 0.02% | -0.05% | 0.03% | 101% | 103%

## Slide 13: Simulation Results
Anchor: VTM3.0
Test 5: Method #5 (Unification for zero and non-zero lines)
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.30% | -0.37% | -0.19% | 99% | 99% | -0.09% | -0.05% | -0.02% | 96% | 97%
Class A2 | 0.00% | 0.02% | 0.01% | 99% | 98% | 0.01% | 0.21% | 0.16% | 97% | 99%
Class B | -0.04% | 0.02% | 0.00% | 101% | 101% | -0.02% | 0.14% | 0.04% | 96% | 100%
Class C | 0.08% | 0.10% | 0.09% | 101% | 102% | 0.04% | -0.09% | -0.04% | 97% | 101%
Class E | 0.05% | 0.06% | 0.26% | 100% | 101% |  |  |  |  | 
Overall | -0.04% | -0.02% | 0.03% | 100% | 100% | -0.01% | 0.05% | 0.03% | 96% | 99%
Class D | 0.02% | -0.09% | 0.08% | 101% | 101% | -0.01% | -0.22% | -0.12% | 97% | 100%
Class F | 0.39% | 0.31% | 0.48% | 101% | 102% | 0.19% | 0.18% | 0.34% | 96% | 100%

## Slide 14: Simulation Results
Anchor: VTM3.0
Test 6: Method #1 + Method #2
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.13% | -0.09% | 0.00% | 98% | 94% | -0.04% | -0.13% | 0.06% | 97% | 97%
Class A2 | -0.05% | -0.02% | -0.06% | 98% | 95% | -0.04% | 0.16% | 0.08% | 98% | 97%
Class B | -0.04% | -0.02% | -0.05% | 99% | 97% | -0.02% | 0.06% | 0.07% | 97% | 98%
Class C | 0.00% | -0.02% | -0.05% | 99% | 99% | 0.04% | -0.03% | 0.00% | 98% | 99%
Class E | -0.07% | -0.08% | 0.07% | 99% | 96% |  |  |  |  | 
Overall | -0.05% | -0.04% | -0.02% | 99% | 96% | -0.01% | 0.02% | 0.05% | 97% | 98%
Class D | -0.02% | 0.02% | -0.02% | 99% | 99% | -0.07% | -0.09% | -0.04% | 98% | 101%
Class F | 0.16% | 0.06% | 0.13% | 99% | 99% | 0.08% | 0.12% | 0.12% | 96% | 97%

## Slide 15: Simulation Results
Anchor: VTM3.0
Test 7: Method #1 + Method #3
 | All Intra Main10 |  |  |  |  | Random Access Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.10% | -0.16% | -0.06% | 102% | 96% | -0.02% | 0.06% | 0.11% | 96% | 96%
Class A2 | -0.03% | 0.00% | -0.02% | 98% | 95% | -0.02% | -0.01% | 0.20% | 97% | 96%
Class B | -0.03% | -0.02% | -0.04% | 99% | 95% | -0.02% | 0.21% | 0.03% | 97% | 97%
Class C | -0.01% | -0.01% | -0.06% | 99% | 100% | 0.04% | -0.11% | 0.11% | 97% | 98%
Class E | -0.06% | -0.09% | -0.06% | 99% | 96% |  |  |  |  | 
Overall | -0.04% | -0.05% | -0.05% | 99% | 96% | -0.01% | 0.05% | 0.10% | 97% | 97%
Class D | -0.01% | -0.04% | -0.11% | 99% | 96% | -0.04% | -0.09% | 0.22% | 97% | 96%
Class F | 0.02% | 0.02% | 0.03% | 98% | 98% | -0.01% | 0.06% | 0.07% | 96% | 96%

## Slide 16: Conclusion
Improvement on MPM list generation, 0.05% coding gain is achieved on top of VTM-3.0
Software and draft text is largely simplified
It is proposed to further study this proposal in CE