## Slide 1: JVET-M0547
Johannes Sauer
RWTH Aachen University

## Slide 2: Status of 360°video coding
Good performance of PHEC anchor
  Coding using cube based projection format, i.e. PHEC
  Loop filters disabled across discontinuous face boundaries
Seams still visible especially at high QPs
Tools addressing this:
  Loop filters using spherical neighbors, especially DBF
  Geometry padding

## Slide 3: 360°coding tools – Geometry padding

## Slide 4: 360°coding tools – Corrected loop filters
Loop filters should use spherical neighbors instead of actual neighbors

## Slide 5: 360°coding tools – Geometry padding – Picture level implementation / Out of loop
Separate additional reference pictures for each cube face
Applicable reference picture can be derived from the location of the block
6 reference pictures
One per cube face

## Slide 6: 360°coding tools – Geometry padding – Implementation discussion
Specification:
  Picture level specification only requires modification of reference picture buffer and high-level syntax changes
  Coding block level specification requires normative tools in the coding loop
Implementation | Pro | Contra
Picture level | High level Easy to integrate | High memory requirement If not all computed pixels are used, unnecessary computational complexity
Coding block level | Low memory requirement For decoder, only required pixels are computed | More difficult to integrate For encoder it is likely that pixels are computed several times, unnecessary high computational complexity

## Slide 7: Uncoded areas for 360°tools
Premise: Code each face with a least one tile
Include padding area for all faces in the reference picture
Green: Coded cube faces
White: Uncoded areas

## Slide 8: Uncoded areas using empty tiles
Based on agreed starting point for tiles L0686
Allow „empty“ tiles, which do not hold any CTUs
Tile rows
Green: Coded cube faces White: Empty tiles

## Slide 9: Syntax change
Based on JVET-L0686
dep_quant_enabled_flag
if( !dep_quant_enabled_flag )
sign_data_hiding_enabled_flag
if( num_tiles_in_tile_group_minus1 > 0 ) {
offset_len_minus1
for( i = 0; i < num_tiles_in_tile_group_minus1; i++ )
tile_coded_flag
if( tile_coded_flag ) {
entry_point_offset_minus1[ i ]
}
}
byte_alignment( )
}

## Slide 10: Discussion of empty tiles for 360
Advantages
  All operations can be done / specified at buffer level
    Geometry padding: Uncoded areas are filled with generated geometry padding samples
      Already padded regions of reference pictures can be reused when referenced again
    Modified loop filters: Uncoded areas are filled with spherical neighbors
      Requires symmetric loop filters
      Generated once, compared to 3 times (DBF, SAO, ALF)
  No arbitrary buffer access at CTU level
    On the fly implementations need to use pixels from up to 3 different locations in the picture (cube corner)
Disadvantages
  Generation of not required samples
    Probably not an issue for loop filters, since just copy
    Problem for rather complex geometry padding
      Possible solution via SEI message signaling required padding amount

## Slide 11: Other applications
Additional reference pictures
  Encoder needs to code different motion vector
Multi layer coding
Scalable coding
Issues:
  Dependencies of tiles on other tiles
Reference picture
Additional reference (empty tile)
Base layer
Upsampled base layer (empty tile)
Enhancement layer
Unused

## Slide 12: Specification of 360°tools
Operation for enabling 360°tools do not require changes at CTU level
  Specification separate from VTM possible, for example ISO/IEC 23090-2 Information technology -- Coded representation of immersive media -- Part 2: Omnidirectional media format
In VTM
  Empty tiles
    Modified tile group header
  Or other technology providing uncoded areas
  Cube face arrangement via SEI message
  SEI message specifying how to use the uncoded areas

## Slide 13: Specification of 360°tools – Geometry padding
Specifciation
  A integer sample location in the padded region is selected
  map to unit cube packing location
  projected to 3D cube location
  back projected to source unit cube packing location
    automatically moves the sample from the padding region inside another face
  Map to fractional sample location in the coded face arrangement
  Interpolation using the found source sample location
Missing
  Specification for chroma
  Interpolation filter
  Specification of loop filter correction (simpler than geometry padding)

## Slide 14: Implementation status
CE13.5.2b already uses a buffer based approach
  for geometry padding.
  for DBF and ALF
  SAO still needs to be adapted
No tiles in VTM yet
  empty tile idea could not implemented/tested yet

## Slide 15: Conclusion
Proposal to specify 360 coding tools at tile/buffer level
Keep specification separate from VTM (core) specification
Recommendation
  Allow empty tiles or other tool providing uncoded areas in VTM
  Further investigation of tile/buffer level approach in CE once tiles are in VTM

## Slide 16: 360°coding tools - Corrected deblocking filter (DBF)
Reference samples of blocks at face boundaries changed
  Original: Samples from top or left block are used
  Modified: Samples are chosen according to 3D cube geometry
Approach can be transferred to other coding formats