## Slide 1: CE4-related: Signaling MMVD syntax elements (JVET-N0126)
Mar., 2019
Seungsoo Jeong, Min Woo Park and Kiho Choi (Samsung)
JVET 14th Meeting

## Slide 2: Introduction
Current MMVD signals syntax element like followings:
  MMVD skip and merge flag are signaled right after skip and merge flag.
  Cu_cbf is not signaled, when MMVD is enabled.

## Slide 3: Proposed method
Proposed MMVD syntax elements
  Propose to disallow MMVD in skip modes.
  Instead of this, when MMVD merge mode is enabled, cu_cbf is signalled, whereas the normal merge mode does not signal cu_cbf and infers it as 1.
Table 3. Proposed merge data syntax
merge_data( x0, y0, cbWidth, cbHeight ) { | Descriptor
if ( CuPredMode[ x0 ][ y0 ] = = MODE_IBC ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if(cu_skip_flag[ x0 ][ y0 ] = = 0) | 
mmvd_flag[ x0 ][ y0 ] | ae(v)
if( mmvd_flag[ x0 ][ y0 ] = = 1 ) { | 
mmvd_merge_flag[ x0 ][ y0 ] | ae(v)
mmvd_distance_idx[ x0 ][ y0 ] | ae(v)
mmvd_direction_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if( MaxNumSubblockMergeCand > 0 && cbWidth >= 8 && cbHeight >= 8 ) | 
merge_subblock_flag[ x0 ][ y0 ] | ae(v)
if( merge_subblock_flag[ x0 ][ y0 ] = = 1 ) { | 

## Slide 4: Proposed method
Table 4. Proposed coding unit syntax
} | 
if( !pcm_flag[ x0 ][ y0 ] ) { | 
if( CuPredMode[ x0 ][ y0 ] != MODE_INTRA && merge_flag[ x0 ][ y0 ] = = 0 ¦¦ mmvd_flag[ x0 ][ y0 ] == 1 ) | 
cu_cbf | ae(v)
if( cu_cbf ) { | 
if( CuPredMode[ x0 ][ y0 ] = = MODE_INTER && sps_sbt_enabled_flag && !ciip_flag[ x0 ][ y0 ] ) { | 
if( cbWidth <= MaxSbtSize && cbHeight <= MaxSbtSize ) { | 
allowSbtVerH = cbWidth >= 8 | 
allowSbtVerQ = cbWidth >= 16 | 
allowSbtHorH = cbHeight >= 8 | 
allowSbtHorQ = cbHeight >= 16 | 
if( allowSbtVerH ¦ ¦ allowSbtHorH ¦ ¦ allowSbtVerQ ¦ ¦ allowSbtHorQ ) | 
cu_sbt_flag | ae(v)
} | 

## Slide 5: Result
RA | Y | U | V | Enc. | Dec. | LD | Y | U | V | Enc. | Dec.
Test 1 | -0.01% | -0.01% | 0.03% | 103% | 104% | Test 1 | -0.01% | 0.12% | -0.10% | 105% | 107%
Test 2 | -0.08% | 0.13% | 0.12% | 102% | 103% | Test 2 | -0.09% | 0.27% | 0.15% | 103% | 105%
Test 3 | -0.11% | -0.11% | -0.07% | 103% | 103% | Test 3 |  |  |  |  | 
Test 4 | -0.13% | -0.01% | 0.05% | 102% | 103% | Test 4 | -0.11% | 0.18% | 0.05% | 104% | 106%
Test result
- Test 1 : MMVD with cu_cbf
- Test 2 : MMVD with cu_cbf + CE4-3.4a
- Test 3 : CE4-3.1a + CE4-3.4a
- Test 4 : MMVD with cu_cbf + CE4-3.1a + CE4-3.4a

## Slide 6: Conclusion
Cu_cbf is signaled for disallowing MMVD in skip mode.
0.01% gain in RA / 0.01% gain in LDB
The adoption of this syntax change (Test 1) on VVC software is requested.
We thank LGE for cross-checking.

## Slide 7
Thank you

## Slide 8: Result
Test 1 : MMVD with cu_cbf

## Slide 9: Result
Test 2 : MMVD with cu_cbf + CE4-3.4a

## Slide 10: Result
Test 3 : CE4-3.1a + CE4-3.4a

## Slide 11: Result
Test 4 : MMVD with cu_cbf + CE4-3.1a + CE4-3.4a