## Slide 1: Non-CE4: Advanced Multi-hypothesis Inter Prediction for bandwidth reduction in B frame
2019/3/18
Yucheng Sun

## Slide 2
Outline
Proposed Method
Bandwidth Analysis
Experimental Results
Conclusion

## Slide 3: Proposed Method
Advance multi-hypothesis inter prediction (AMHP)
  For uni-prediction of AMVP mode
  Only one extra MV refer to the same reference frame
  Two modes
    Non-symmetric mode
    symmetric mode

## Slide 4: Proposed Method
Advance multi-hypothesis inter prediction (AMHP)
  MVD direction is determined by uni-prediction MV’s direction
MVD direction

## Slide 5: Proposed Method
Advance multi-hypothesis inter prediction (AMHP)
  MVD direction is determined by uni-prediction MV’s direction
MVD direction
MVD direction

## Slide 6: Proposed Method
Advance multi-hypothesis inter prediction (AMHP)
  MVD direction is determined by uni-prediction MV’s direction
MVD direction
MVD direction

## Slide 7: Proposed Method
Advance multi-hypothesis inter prediction (AMHP)
  MVD direction is determined by uni-prediction MV’s direction
  MVD value is determined by amhp_idx
amhp_idx | 0 | 1 | 2 | 3 | 4 | 5
AMHP mode | Non-sym mode |  |  |  | Sym mode | 
MVD value | 1/4-pel | 1/16-pel | 1/4-pel | 1/16-pel | 1/4-pel | 1/2-pel

## Slide 8: Proposed method
Be referenced by other mode
  AMVP mode:
    Regard AMHP as a uni-prediction block
    Use average MV for MVP list construction
  Other mode( Merge, HMVP, MMVD):
    Regard AMHP as a bi-predction block
    Use two AMHP MV for candidate list construction

## Slide 9: Bandwidth Analysis
Advance multi-hypothesis inter prediction (AMHP)
  Only in B frame
    AMHP get the prediction block from the same reference
    AMHP decrease the bandwidth cost.
      from 10.31 to 9
block size |  | bandwidth |  | 
width | height | uni-prediction | bi-prediction | AMHP
4 | 4 | 7.56 | - | 9
4 | 8 | 5.16 | Disable (10.31) | 6
8 | 4 | 5.16 | Disable (10.31) | 6
8 | 8 | 3.52 | 7.03 | -
4 | 16 | 3.95 | 7.91 | -
16 | 4 | 3.95 | 7.91 | -

## Slide 10: Experimental Results
 | Random access Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.10% | 0.09% | 100% | 101%
Class A2 | 0.06% | 0.19% | 0.25% | 101% | 99%
Class B | 0.04% | 0.09% | 0.17% | 101% | 101%
Class C | 0.13% | 0.11% | 0.14% | 101% | 103%
Class E |  |  |  |  | 
Overall | 0.06% | 0.12% | 0.16% | 101% | 101%
Class D | 0.18% | 0.27% | 0.18% | 101% | 105%
Class F | 0.05% | 0.13% | 0.07% | 101% | 103%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | -0.19% | -0.06% | 100% | 102%
Class C | 0.09% | 0.57% | 0.23% | 101% | 103%
Class E | 0.07% | 0.07% | -0.28% | 101% | 104%
Overall | 0.06% | 0.13% | -0.02% | 101% | 103%
Class D | 0.22% | 0.53% | 0.18% | 100% | 102%
Class F | 0.05% | 0.04% | -0.07% | 101% | 102%
Thank MediaTek for the cross-checking
 | Random access Main10 |  |  |  | 
 | Over VTM-4.0 4x8 8x4 bi off |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C |  |  |  |  | 
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D |  |  |  |  | 
Class F |  |  |  |  | 
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 4x8 8x4 bi off |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C |  |  |  |  | 
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D |  |  |  |  | 
Class F |  |  |  |  | 

## Slide 11: Conclusion
AMHP is a multi-hypothesis prediction for uni-prediction of AMVP mode.
  Same reference
  MV difference no more than 1 pixel
Bandwidth reduction from 10.31 to 9 (B frame)
  Disable bi-prediction: 8x4 4x8
  Enable AMHP : 4x4 8x4 4x8
Experimental results reportedly show
  0.06% 0.12% 0.16% Enc 101% Dec 101% compared to VTM-RA
  0.06% 0.13% -0.02% Enc 101% Dec 103% compared to VTM-LDB
Based on the above results, it is suggested to further study it in CE