## Slide 1: Non-CE4: Advanced Multi-hypothesis Inter Prediction
2019/3/19
Yucheng Sun

## Slide 2
Outline
Proposed method
Bandwidth analysis
Experimental Results
Conclusion

## Slide 3: Proposed method
Advance multi-hypothesis inter prediction (AMHP)
  For uni-prediction of AMVP mode
  Only one extra MV refer to the same reference frame
  Two modes
    Non-symmetric mode
    symmetric mode

## Slide 4: Proposed method
Advance multi-hypothesis inter prediction (AMHP)
  MVD direction is determined by uni-prediction MV’s direction
MVD direction

## Slide 5: Proposed method
Advance multi-hypothesis inter prediction (AMHP)
  MVD direction is determined by uni-prediction MV’s direction
MVD direction
MVD direction

## Slide 6: Proposed method
Advance multi-hypothesis inter prediction (AMHP)
  MVD direction is determined by uni-prediction MV’s direction
MVD direction
MVD direction

## Slide 7: Proposed method
Advance multi-hypothesis inter prediction (AMHP)
  MVD direction is determined by uni-prediction MV’s direction
  MVD value is determined by amhp_idx
amhp_idx | 0 | 1 | 2 | 3 | 4 | 5
AMHP mode | Non-sym mode |  |  |  | Sym mode | 
MVD value | 1/4-pel | 1/16-pel | 1/4-pel | 1/16-pel | 1/4-pel | 1/2-pel

## Slide 8: Proposed method
Be referenced by other mode
  AMVP mode:
    Regard AMHP as a uni-prediction block
    Use average MV for MVP list construction
  Other mode( Merge, HMVP, MMVD):
    Regard AMHP as a bi-predction block
    Use two AMHP MV for candidate list construction

## Slide 9: Bandwidth analysis
Advance multi-hypothesis inter prediction (AMHP)
  In P frame
    AMHP get the prediction block from the same reference
    AMHP won’t increase the bandwidth.
block size |  | bandwidth |  | 
width | height | uni-prediction | bi-prediction | AMHP
4 | 4 | 7.56 | - | Disabled
4 | 8 | 5.16 | - | Disabled
8 | 4 | 5.16 | - | Disabled
8 | 8 | 3.52 | - | 4
4 | 16 | 3.95 | - | 4.5
16 | 4 | 3.95 | - | 4.5

## Slide 10: Bandwidth analysis
Advance multi-hypothesis inter prediction (AMHP)
  In B frame
    AMHP is disabled when the reference frame exist in both list
      E.g. list0{ 0, 8 } list1 { 8, 16 }, AMHP is disabled when uni-prediction MV referring to frame 8.
    AMHP get the prediction block from the same reference
    AMHP won’t increase the bandwidth
block size |  | bandwidth |  | 
width | height | uni-prediction | bi-prediction | AMHP
4 | 4 | 7.56 | - | 9
4 | 8 | 5.16 | 10.31 | 6
8 | 4 | 5.16 | 10.31 | 6
8 | 8 | 3.52 | 7.03 | 4
4 | 16 | 3.95 | 7.91 | 4.5
16 | 4 | 3.95 | 7.91 | 4.5

## Slide 11: Experimental Results
 | Random access Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.06% | 0.01% | 101% | 101%
Class A2 | -0.03% | -0.02% | -0.01% | 101% | 99%
Class B | -0.04% | -0.02% | -0.04% | 101% | 101%
Class C | -0.03% | -0.02% | -0.18% | 101% | 104%
Class E |  |  |  |  | 
Overall | -0.03% | -0.00% | -0.06% | 101% | 101%
Class D | 0.00% | -0.09% | 0.00% | 102% | 104%
Class F | -0.04% | -0.01% | -0.14% | 102% | 104%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | -0.15% | -0.20% | 101% | 101%
Class C | -0.05% | 0.21% | 0.14% | 101% | 102%
Class E | -0.04% | 0.32% | -0.37% | 101% | 104%
Overall | -0.02% | 0.09% | -0.13% | 101% | 102%
Class D | 0.01% | 0.63% | -0.42% | 101% | 102%
Class F | -0.17% | -0.07% | -0.54% | 101% | 102%
 | Low delay P Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.95% | -1.29% | -1.30% | 102% | 103%
Class C | -0.66% | -0.96% | -1.00% | 102% | 99%
Class E | -0.83% | -1.02% | -0.96% | 102% | 99%
Overall | -0.82% | -1.11% | -1.12% | 102% | 100%
Class D | -0.49% | -0.47% | -0.47% | 99% | 101%
Class F | -0.43% | 0.09% | -0.15% | 101% | 102%
Thank MediaTek for the cross-checking

## Slide 12: Conclusion
AMHP is a multi-hypothesis prediction for uni-prediction of AMVP mode.
  Same reference
  MV difference no more than 1 pixel
AMHP won’t increase bandwidth cost
  For P frame : AMHP is enabled when
    ( block_width + block_height ) > 12
  For B frame : AMHP is enabled in all block size
Experimental results reportedly show
  -0.03% -0.00% -0.06% Enc 101% Dec 101% compared to VTM-RA
  -0.02% 0.09% -0.13% Enc 101% Dec 102% compared to VTM-LDB
  -0.82% -1.11% -1.12% Enc 102% Dec 100% compared to VTM-LDB
Based on the above results, it is suggested to further study it in CE