## Slide 1: JVET-N0170 CE3-related: Explicitly signal non angular modes with encoding changes
Fujitsu
14th JVET Meeting: Geneva, CH, 19–27 Mar. 2019

## Slide 2: Intro - CE3-3.5.1
Explicitly signal non angular modes
  intra_luma_non_ang_flag 0 : angular 1 : non-angular
  intra_luma_planar_flag 0 : DC 1 : Planar
MPM list only for angular modes
  Derivation process the same as current used in VTM for ref_idx > 0
  No dependency with ISP mode and ref_idx for MPM derivation and index coding
VTM-4.0
parse intra_luma_ref_idx
if (intra_luma_ref_idx == 0)
parse intra_subpartitions_mode_flag
if (intra_subpartitions_mode_flag == 0)
parse intra_luma_mpm_flag
MPM with Planar&DC
else
MPM without DC
else
MPM without Planar&DC
Proposed
parse intra_luma_non_ang_flag
if(intra_luma_non_ang_flag == 1)
// no MPM
parse intra_luma_planar_flag
if (intra_luma_planar_flag)
parse intra_subpartitions_mode_flag
else
parse intra_luma_mpm_flag
if (intra_luma_mpm_flag)
parse intra_luma_ref_idx
if (intra_luma_ref_idx == 0)
parse intra_subpartitions_mode_flag
MPM without Planar&DC
Notes: Coding mpm_flag before mrl and isp.
Such design ensure independency of isp and mrl during the MPM process and MPM_idx coding process.

## Slide 3: Spec changes
coding_unit( x0, y0, cbWidth, cbHeight, treeType ) { | Descriptor
… | 
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
intra_luma_non_ang_flag[ x0 ][ y0 ] | ae(v)
if( intra_luma_non_ang_flag[ x0 ][ y0 ] ) | 
intra_luma_planar_flag[ x0 ][ y0 ] | ae(v)
else { | 
intra_luma_mpm_flag[ x0 ][ y0 ] | ae(v)
if( intra_luma_mpm_flag[ x0 ][ y0 ] ) | 
intra_luma_mpm_idx[ x0 ][ y0 ] | ae(v)
else | 
intra_luma_mpm_remainder[ x0 ][ y0 ] | ae(v)
} | 
if( intra_luma_mpm_flag[ x0 ][ y0 ] && ( y0 % CtbSizeY ) > 0 ) | 
intra_luma_ref_idx[ x0 ][ y0 ] | ae(v)
if ( ( ( intra_luma_mpm_flag[ x0 ][ y0 ] && intra_luma_ref_idx[ x0 ][ y0 ] = = 0 ) ¦¦ intra_luma_planar_flag[ x0 ][ y0 ] ) && ( cbWidth <= MaxTbSizeY ¦ ¦ cbHeight <= MaxTbSizeY ) && ( cbWidth * cbHeight > MinTbSizeY * MinTbSizeY ) ) | 
intra_subpartitions_mode_flag[ x0 ][ y0 ] | ae(v)
if( intra_subpartitions_mode_flag[ x0 ][ y0 ] = = 1 && cbWidth <= MaxTbSizeY && cbHeight <= MaxTbSizeY ) | 
intra_subpartitions_split_flag[ x0 ][ y0 ] | ae(v)
} | 
… | 
} | 

## Slide 4: Encoding only changes
VTM-4.0 adding left intra mode(L) and above intra mode(A) into the R-D check list
Propose to add modes with lowest bit cost for mode signaling depend on L and A
if L == A
if L > DC
adding lowest bit cost angular mode into R-D check list
else
adding lowest bit cost non-angular mode into R-D check list
else
adding lowest bit cost angular mode + non-angular mode into R-D check list
if L == A
adding L into R-D check list
else
adding L + A into R-D check list

## Slide 5: Result
Encoding time not reliable
 | All Intra Main10 |  |  |  | 
 | Over VTM 4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.42% | -0.39% | -0.32% | 98% | 98%
Class A2 | -0.14% | -0.02% | -0.15% | 98% | 99%
Class B | -0.18% | -0.12% | -0.09% | 101% | 97%
Class C | -0.03% | -0.12% | -0.02% | 102% | 98%
Class E | -0.20% | -0.18% | -0.06% | 107% | 97%
Overall | -0.18% | -0.16% | -0.12% | 101% | 98%
Class D | -0.09% | -0.07% | -0.15% | 107% | 95%
Class F | 0.08% | 0.07% | -0.02% | 102% | 98%
 | Random access Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM!
Class B | -0.03% | 0.02% | 0.03% | 106% | #NUM!
Class C | -0.02% | 0.03% | -0.17% | 115% | 100%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #NUM!
Class D | -0.01% | -0.12% | 0.04% | 140% | 100%
Class F | 0.05% | -0.05% | -0.01% | 124% | 100%

## Slide 6: Conclusion
Propose a encoding only changes for explicitly signal non angular modes
  Better trade-off between the gain and the encoding run-time
    0.2%(0.4% for class A1) luma gain with 101%/98% coding runtime for AI
    0.x%(0.x% for class A1) luma gain with 100%/100% coding runtime for RA
Suggest to adopt CE3-3.5.1 with the proposed encoding only changes
Thanks for NHK’s cross checking