## Slide 1: CE 3-related: A unified MPM list for intra mode coding (JVET-N0185)
Audiovisual Technology Laboratory
Biao Wang, Anand Meher Kotra, Semih Esenlik, Han Gao, Jianle Chen
Mar. 20. 2019

## Slide 2: Problem and Proposed Solution
In VTM4.0, three different 6-MPM list generations are used, e.g. :
  A 6-MPM list for intra blocks with MRL enabled
  A 6-MPM list for intra blocks with ISP mode enabled
  A 6-MPM list for normal intra block
Ideal solution: using a single list with fixed number of candidates and same index coding.
Proposed solution: a single MPM list is shared by Normal, MRL and ISP
  MPM list construction independent of normal, MRL, or ISP block
  with same index coding
  1st bin of MPM index is coded with contexts
Results:
  AI -0.06% (Y) 0.02% (U) 0.02% (V)
  RA 0.00% (Y) -0.01% (U) -0.09% (V)

## Slide 3: A Simple Unified MPM list:
As simple as MPM list when MRL=0 and ISP=0:
  both Left and Above non-angular
  both angular and they are the same
  one angular, the other non-angular
  both angular and they are different
    if abs (Left – above) in the ranges of 2 to 62
    Otherwise
The unified MPM list is much simpler than VTM4.0:
 | Possible branches | #comparison
Proposed | 5 | 6
VTM4.0 | 20 | 7

## Slide 4: Results (CTC conditions)
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.34% | -0.26% | -0.20% | 100% | 101%
Class A2 | -0.05% | 0.04% | -0.05% | 101% | 101%
Class B | -0.06% | 0.06% | 0.09% | 101% | 100%
Class C | 0.08% | 0.05% | 0.05% | 102% | 99%
Class E | 0.04% | 0.19% | 0.12% | 101% | 99%
Overall | -0.06% | 0.02% | 0.02% | 101% | 100%
Class D | -0.08% | 0.06% | -0.17% | 101% | 100%
Class F | 0.22% | 0.19% | 0.17% | 102% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | -0.20% | -0.08% | 101% | 101%
Class A2 | 0.04% | 0.05% | 0.10% | 102% | 101%
Class B | -0.01% | 0.10% | -0.18% | 101% | 100%
Class C | 0.04% | -0.06% | -0.14% | 101% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | -0.01% | -0.09% | 101% | 100%
Class D | -0.02% | -0.12% | -0.10% | 100% | 99%
Class F | 0.18% | 0.05% | -0.01% | 101% | 100%

## Slide 5: Summary && Conclusions
A unified MPM list is proposed for intra mode coding
  regardless of whether an intra block is MRL, ISP or normal one.
  MPM index coding is also unified
The unified MPM list is much simpler than VTM4.0:
  Number of MPM branches : 20  5
  Number of comparison : 7  6
Results:
  AI -0.06% coding gain with unified design.
  RA no loss
Conclusion: we suggest to adopt the proposed solution, because we achieve
  fixed number of candidates
  same index coding
Thanks for MediaTek performing the crosscheck (JVET-N0750)