## Slide 1
CE7-7.3:
Unified rice parameter derivation
for bypassed level coding
Samsung Research
Yinji Piao
JVET-N0188

## Slide 2: Coefficient coding in VTM4.0
Binarization and Sub-block coding order
  for( k … ) { // 1st pass, max 32 bins
    sig_flag[ k ]
    if( sig_flag[ k ] ) {
    gt1_flag[k]
    if( gt1_flag[ k ] )
    par_flag[ k ]
    gt3_flag[k]
    }}
    for( k …k1 ) { // 2nd pass (EP bins)
    if(gt3_flag[k])
    remainder[ k ] // baseLevel = 4
    }
    for( k1-1 … 0) { // 3rd pass (EP bins)
    Abs_level[ k ] // baseLevel = 0
    }
if( ricePar < 3 && rem > (3<<ricePar)-1 )
{
ricePar++;
}
ricePar = riceParTable[sumAbsLevel]
where sumAbsLevel = sum of absolute neighboring
5 coeffs.
HEVC-like
JEM-like
Rice Para derivation

## Slide 3: Proposed method
Unified solution for rice parameter derivation
    for( k …k1 ) { // 2nd pass
    if(gt3_flag[k])
    remainder[ k ]
    }
    for( k1-1 … 0) { // 3rd pass
    Abs_level[ k ]
    }
ricePar = riceParTable[sumAbsLevel]
where sumAbsLevel = relative sum of AbsLevel (neighboring 5 coeffs)
, baseLevel = 0
Rice Para derivation
ricePar = riceParTable[sumAbsLevel]
where sumAbsLevel = relative sum of AbsLevel (neighboring 5 coeffs)
, baseLevel = 4
Current: sumAbsLevel = min (sum, 31)
Proposed: sumAbsLevel = max(min(sum – 5 x baseLevel, 31), 0)

## Slide 4: Proposed method
Unified solution for rice parameter derivation
  More robust for parallel processing
    Enables parallel derivation of rice parameters for the positions locate on the same diagonal line for each 4x4 subblock
Current position
Neighboring positions for sumAbsLevel
Positions for parallel derivation of rice para

## Slide 5: Experimental result
Proposed unified solution
Proposed @ lowQP
Proposed @ CTC
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-4.0 |  |  |  |  | Over VTM-4.0_lowQP |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | 0.01% | 102% | 99% | 0.00% | 0.00% | 0.00% | 102% | 99%
Class A2 | -0.01% | 0.11% | -0.01% | 100% | 101% | -0.03% | -0.07% | -0.06% | 102% | 102%
Class B | 0.00% | -0.01% | 0.08% | 102% | 101% | -0.01% | -0.01% | -0.04% | 102% | 102%
Class C | 0.00% | 0.01% | -0.07% | 101% | 101% | 0.03% | -0.03% | 0.00% | 102% | 103%
Class E | -0.01% | 0.00% | -0.03% | 101% | 102% | -0.02% | 0.00% | -0.02% | 103% | 102%
Overall | 0.00% | 0.01% | 0.00% | 102% | 101% | 0.00% | -0.02% | -0.02% | 102% | 102%
Class D | 0.00% | -0.01% | -0.08% | 102% | 101% | 0.06% | -0.01% | 0.05% | 102% | 101%
Class F | 0.05% | 0.11% | 0.03% | 102% | 102% | -0.05% | -0.03% | -0.03% | 102% | 100%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-4.0 |  |  |  |  | Over VTM-4.0_lowQP |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.09% | 0.01% | 100% | 100% | 0.00% | -0.01% | -0.01% | 100% | 102%
Class A2 | -0.05% | 0.12% | 0.02% | 100% | 101% | -0.01% | -0.02% | -0.02% | 101% | 103%
Class B | -0.02% | 0.16% | -0.18% | 101% | 99% | 0.00% | 0.00% | 0.00% | 102% | 104%
Class C | -0.01% | -0.11% | -0.20% | 103% | 101% | 0.01% | -0.02% | -0.07% | 102% | 103%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.02% | 0.03% | -0.11% | 101% | 100% | 0.00% | -0.01% | -0.02% | 102% | 103%
Class D | -0.03% | -0.17% | -0.36% | 104% | 102% | 0.01% | -0.03% | -0.09% | 103% | 103%
Class F | 0.01% | -0.13% | -0.17% | 102% | 101% | -0.11% | -0.08% | -0.04% | 102% | 100%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-4.0 |  |  |  |  | Over VTM-4.0_lowQP |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.01% | -0.26% | -0.48% | 100% | 101% | 0.00% | 0.01% | 0.00% | 101% | 102%
Class C | 0.01% | 0.32% | -0.10% | 99% | 97% | -0.01% | 0.00% | 0.03% | 102% | 103%
Class E | -0.05% | 0.77% | 0.12% | 100% | 101% | 0.01% | -0.05% | -0.03% | 102% | 102%
Overall | -0.01% | 0.19% | -0.20% | 100% | 100% | 0.00% | -0.01% | 0.00% | 102% | 102%
Class D | -0.02% | 0.12% | 0.10% | 100% | 98% | -0.01% | -0.01% | -0.05% | 101% | 103%
Class F | -0.01% | 0.46% | 0.04% | 87% | 97% | -0.08% | 0.08% | 0.02% | 102% | 103%

## Slide 6: Conclusion
Unified solution for remaining level and fully bypass-coded level coding
No performance decrease
More robust for parallel processing