## Slide 1
Non-CE7:
Unified last position coding for 32-point transforms
Samsung Research
Yinji Piao
JVET-N0189

## Slide 2: Coefficient coding in VTM4.0
Binarization for last significant position
  If 32-point transform (32xN, Mx32)
    DST7/DCT8 || Subblock-transform
      Keep top-left min(16,M) x min(16,N), zero-out high frequency coefficients
      Last position: 12-15 / 16 (7+2=9bins)
    DCT2/DCT2 || TransformSkip
      Keep all coefficients
      Last position: 12-15 / 32 (8+2=10bins)
Magnitude of last position component | Truncated unary(context model) | Fixed binary(bypass) | 
0 | 0 | - | 0
1 | 10 | - | 0
2 | 110 | - | 0
3 | 111(0) | - | 0
4-5 | 11110 | X | 0-1
6-7 | 11111(0) | X | 0-1
8-11 | 1111110 | XX | 0-3
12-15 | 1111111(0) | XX | 0-3
16-23 | 111111110 | XXX | 0-7
24-31 | 111111111 | XXX | 0-7

## Slide 3: Proposed method
Unified binarization for all 32-point transforms
  Code last position in range of 0-15 as position within block size of 32
if( ( tu_mts_idx[ x0 ][ y0 ] > 0 ¦ ¦ ( cu_sbt_flag && log2TbWidth < 6 && log2TbHeight < 6 ) ) && cIdx = = 0 && log2TbWidth > 4 )
log2TbWidth = 4
else
log2TbWidth = Min( log2TbWidth, 5 )
if( tu_mts_idx[ x0 ][ y0 ] > 0 ¦ ¦ ( cu_sbt_flag && log2TbWidth < 6 && log2TbHeight < 6 ) ) && cIdx = = 0 && log2TbHeight > 4 )
log2TbHeight = 4
else
log2TbHeight = Min( log2TbHeight, 5 )
Parse last_sig_coeff

## Slide 4: Experimental result
Proposed unified solution
Proposed @ lowQP
Proposed @ CTC
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-4.0 |  |  |  |  | Over VTM-4.0_lowQP |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.02% | 0.00% | 101% | 103% | 0.01% | 0.03% | -0.01% | 103% | 106%
Class A2 | 0.01% | 0.15% | 0.03% | 103% | 106% |  |  |  |  | 
Class B | 0.02% | 0.04% | 0.04% | 101% | 107% | 0.00% | 0.02% | 0.00% | 101% | 101%
Class C | 0.01% | -0.04% | 0.01% | 100% | 97% | 0.00% | 0.00% | -0.01% | 101% | 103%
Class E | 0.04% | 0.02% | -0.05% | 100% | 99% | 0.01% | 0.01% | 0.00% | 105% | 100%
Overall | 0.02% | 0.03% | 0.01% | 101% | 102% |  |  |  |  | 
Class D | 0.01% | -0.09% | -0.04% | 100% | 99% | 0.00% | -0.01% | 0.03% | 111% | 105%
Class F | 0.00% | -0.01% | 0.00% | 101% | 103% | 0.01% | 0.02% | -0.02% | 100% | 100%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-4.0 |  |  |  |  | Over VTM-4.0_lowQP |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.04% | 0.00% | 106% | 105% |  |  |  |  | 
Class A2 | -0.01% | 0.09% | 0.04% | 105% | 104% |  |  |  |  | 
Class B | 0.02% | 0.03% | -0.06% | 101% | 103% |  |  |  |  | 
Class C | 0.02% | -0.11% | -0.13% | 100% | 99% | 0.00% | -0.01% | 0.02% | 100% | 102%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.01% | -0.01% | -0.05% | 103% | 102% |  |  |  |  | 
Class D | 0.01% | -0.08% | 0.15% | 100% | 99% | 0.00% | 0.02% | -0.05% | 99% | 100%
Class F | -0.01% | 0.00% | 0.08% | 100% | 99% |  |  |  |  | 
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-4.0 |  |  |  |  | Over VTM-4.0_lowQP |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.00% | -0.14% | 0.07% | 100% | 97% |  |  |  |  | 
Class C | -0.02% | 0.35% | 0.03% | 102% | 114% | -0.01% | 0.04% | 0.01% | 101% | 108%
Class E | -0.01% | 0.42% | 0.30% | 102% | 114% |  |  |  |  | 
Overall | -0.01% | 0.17% | 0.11% | 101% | 106% |  |  |  |  | 
Class D | 0.02% | 0.05% | -0.22% | 99% | 100% | -0.02% | -0.05% | -0.02% | 99% | 102%
Class F | -0.05% | -0.33% | 0.86% | 88% | 100% |  |  |  |  | 

## Slide 5: Conclusion
Unified last position coding for MTS/Sub-block transform/DCT2/TransformSkip
No performance loss
Suggest adoption to next VTM s/w