## Slide 1
JVET-N0204
AHG18: Support of quantization matrices
T. Toma, K. Abe
Panasonic Corporation
S.-C. Lim, J. Kang
ETRI

## Slide 2
2
Background
Quantization matrices have been proposed in Macao and Marrakech (JVET-L0121, M-0083) and it was agreed in principle that quantization matrices are necessary in VVC.

## Slide 3
3
Introduction
This contribution proposes HEVC based quantization matrices with the following extensions.
  Support matrices signaling of 2x2 chroma CU and 64x64 luma CU.
  Derive matrices for rectangular CU by down-sampling from those for square CU.
  Disable quantization matrices for luma regardless of CU size if transform skip is enabled.

## Slide 4
4
1. Support matrices signaling of 2x2 chroma CU and 64x64 luma CU
Quantization matrices for 2x2 chroma CU and 64x64 luma CU are signaled on top of 4x4, 8x8, 16x16 and 32x32.
Default matrices are also supported.
  4x4, 8x8, 16x16, and 32x32 are the same as those in HEVC.
  2x2 default matrices for chroma are down-sampled from 4x4 matrices, and 64x64 default matrices for luma are up-sampled from 8x8 matrices.
Size of quantization matrix | sizeId
2x2 (chroma only) | 1
4x4 | 2
8x8 | 3
16x16 | 4
32x32 | 5
64x64 (luma only) | 6

## Slide 5
5
2. Creation of quantization matrices for rectangular CU
INTRA8X8_LUMA =
16, 16, 16, 16, 17, 18, 21, 24,
16, 16, 16, 16, 17, 19, 22, 25,
16, 16, 17, 18, 20, 22, 25, 29,
16, 16, 18, 21, 24, 27, 31, 36,
17, 17, 20, 24, 30, 35, 41, 47,
18, 19, 22, 27, 35, 44, 54, 65,
21, 22, 25, 31, 41, 54, 70, 88,
24, 25, 29, 36, 47, 65, 88,115,
INTRA4X8_LUMA =
16, 16, 17, 21,
16, 16, 17, 22,
16, 17, 20, 25,
16, 18, 24, 31,
17, 20, 30, 41,
18, 22, 35, 54,
21, 25, 41, 70,
24, 29, 47, 88,
Quantization matrices for rectangular CU are obtained by down-sampling from matrices for square CU.
  Short side of matrix coefficients for MxN or NxM (M < N) rectangular CU are down-sampled from matrix coefficients for NxN square CU.

## Slide 6
6
3. Disabling quantization matrices if transform skip is enabled
Scaling with quantization matrices is disabled for a transform skipped luma CU regardless of CU size. [Note] In HEVC, quantization matrices are always applied for 4x4 block.
[ HEVC (VTM4.0) ]
return m_scalingListEnabledFlag && (!isTransformSkip || ((width == 4) && (height == 4)));
[ This proposal ]
return m_scalingListEnabledFlag && (!isTransformSkip);

## Slide 7
7
Simulation results
Proposed method is implemented into VTM 4.0.
Simulation was conducted using default matrices that are obtained from HEVC are used.
BD-rate loss is 1.48% for AI, 0.40% for RA, and 0.80% for LDB.
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 1.66% | 1.46% | -0.80% | 108% | 104%
Class A2 | 1.99% | 0.17% | -0.19% | 106% | 106%
Class B | 1.32% | -1.38% | -1.73% | 107% | 104%
Class C | 1.96% | -0.44% | -0.61% | 99% | 108%
Class E | 0.43% | -0.88% | -1.09% | 109% | 104%
Overall | 1.48% | -0.36% | -0.96% | 106% | 105%
Class D | 2.13% | -0.61% | -0.80% | 98% | 116%
Class F | 0.81% | 0.25% | -0.10% | 103% | 104%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.09% | 1.60% | -0.79% | 104% | 101%
Class A2 | -0.56% | -0.41% | -0.60% | 102% | 102%
Class B | 0.43% | -1.20% | -1.89% | 105% | 103%
Class C | 1.43% | -0.45% | -0.72% | 102% | 111%
Class E |  |  |  |  | 
Overall | 0.40% | -0.28% | -1.10% | 103% | 104%
Class D | 1.49% | -1.10% | -0.92% | 101% | 132%
Class F | 0.73% | 0.33% | -0.04% | 104% | 108%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.49% | -1.95% | -2.87% | 106% | 106%
Class C | 1.29% | -0.12% | -0.90% | 102% | 113%
Class E | 0.67% | -0.53% | -1.63% | 105% | 111%
Overall | 0.80% | -0.98% | -1.90% | 104% | 109%
Class D | 1.19% | -0.86% | -1.23% | 102% | 136%
Class F | 0.55% | 0.41% | 0.20% | 105% | 113%

## Slide 8
8
Conclusions
HEVC based quantization matrices with following extensions is proposed.
  Support matrices signaling of 2x2 chroma CU and 64x64 luma CU.
  Derive matrices for rectangular CU by down-sampling from those for square CU.
  Disable quantization matrices for luma regardless of CU size if transform skip is enabled.
This method is implemented into VTM 4.0
It is suggested to adopt this proposal into VVC.

## Slide 9
9
Thank Sony for cross-checking this proposal !