## Slide 1
JVET-N0207
AHG14 : CABAC skip mode
K. Abe, T. Toma
Panasonic Corporation

## Slide 2
2
Proposal
Introduce CABAC skip mode which directly outputs binarized bins.
It is originally proposed by JVET-M0089.
Binarization
CABAC
Trans/Quant
＋
－
Intra Pred
Inter Pred
Input
image
Output
stream
Inv Quant/Trans
Bin stream
buffer
Bit stream
buffer
It can avoid processing delay cased by CABAC throughput.
It can be switched at stream level.

## Slide 3
3
CABAC throughput issue
Example of CABAC throughput (assume low performance HW)
Decoder
Encoding
decision
1 cycle
pState
transition
1 bin
Renorm
pState
Table
N bits
Decoding
decision
pState
transition
Renorm
pState
Table
N bits
1 bin
1 cycle
1bin per 1cycle
Encoder
1bin per 2cycle
Decoder performance tends to be the bottleneck.
※High performance HW might be able to
improve it with parallel scheme.

## Slide 4
4
CABAC throughput issue
Peak bit to bin ratio
CABAC throughput
Peak bitrate
CABAC
decoder
Binarization
decoder
“CABAC throughput” has to be greater than “Peak bitrate” “Peak bit to bin ratio”
Guarantee condition of decode buffer
Bit stream
buffer
Bin stream
buffer
Input bit stream
Bit stream
buffer size
Bin stream
buffer size

## Slide 5
5
CABAC throughput issue
Assumption1
(Broadcasting TV)
This issue will occurs with low performance HW & high bitrate use cases.
Assumption2
(Automotive camera system)
HW core (per 1ch) : 400MHz, 1000mW
Delay : 500msec
Stream : 30Mbps, 4K/60p, RA
Peak bit to bin ratio : 1.5 (at I-Picture)
HW core (per 1ch) : 400MHz, 500mW
Delay : 3msec
Stream : 160Mbps, 4K/60p, AI
Peak bit to bin ratio : 1.5 (at I-Picture)
200M 30M 1.5
200M 160M 1.5
1bin/2cycle with 400MHz
(throughput)
(bitrate)
(bit to bin ratio)
(throughput)
(bitrate)
>
<
(bit to bin ratio)
OK
NG
It is assumed experientially, but below the limitation of specification.
It might be more large since the limitation of specification will be greater in this condition.
difficult to improve it

## Slide 6
CABAC throughput issue
CABAC throughput issue is more significant for low delay
Low delay
Non low delay
Local bin peak is acceptable if it is guaranteed by picture level.
Total bin has to be guaranteed by each tile (bin peak is not acceptable).
Image quality degradation
# bin at local area
max
min
# bin at local area
max
min

## Slide 7
Example of CABAC skip mode use cases
Delay of several milliseconds is required for video codec in these fields.
But bitrate is not so critical for some cases. Some applications in these fields still use H.264 with CAVLC due to the mentioned issue.
ex2) Cooperative driving
ex3) Remote operation
ECU
ex1) Automotive camera
CABAC skip mode is useful for these use cases.

## Slide 8
Simulation results
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 30.23% | 21.59% | 24.13% | 129% | 101%
Class A2 | 26.76% | 21.68% | 24.25% | 110% | 103%
Class B | 25.35% | 22.96% | 22.21% | 111% | 100%
Class C | 21.70% | 20.67% | 20.51% | 96% | 100%
Class E | 21.89% | 19.90% | 19.69% | 109% | 99%
Overall | 25.01% | 21.50% | 22.07% | 110% | 101%
Class D | 22.07% | 20.38% | 20.80% | 93% | 98%
Class F | 22.14% | 22.67% | 22.39% | 104% | 94%
Low delay B Main10 |  |  |  | 
Y | U | V | EncT | DecT
33.03% | 11.69% | 10.58% | 87% | 100%
29.25% | 16.15% | 15.21% | 87% | 101%
28.87% | 12.16% | 10.85% | 93% | 109%
30.73% | 13.29% | 12.19% | 89% | 102%
27.87% | 9.79% | 11.14% | 86% | 99%
32.24% | 25.48% | 25.16% | 99% | 116%
Anchor : VTM-4.0
Test : Proposed CABAC skip mode
The loss is large, but it still keeps higher gain compared to HEVC.
Random Access Main 10 |  |  |  | 
Y | U | V | EncT | DecT
28.68% | 24.60% | 22.14% | 101% | 91%
26.46% | 17.20% | 20.72% | 94% | 94%
28.01% | 17.48% | 16.93% | 97% | 93%
24.01% | 17.30% | 16.75% | 97% | 95%
26.77% | 18.80% | 18.68% | 97% | 93%
23.06% | 15.00% | 15.84% | 94% | 96%
24.93% | 23.80% | 24.34% | 102% | 97%

## Slide 9
Additional information1
Anchor : H.264/CABAC (JM-19.0)
Test : H.264/CAVLC (JM-19.0)
Bits increasing of proposal is almost same as that of H.264/CAVLC.
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 35.41% | 25.00% | 23.75% | 91% | 97%
Class A2 | 29.90% | 19.21% | 17.67% | 95% | 113%
Class B | 25.08% | 13.79% | 14.62% | 98% | 98%
Class C | 16.36% | 10.86% | 11.09% | 108% | 95%
Class E |  |  |  |  | 
Overall | 25.78% | 16.33% | 16.12% | 99% | 100%
Class D | 13.91% | 7.70% | 7.92% | 115% | 91%
Class F |  |  |  |  | 

## Slide 10
Additional information2
Anchor : H.264/CAVLC (JM-19.0)
Test : VTM-4.0 + Proposal
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -70.68% | -72.53% | -74.61% | 739% | 155%
Class A2 | -68.70% | -68.30% | -64.25% | 786% | 157%
Class B | -61.66% | -68.07% | -70.13% | 676% | 166%
Class C | -50.47% | -56.56% | -57.93% | 693% | 235%
Class E |  |  |  |  | 
Overall | -61.89% | -65.94% | -66.60% | 714% | 178%
Class D | -46.55% | -55.15% | -56.20% | 640% | 274%
Class F |  |  |  |  | 
Proposal already has enough benefit compared to H.264/CAVLC.

## Slide 11
11
Conclusions
CABAC skip mode can avoid the delay cased by CABAC throughput.
We propose to introduce CABAC skip mode into VVC.
It is useful for the use case of high bitrate with low performance HW.
(mainly for low delay)
25%, 27%, 31% bits increasing for AI, RA, LDB on VTM-4.0.
It still keeps higher gain compared to HEVC, and it is twice as high performance as H.264 with CAVLC.

## Slide 12
12
Thanks Canon for cross-checking of the proposal.
Acknowledgments