## Slide 1
JVET-N0215
Non-CE3 : Intra prediction mode restriction in small blocks
Daeyoung Lee
daeyung2002@khu.ac.kr

## Slide 2
Many directional modes are used
  Many bits are needed to represent many modes
Intra modes : 0,1,2,3,4, … , 64,65,66
Intra prediction modes
JVET-N0215

## Slide 3
Restriction the use of odd number intra angular mode in 4x4 blocks
  In a small block such as 4x4, the signal size for expressing the prediction mode may be burden rather than the size of the prediction error
Proposal
Intra modes : 0,1,2,3,4, … , 64,65,66
Intra modes : 0,1, 2,4,6, … , 62,64,66
4x4 blocks
Other blocks
0 : Planar
1 : DC
JVET-N0215

## Slide 4
Proposal
Modified 6MPM generation
  In the 4x4 block, make MPM list configured in even angular mode
Truncated Binary Code (TBC) in 29 non-MPM modes in 4x4 blocks
  Since the 32 odd angular modes of the intra prediction are not used in the 4x4 blocks, the TBC is performed for a total of 29 modes in the 4x4 blocks which excludes the 32 odd modes and 6 MPM modes
VTM 4.0 | Proposal | 
 | 4x4 blocks (For angular modes) | The others (no changes)
Left mode | (Left mode >> 1) << 1 | Left mode
Above mode | (Above mode >> 1) << 1 | Above mode
Neighbor mode + 1 | Neighbor mode + 2 | Neighbor mode + 1
Neighbor mode - 1 | Neighbor mode – 2 | Neighbor mode - 1
Neighbor mode + 2 | Neighbor mode + 4 | Neighbor mode + 2
Neighbor mode - 2 | Neighbor mode – 4 | Neighbor mode - 2
JVET-N0215

## Slide 5
Conclusion
Experimental result
  Suggest these conditions for further study
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.04% | -0.03% | 101% | 101%
Class A2 |  |  |  |  | 
Class B | -0.02% | -0.02% | 0.08% | 100% | 100%
Class C | -0.03% | -0.07% | -0.05% | 98% | 98%
Class E | -0.04% | 0.02% | 0.01% | 101% | 98%
Overall |  |  |  |  | 
Class D | -0.08% | -0.03% | -0.10% | 101% | 104%
Class F (optional) |  |  |  |  | 
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 0.02% | 0.19% | 0.24% | 97% | 98%
Overall |  |  |  |  | 
Class D | -0.01% | -0.13% | -0.37% | 97% | 95%
Class F (optional) |  |  |  |  | 
JVET-N0215