## Slide 1: [AHG12/AHG17] Signaling of virtual boundaries
Amith DSouza

## Slide 2: Cubemap based face arrangements
Multiple face arrangements for Cubemap based formats and the discontinuities marked in red

## Slide 3: Sample tile group split for alternate face arrangement
Example tile groups is shown in figure
There can be other alternate tile grouping mechanisms than shown
Blue lines show the discontinuities in the picture
Dotted greens show the possible virtual boundaries with current tile groups
Some additional pixels will be defined as virtual boundary even though there is no actual discontinuity in the image

## Slide 4: Signalling of virtual boundaries
tile_group_ virtual_boundary_flag[i] defines if virtual boundaries are present in the ith tile group
derive_tile_group_virtual_boundary_flag[i] indicates that the virtual boundary co-ordinates are derived from the previous tile group
tile_group_num_vert_boundary[i] and tile_group_num_hor_boundary[i] defines the number of vertical and horizontal boundaries in the ith tile group respectively
tile_group_XXXX_boundary_ctu_idx[i][j] indicates the CTU containing the jth virtual boundary in the ith tile group
tile_group_XXXX_boundary_ctu_offset[i][j] indicates the offset of the virtual boundary from the first sample of the CTU
pic_parameter_set_rbsp( ) { |  | Descriptor
… |  | 
if( rect_tile_group_flag ) { |  | 
signalled_tile_group_id_flag |  | u(1)
if( signalled_tile_group_id_flag ) { |  | 
signalled_tile_group_id_length_minus1 |  | ue(v)
for( i = 0; i <= num_tile_groups_in_pic_minus1; i++ ) |  | 
tile_group_id[ i ] |  | u(v)
} |  | 
} |  | 
} |  | 
for( i = 0; i <= num_tile_groups_in_pic_minus1; i++ ) { |  | 
tile_group_virtual_boundary_flag[i] |  | u(1)
if(tile_group_virtual_boundary_flag[i]){ |  | 
if( i>0 ){ |  | 
derive_tile_group_virtual_boundary_flag[i] |  | u(1)
} |  | 
if(!derive_tile_group_virtual_boundary_flag[i]){ |  | 
tile_group_num_vert_boundary[i] |  | u(2)
for(j=0;j< tile_group_num_vert_boundary[i];j++){ |  | 
tile_group_vert_boundary_ctu_idx[i][j] |  | ue(v)
tile_group_vert_boundary_ctu_offset[i][j] |  | ue(v)
} |  | 
tile_group_num_hor_boundary[i] |  | u(2)
for(j=0;j< tile_group_num_hor_boundary[i];j++){ |  | 
tile_group_hor_boundary_ctu_idx[i][j] |  | ue(v)
tile_group_hor_boundary_ctu_offset[i][j] |  | ue(v)
} |  | 
} |  | 
} |  | 
} |  | 
… |  | 
} |  | 

## Slide 5: Conclusion
A method of signalling virtual boundaries is shown in this contribution
The virtual boundaries are signalled at PPS level
Virtual boundaries are defined for tile groups rather than entire picture
Virtual boundaries span across the entire tile group
In-loop filters at additional pixels can be disabled if the virtual boundaries do not span across the entire tile group
An alternative could be to signal the start and end co-ordinates of the virtual boundaries

## Slide 6: Thank You