## Slide 1: JVET-N0243 Non-CE5: Complementary results of tests CE5-3 on Non-Linear ALF
Jonathan Taquet Patrice Onno Christophe Gisquet Guillaume Laroche

## Slide 2: JVET-N0243 Non-CE5: Complementary results of tests CE5-3 on Non-Linear ALF
Jonathan Taquet Patrice Onno Christophe Gisquet Guillaume Laroche
2019-03-20

## Slide 3: Non-Linear ALF in CE5-3

## Slide 4: Non-Linear ALF (as in M0385 and in CE5-3 Test-1)
ALF
NL-ALF
  Parameters for each filter:
    Filter coefficients ()
    Filter clipping values ( for in )

## Slide 5: Non-Linear ALF in CE5-3 Tests-2 & Test-3
Test 2:
  Enable switching between linear and non-linear filters signalling
    i.e. possibility to disable the signaling of the clipping values
  Not so much complexity difference with Test-1, slight coding gains.
Test 3:
  Reduce the number of clipping operations (and of signalled clipping values)
    Only apply clipping to a sub-set of positions (Luma and Chroma)

## Slide 6: Proposed changes

## Slide 7: Enable use of alternative filters at CTU level
Proposal contains 2 main aspects:
At « Tile Group » level,
  Addition of further alternative Luma filter sets
    Up to 8 Luma filter sets can be signaled
  Addition of further filter index mapping tables for new alternative Luma filter sets
  Addition of further alternative Chroma filters
    Up to 8 Chroma filters can be signaled
At CTU level, signal the selected filter alternative
  If ALF is enabled on Luma CTB
    Signal alternative filter set index, for each filter index (filter indexes in the first alternative set)
      Indicates which filter to use when processing samples of a given class in a given Luma CTB [using filter index mapping tables]
  If ALF is enabled on a Chroma CTB
    Signal alternative filter index
      Indicates which filter to use when processing samples in a given Chroma CTB

## Slide 8: Signaling of Luma alternative filter sets
Goal: Reduce alf_luma_coeff_delta_idx signaling by using “embedded” tables
  Each alternative filter set table ‘’ has a number of filters
  Class/filter index merging of previous alternative filter set table ‘-1’ is kept or further merged

## Slide 9: Results

## Slide 10: Tests
Test-1: CE5-3.2 + proposed changes
  cross-checked
Test-2: CE5-3.2 + proposed changes, with reduced encoder complexity
  informative
Test-3: CE5-3.2 + CE5-3.3 (less clipping operations) + proposed changes
  cross-checked

## Slide 11: Results AI
Chart: AI - BDR gains / Encoder runtime increase
| -6.0000000000000001E-3 | 0
 | 1.06 | 1
 | 1.0142 | 1.0165 | 1.0009 | 1.0137 | 1.0099 | 1.0045
YUV = (14*Y+U+V)/16
Class (NumCTUs) | Luma | Chroma
 | All Tests | All Tests
Class A (510) | 1 | 8
Class B (135) | 1 | 8
Class C (28) | 1 | 8
Class D (8) | 1 | 8
Class E (60) | 1 | 8
Class F (28) | 1 | 8
Class F (60) | 1 | 8
Class F (135) | 1 | 8
Max. number of tested alternatives

## Slide 12: Results RA
Chart: RA - BDR gains / Encoder runtime increase
| -1.2E-2 | 0
 | 1.12 | 1
 | 1.031 | 1.0153 | 0.99741 | 0.9988 | 1.0032 | 0.98972
YUV = (14*Y+U+V)/16
Class (NumCTUs) | Luma |  | Chroma
 | Test-1 and Test-3 | Test-2 | All Tests
Class A (510) | 6 | 5 | 8
Class B (135) | 5 | 4 | 8
Class C (28) | 2 | 1 | 8
Class D (8) | 1 | 1 | 8
Class E (60) | 3 | 2 | 8
Class F (28) | 2 | 1 | 8
Class F (60) | 3 | 2 | 8
Class F (135) | 5 | 4 | 8
Max. number of tested alternatives

## Slide 13: Results LB
Chart: LB - BDR gains / Encoder runtime increase
| -1.6E-2 | 0
 | 1.16 | 1
 | 1.0891 | 1.0617 | 1.0239 | 1.0341 | 1.0386 | 1.0139
YUV = (14*Y+U+V)/16
Class (NumCTUs) | Luma |  | Chroma
 | Test-1 and Test-3 | Test-2 | All Tests
Class A (510) | 6 | 5 | 8
Class B (135) | 5 | 4 | 8
Class C (28) | 2 | 1 | 8
Class D (8) | 1 | 1 | 8
Class E (60) | 3 | 2 | 8
Class F (28) | 2 | 1 | 8
Class F (60) | 3 | 2 | 8
Class F (135) | 5 | 4 | 8
Max. number of tested alternatives

## Slide 14: Results LP
Chart: LP - BDR gains / Encoder runtime increase
| -2.1999999999999999E-2 | 0
 | 1.22 | 1
 | 1.1682 | 1.1178 | 1.0672 | 1.0803 | 1.0842 | 1.0396
YUV = (14*Y+U+V)/16
Class (NumCTUs) | Luma |  | Chroma
 | Test-1 and Test-3 | Test-2 | All Tests
Class A (510) | 6 | 5 | 8
Class B (135) | 5 | 4 | 8
Class C (28) | 2 | 1 | 8
Class D (8) | 1 | 1 | 8
Class E (60) | 3 | 2 | 8
Class F (28) | 2 | 1 | 8
Class F (60) | 3 | 2 | 8
Class F (135) | 5 | 4 | 8
Max. number of tested alternatives

## Slide 15: Results summary
AI
RA
LB

## Slide 16: Conclusion
Proposed changes enable good coding gains/complexity trade-off
Consider it for an adoption in VTM-5.0
Thanks to ETRI for cross-checking

## Slide 17: Thank you for your attention.

## Slide 18: Luma alternative filter sets (backup slide)
Reduce alf_luma_coeff_delta_idx signaling by imbricating tables
  Each alternative filter set table ‘’ has a number of filters
  Class/filter index merging of previous alternative filter set table ‘-1’ is kept or further merged
alf_data( ) { | Descriptor
alf_chroma_idc | tu(v)
alf_luma_num_alts_minus1 | tb(v)
for( altIdx = 0; altIdx <= alf_luma_num_alts_minus1; altIdx++ ) { | 
alf_luma_num_filters_signalled_minus1[ altIdx ] | tb(v)
if( alf_luma_num_filters_signalled_minus1[ altIdx ] > 0 ) { | 
for( filtIdx = 0; filtIdx < NumAlfFilters[ altIdx ] ; filtIdx++ ) | 
alf_luma_coeff_alt_merge_idx[ altIdx ] [ filtIdx ] | tb(v)
} | 
alf_luma_coeff_delta_flag[ altIdx ] | u(1)
} | 
} | 
…[ altIdx ] …
…
The table NumAlfFilters[ altIdx ] specify the number of different accessible adaptive loop filters for an alternative filter set for Luma component with index altIdx ranging from 0 to alf_luma_num_alts_minus1. NumAlfFilters[ 0 ] is set equal to 25. For altIdx greater than 0 NumAlfFilters[ altIdx ] is set equal to alf_luma_num_filters_signalled_minus1[ altIdx – 1 ] + 1.
…

## Slide 19: CTU signaling (backup slide)
coding_tree_unit( ) { | Descriptor
xCtb = ( CtbAddrInRs % PicWidthInCtbsY ) << CtbLog2SizeY | 
yCtb = ( CtbAddrInRs / PicWidthInCtbsY ) << CtbLog2SizeY | 
... | 
if( tile_group_alf_enabled_flag ){ | 
alf_ctb_flag [ 0 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ] | ae(v)
if( alf_ctb_flag[ 0 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ] && alf_luma_num_alts_minus1 > 0 ) { | 
for(sigFiltIdx = 0; sigFiltIdx <= alf_luma_num_filters_signalled_minus1[ 0 ] ; sigFiltIdx++) | 
alf_ctb_filter_alt_idx[ 0 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ][ sigFiltIdx ] | ae(v)
} | 
if( alf_chroma_idc = = 1 ¦ ¦ alf_chroma_idc = = 3 ) { | 
alf_ctb_flag[ 1 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ] | ae(v)
if( alf_ctb_flag[ 1 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ] && alf_chroma_num_alts_minus1 > 0 ) | 
alf_ctb_filter_alt_idx[ 1 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ][ 0 ] | ae(v)
} | 
if( alf_chroma_idc = = 2 ¦ ¦ alf_chroma_idc = = 3 ) { | 
alf_ctb_flag[ 2 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ] | ae(v)
if(alf_ctb_flag[ 2 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ] && alf_chroma_num_alts_minus1 > 0 ) | 
alf_ctb_filter_alt_idx[ 2 ][ xCtb >> Log2CtbSize ][ yCtb >> Log2CtbSize ][ 0 ] | ae(v)
} | 
} | 
... | 
} | 

## Slide 20: Encoder – main loop (backup slide)
For each component type,
  loop encoding process for numAlts a number of alternatives filters/filter set ranging from MaxNumTestedAlternatives down to 1
    MaxNumTestedAlternatives =
      Luma
        min( MAX_NUM_ALF_ALTERNATIVES_LUMA, max( 1, log2_floor - 2 ) ) [Test-1, Test-3 and Test-4]
        min( MAX_NUM_ALF_ALTERNATIVES_LUMA, max( 1, log2_floor - 3 ) ) [Test-2]
        Chroma
        min( MAX_NUM_ALF_ALTERNATIVES_CHROMA, m_numCTUsInPic * 2 ) [any test]
  Keep best RDO choice

## Slide 21: Encoder – Luma encoding process (backup slide)
Initialize:
  set ALF as active on all CTBs [‘alf_ctb_flag’s]
  set default alternative index [‘alf_ctb_filter_alt_idx’s]
    altIdx = (floor(ctuIdx * numAlts / numCTUs), for each CTUs, for all class/filter
Loop (as many times as VTM for optimizing ‘alf_ctb_flag’s + numAlts-1)
  Compute frame statistics (cov matrices) for each alternative index, for each class index
  Optimize numAlts alternative filter sets
    Optimize alternative filter set with altIdx=0
    Optimize alternative filter set with altIdx=1
      starting from filter index merging of optimized alternative filter set with altIdx=0
    […] with altIdx=2
      starting from filter index merging of optimized alternative filter set with altIdx=1
    …
  Update ‘alf_ctb_filter_alt_idx’s and ‘alf_ctb_flag’s

## Slide 22: Encoder – Chroma encoding process (backup slide)
Initialize:
  set ALF as active on all CTBs on all chroma components [‘alf_ctb_flag’s]
  set default alternative index on all chroma CTB [‘alf_ctb_filter_alt_idx’s]
    altIdx = (floor(ctuIdx * numAlts / numCTUs), for each CTUs, for all class/filter
Loop (as many times as VTM for optimizing ‘alf_ctb_flag’s + numAlts-1)
  Compute frame statistics (cov matrices) for each alternative index
  Optimize numAlts alternative filters
    Optimize alternative filter altIdx=0, using cov matrix for altIdx=0
    Optimize alternative filter altIdx=1, using cov matrix for altIdx=1
    …
  Update ‘alf_ctb_filter_alt_idx’s and ‘alf_ctb_flag’s