## Slide 1: Non-CE8: Reference memory reduction for intra block copy
Jizheng Xu, Li Zhang, Kai Zhang, Hongbin Liu, Yue Wang

## Slide 2: Memory reduction for IBC reference buffer
Solution 1
  Reduced 3 additional 64x64 buffers to 8-bit
    20% memory reduction, i.e. 4.5KBytes
Solution 2
  An separate IBC buffer w/ 7-bit precision
    Buffer design described in JVET-N0472
    6.7% memory reduction, i.e. 1.5Kbytes
Thanks to LG for cross-checking

## Slide 3: Performance
Solution A
Solution B
 | All Intra |  |  |  | 
 | Over VTM-4.0 w/ IBC on |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.03% | -0.08% | 127% | 100%
Class A2 | 0.02% | 0.00% | 0.00% | 131% | 101%
Class B | -0.02% | -0.07% | -0.02% | 131% | 101%
Class C | -0.02% | 0.08% | 0.01% | 127% | 99%
Class E | -0.10% | -0.05% | -0.01% | 132% | 100%
Overall | -0.02% | 0.00% | -0.02% | 129% | 100%
Class D | 0.01% | 0.04% | 0.05% | 125% | 106%
Class F | -0.12% | -0.06% | -0.01% | 112% | 98%
4:2:0 TGM | -0.13% | -0.16% | -0.12% | 101% | 100%
 | Random Access |  |  |  | 
 | Over VTM-4.0 w/ IBC on |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.01% | 0.02% | 108% | 100%
Class A2 | 0.00% | -0.08% | 0.00% | 111% | 100%
Class B | -0.01% | -0.17% | -0.25% | 111% | 101%
Class C | 0.00% | 0.27% | -0.06% | 114% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | -0.10% | 111% | 100%
Class D | 0.04% | 0.07% | 0.22% | 116% | 99%
Class F | -0.07% | -0.10% | -0.12% | 107% | 99%
4:2:0 TGM | -0.62% | -0.46% | -0.54% | 106% | 102%
 | All Intra |  |  |  | 
 | Over VTM-4.0 w/ IBC on |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.09% | -0.10% | 132% | 101%
Class A2 | 0.05% | 0.00% | 0.06% | 135% | 100%
Class B | 0.00% | -0.02% | 0.01% | 135% | 100%
Class C | -0.02% | 0.01% | 0.03% | 130% | 98%
Class E | -0.13% | -0.16% | -0.04% | 135% | 99%
Overall | -0.02% | -0.05% | 0.00% | 133% | 100%
Class D | 0.04% | 0.04% | 0.12% | 127% | 107%
Class F | -0.99% | -1.14% | -1.18% | 115% | 99%
4:2:0 TGM | -2.57% | -2.73% | -2.67% | 104% | 102%
 | Random Access |  |  |  | 
 | Over VTM-4.0 w/ IBC on |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.01% | 0.01% | 109% | 100%
Class A2 | 0.00% | -0.04% | 0.03% | 111% | 100%
Class B | -0.01% | -0.10% | -0.22% | 113% | 101%
Class C | -0.01% | 0.17% | 0.12% | 115% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | -0.04% | 112% | 100%
Class D | 0.05% | 0.16% | 0.20% | 117% | 101%
Class F | -0.71% | -0.77% | -0.77% | 109% | 99%
4:2:0 TGM | -1.81% | -1.65% | -1.64% | 107% | 101%
 | All Intra |  |  |  | 
 | Over VTM-4.0 w/ IBC on |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.01% | -0.01% | 127% | 103%
Class A2 | -0.01% | 0.01% | -0.03% | 130% | 100%
Class B | -0.03% | -0.01% | -0.03% | 132% | 104%
Class C | -0.03% | 0.03% | -0.03% | 127% | 111%
Class E | -0.12% | -0.16% | -0.11% | 132% | 105%
Overall | -0.04% | -0.03% | -0.04% | 130% | 105%
Class D | -0.02% | -0.01% | 0.07% | 124% | 96%
Class F | -0.09% | -0.01% | -0.21% | 113% | 110%
4:2:0 TGM | -0.24% | -0.25% | -0.27% | 101% | 102%
 | Random Access |  |  |  | 
 | Over VTM-4.0 w/ IBC on |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.08% | 0.02% | 107% | 100%
Class A2 | -0.02% | -0.06% | -0.05% | 110% | 100%
Class B | -0.02% | -0.18% | -0.32% | 111% | 102%
Class C | -0.03% | 0.13% | -0.01% | 115% | 109%
Class E |  |  |  |  | 
Overall | -0.02% | -0.05% | -0.12% | 111% | 103%
Class D | 0.03% | 0.03% | -0.02% | 116% | 112%
Class F | -0.12% | -0.07% | -0.13% | 108% | 102%
4:2:0 TGM | -0.76% | -0.62% | -0.65% | 106% | 103%
Local search range fix