## Slide 1: JVET-N00275: AHG14/AHG8/AHG17: Sections for intra refresh and inloop filter disabling
Jill Boyce, Ryan Lei, Lidong Xu

## Slide 2: Introduction
Divide a picture into two sections:
  Special section
  Remainder section of the picture outside of the special section
Flexibly use the special section for any of several encoder-selected features applied within the special section or at the boundaries between the special section and the remainder section
Section mapping
  Boundaries not associated with tiles
  Signal mapping in PPS with tile group header override at an encoder-selected granularity as small as MinCbSizeY
  Regions contained within the special section need not be contiguous
Use cases: progressive intra refresh, 360 video, region-of-interest coding

## Slide 3: Example Mapping
Special section
Remainder section

## Slide 4: Encoder selectable features
  Disabling in-loop filters across special section and remainder section boundaries
  QP offset within special section
  Forced intra within special section
  Prediction restriction for progressive intra refresh
  Extensible for other features

## Slide 5: Signaling of special section mapping
Mapping signaled in PPS, optionally overwritten in the tile group header
Horizontal and vertical granularity explicitly signaled
  Smallest signaling granularity is MinCbSizeY
    Semantic restriction that entire CU must be in same section
  Largest signaling granularity is the coded picture width or height
Syntax elements signal the number of units into which coded picture width and coded picture height are split into
  section_active_flag[ i ][ j ] signaled for each i in 0..section_hor_units_minus1, j in 0 .. section_ver_units_minus
SectionActiveMinCb[ x ][ y ] = section_active_flag
[ (x * (section_hor_units_minus1 + 1)/ PicWidthInMinCbSizeY) ]
[ (y * (section_ver_units_minus1 + 1)/ PicHeightInMinCbSizeY) ]
Decoder storage of flag at MinCbSizeY block granularity

## Slide 6: Example: 4 horizontal units, 2 vertical units
Special section
Remainder section

## Slide 7: Example: 1 hor units and 2 ver units, for 360 video cube map
Dashed lines represent cube face boundaries
Cube face rows mapped into separate sections

## Slide 8: Example 4 hor units and 1 ver unit, for progressive intra refresh
Special section for intra update region
More typical example would be 1/32 of picture

## Slide 9: Disabling in-loop filters across special section and remainder section boundaries
Flag in PPS to signal that for the two blocks across a horizontal edge or vertical edge, if one block is within the special section and the other block is within the remainder section, in-loop filtering be disabled across that edge
  Semantics to disable the in-loop filters are the same as proposed in JVET-M0892 [2], and includes all of ALF, SAO and deblocking.
  This contribution differs from JVET-M0387 in that, when selected, in-loop filters are disabled across all boundaries between the special section and remainder section, regardless of whether the remainder section is part of a “clean” region from a previously coded picture. This allows flexible section mapping patterns, while avoiding the need to keep track of “clean” regions across pictures.

## Slide 10: QP offset within special section
Flag in PPS to signal negative QP offsets for luma and chroma to be applied within the special section, used in addition to the signaled CU QP delta.
Can be used for progressive intra refresh, or for coding a region of interest with a higher quality level.
It is expected that signaling a negative QP offsets for luma and chroma for the entire special section will save bitrate vs. signaling a QP delta individually for each CU
  No experimental numbers available

## Slide 11: Forced intra within special section
Flag in PPS to force intra coding of CUs within the special section, without signaling of cu_skip_flag[ x0 ][ y0 ] and pred_mode_flag
It is expected that forcing intra coding for entire special section will save bitrate by avoiding signaling of cu_skip_flag[ x0 ][ y0 ] and pred_mode_flag at the CU level
JVET-M0387 also included a proposal to avoid signaling of these syntax elements within a progressive intra refresh area. The combined proposal in JVET-M0387, which also contained some additional features, provided some coding efficiency gains, but did not break down the gains of the different components of the proposal.

## Slide 12: Prediction restriction for progressive intra refresh
Two flags to indicate that the encoder has constrained intra and inter prediction, respectively, to enable progressive intra refresh functionality.
  Intra prediction restriction flag indicates that for the current picture, all spatial intra prediction of CUs within the special section may not refer to any samples outside of a “clean” progressive intra refresh section.
  Inter prediction restriction flag restricts inter prediction to enable “clean” progressive intra refresh decoder operation.
These flags do not require any normative changes to decoder behavior. Could be placed in VUI instead of PPS.
For “clean” intra and inter prediction operation in the progressive intra refresh mode of operation, clean and dirty regions of the picture can be tracked and updated for each coded video picture, in coding order.

## Slide 13: Clean and dirty regions
Intra prediction for clean regions in the current picture is only allowed from clean regions in the current picture.
Inter prediction for clean regions in the current picture is only allowed from clean regions in the reference picture.
Whenever the upper left minCB block of a picture is included within the special section, a reset takes place and all blocks within the special section of the current picture are set to be clean, and the blocks in the remainder section are reset to be dirty.
For subsequent pictures in coding order, the clean/dirty region mapping is inherited from the previously coded picture and then updated by setting the blocks within the special section of the current picture to be clean.

## Slide 14: PPS Syntax
pic_parameter_set_rbsp( ) { | Descriptor
…. | ue(v)
pps_section_flag | u(1)
if ( pps_section_flag) { | 
section_disable_inloop_filters_flag | u(1)
section_qp_offset_flag | u(1)
if ( section_qp_offset_flag ) { | 
section_neg_qp_offset_luma | u(4)
section_neg_qp_offset_chroma | u(4)
} | 
section_force_intra_flag | u(1)
section_intra_pred_restrict_flag | u(1)
if (section_intra_pred_restrict_flag) | 
section_inter_pred_restrict_flag | u(1)
section_hor_units_minus1 | ue(v)
section_ver_units_minus1 | ue(v)
for ( i = 0; i <= section_hor_units_minus1; i++ ) | 
for ( j = 0; j<= section_ver_units_minus1; j++ ) | 
section_active_flag[ i ][ j ] | u(1)
pps_section_tile_group_mapping_present_flag | u(1)
} | 
rbsp_trailing_bits( ) | 
} | 

## Slide 15: Tile group header syntax
… | 
if( pps_section_tile_group_mapping_present_flag ){ | 
tile_group_section_hor_units_minus1 | ue(v)
tile_group_section_ver_units_minus1 | ue(v)
for ( i = 0; i <= tile_group_section_hor_units_minus1; i++ ) | 
for ( j = 0; j<= tile_group_section_ver_units_minus1; j++ ) | 
tile_group_section_active_flag[ i ][ j ] | u(1)
} | 
… | 

## Slide 16: Coding Unit syntax
coding_unit( x0, y0, cbWidth, cbHeight, treeType ) { | Descriptor
if( ( tile_group_type != I ¦ ¦ sps_ibc_enabled_flag) && !(section_force_intra_flag && SectionActiveMinCb[x0>> MinCbLog2SizeY][y0>> MinCbLog2SizeY] ) ) { | 
if( treeType != DUAL_TREE_CHROMA ) | 
cu_skip_flag[ x0 ][ y0 ] | ae(v)
if( cu_skip_flag[ x0 ][ y0 ] = = 0 ) | 
pred_mode_flag | ae(v)
} | 
… | 

## Slide 17: Conclusion
Proposes mapping of picture into two sections, unaligned with tiles
  Encoder selected signaling granularity for bitrate efficiency
  Decoder storage of flag at MinCbSizeY block granularity
Compared to tile or tile groups
  Avoids coding efficiency penalty associated with tiles
  Allows finer granularity
Flexible selection of tools applied to special section
  Can be applied to gradual decoder refresh or other use cases