## Slide 1: JVET-N00276: AHG15: On interoperability point signalling
Jill Boyce

## Slide 2: Introduction
Five new constraint flags are proposed, primarily for tool adoptions at the prior meeting, and small modifications of existing constraint flags to align with renaming or syntax reordering in the VVC Draft 4 specification
Have the presence of tool enable flags in the SPS, PPS, and tile group header be conditioned on the value of the corresponding constraint flags in the general_constraint_info( ) syntax structure
Add a syntax element in the profile_tier_level( ) syntax structure for 3rd party sub-profile indication

## Slide 3: New constraint flags
no_partition_constraints_override _constraint_flag
no_dmvr_constraint_flag
no_sbt_constraint_flag
no_fpel_mmvd_constraint_flag
no_transform_skip_constraint_flag
Some additional renaming or reordering of existing constraint flags to align with VVC Draft 4

## Slide 4: Sub-profile indication
Carry sub-profile indicator in profile_tier_level( )
Intended for 3rd party use
ITU-T T.35 as registration authority
3 bytes
  1 byte: Country Code
  1 byte: Terminal Provider
  1 byte: For the subprofile ID within a profile for each terminal provider

## Slide 5: Conditional presence of parameter set syntax elements
Proposed to not signal the syntax element for a tool enable flag if the use of the tool is already forbidden by the corresponding constraint flag.
When an enable flag syntax element is not present, its value is inferred to be equal to 0.
This enables a savings in bitrate overhead for the flags, and avoids the possibility of conflicting signaling in non-conforming bitstreams.
It is noted that some enable flags are signaled in the PPS, while the constraint flags are signaled in the general_constraint_info( ) syntax structure of the SPS. JVET-M0133 has proposed to allow a relaxation of the general design principle followed for AVC and HEVC that avoided parsing dependency of the PPS on the SPS.

## Slide 6: Conclusion
Proposes mapping of picture into two sections, unaligned with tiles
  Encoder selected signaling granularity for bitrate efficiency
  Decoder storage of flag at MinCbSizeY block granularity
Compared to tile or tile groups
  Avoids coding efficiency penalty associated with tiles
  Allows finer granularity
Flexible selection of tools applied to special section
  Can be applied to gradual decoder refresh or other use cases